## Slide 1: TXOP Preemption Follow Up
Date: 2023-07-06
Authors:

## Slide 2: Introduction
In [1] and [2], we discussed TXOP preemption as a candidate feature of UHR to support low latency traffic.
In this document, we discuss further details of TXOP preemption

## Slide 3: Recap) TXOP Preemption – Possible Cases [1]
Case 1: DL low latency data TX in a UL TXOP
  TXOP responder (AP) needs to preempt the UL TXOP.
Case 2: UL low latency data TX in a DL TXOP
  During a DL TXOP, an AP needs to transmit a Trigger frame for scheduling UL resource for UL low latency traffic
Case 3: UL low latency data TX in a UL TXOP
  A TXOP holder (non-AP STA) needs to allocate a time period for an AP to schedule a UL resource for UL low latency traffic.
Case 4: Low latency data TX in an OBSS TXOP
  Aggressive Spatial Reuse can be defined for an AP/non-AP STA to transmit a low latency frame during an OBSS TXOP.

## Slide 4: General Issue and Solution
Issue: Long PPDU length
  Long PPDU transmission from a TXOP holder may forbid for a non-TXOP holder to preempt the TXOP with less delay
    As the PPDU length transmitted by the TXOP holder is longer, delay of the low latency packet becomes larger  Less gain of TXOP preemption
Potential solution
  An AP announces the maximal PPDU length through Beacon (Probe Response, Association Response etc.) that a non-AP STA can use.
    A non-AP STA in the BSS can’t transmit a PPDU that is longer than the announced PPDU length.
    The restricted PPDU length can be applied to the PPDU of non-low latency traffic only or any PPDU.

## Slide 5: DL low latency frame transmission in the UL TXOP (Case 1)
Assumption
  A non-AP STA is a TXOP holder.
  An AP is a TXOP responder, and the AP has a buffered low latency frame.
Issue
  When the non-AP STA does not allocate a time period using RDG to the AP, the AP cannot transmit its buffered low latency frame before the end of the TXOP.
Potential solution
  Option 1: The AP requests TXOP preemption in an immediate response frame (e.g., BA) to the TXOP holder and it transmits a low latency frame.
    After transmitting the low latency frame, the AP transmits a frame indicating TXOP Preemption Release to the TXOP holder.
    The TXOP holder can resume its transmission during the remaining TXOP.
  Option 2: The TXOP holder transmits multiple PPDUs using a longer IFS (e.g., PIFS), and the TXOP responder may preempt the TXOP using a shorter IFS (e.g., SIFS) to transmit the low latency frame.
    A UL PPDU can include an indication of whether preemption is allowed after the UL PPDU.
    To avoid collision, only TXOP responder can preempt the TXOP during the UL TXOP.
Option 1
Option 2

## Slide 6: UL low latency frame transmission in the DL TXOP (Case 2)
Assumption
  An AP is a TXOP holder.
  A non-AP STA (TXOP responder or non-TXOP responder) has a buffered low latency frame.
Issue
  The AP is not aware of which non-AP STA has a buffered low latency frame.
  When and how the AP provides a preemption opportunity to a non-AP STA with low latency frame is the issue to be addressed.
Potential solution
  A non-AP STA preempts the TXOP using a shorter IFS (e.g., SIFS) to transmit the low latency frame while an AP transmits multiple PPDUs using a longer IFS (e.g., PIFS).
    A DL PPDU can include an indication of whether preemption is allowed after the DL PPDU.
    To avoid collision from multiple non-AP STAs, a Low Latency Indication frame (w/ unified frame format such as e.g., a simultaneous CTS frame in response to an MU-RTS Trigger frame, etc.) can be transmitted to request UL resource allocation for low latency frame transmission.
    The AP that receives a Low Latency Indication frame can allocate UL resource for transmission of the low latency frame.

## Slide 7: UL low latency frame transmission in the UL TXOP (Case 3)
Assumption
  A non-AP STA is a TXOP holder.
  Other non-AP STA has a buffered low latency frame.
Issue
  The AP is not aware of which non-AP STA has a buffered low latency frame.
  How the TXOP holder provides a preemption opportunity to other non-AP STAs with low latency frame is the issue to be addressed.
Potential solution
  For further study

## Slide 8: Low latency frame transmission in the OBSS’ TXOP (Case 4)
Assumption
  An OBSS STA is a TXOP holder.
  A non-AP STA or an AP has a buffered low latency frame.
Issue
  Due to a non-zero basic NAV set by an OBSS frame, the AP/non-AP STA is not able to deliver the buffered low latency frame during the OBSS TXOP.
Potential solution
  For further study

## Slide 9: Summary
For low latency frame transmission, the followings can be considered for TXOP preemption in UHR.
  A PPDU length can be limited in the TXOP.
  An AP can request preemption of the TXOP to a non-AP STA that is a TXOP holder.
  After a PPDU indicating preemption allowance, a low latency frame or a Low Latency Indication frame can be transmitted by a non-TXOP holder using a shorter IFS in a TXOP.

## Slide 10: References
[1] IEEE 802.11-23/0018 Low latency support in UHR
[2] IEEE 802.11-23/0092 Preemption