## Slide 1: Further Discussion on AMP PAR
Date: 2023-07-12
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Doc.: IEEE 802.11-23/1190r1
July 2023

## Slide 2: Abstract
Common consensus on study scope has been achieved in TIG and further discussion on PAR scope happened in the past telcos.
New air-interface design and further MAC optimization are needed to support ultra-low power consumption and ultra-low complexity AMP devices.
Doc.: IEEE 802.11-23/1190r1

## Slide 3
Deployment Option 1
  Communication links
    Both DL and UL in S1G
    DL: new air-interface with WUR-like design (i.e. MC-OOK) with scaling, e.g., SCS 312.5kHz  31.25kHz, OFDM symbol duration 4us  40us, etc.
    UL: new air-interface with OOK/FSK/PSK
  RF power transfer (when RF power is used)
    Fixed AP or mobile AP, e.g., cell phone, as RF energy source
    Same S1G band as communication link
    Assisted Node can be optionally deployed for additional power source
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-23/1190r1
July 2023
AMP DL air interface @S1G
AMP UL air interface @S1G
RF power transfer @S1G
or
Fixed AP
Mobile AP
AMP device
RF power transfer @S1G
Assisting Node

## Slide 4
Deployment Option 2
  Communication links
    Both DL and UL in 2.4GHz
    DL air-interface: WUR-like design
    UL air-interface: OOK/PSK/FSK or DSSS for backward compatibility
  RF power transfer(when RF power is used)
    Fixed AP or mobile AP, e.g., cell phone, as RF energy source
    Assisted Node can be optionally deployed for additional power source
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-23/1190r1
July 2023
DL communication @2.4GHz
UL communication @2.4GHz
RF power transfer @S1G/2.4GHz
or
Fixed AP
Mobile AP
AMP device
Assisting Node
RF power transfer @S1G/2.4GHz

## Slide 5
Issues to be standardized
  New air-interface design for DL/UL for deployment option 1(Sub-1 GHz), e.g.
    WUR-like design for DL
    OOK/PSK/FSK for UL
  Enhanced air-interface for deployment option 2 (2.4GHz), e.g.
    WUR for DL
    OOK/PSK/FSK or DSSS for UL with backward combability
  MAC optimization for both deployment option 1/2, e.g.
    Routine MAC procedures including association/disassociation and authentication, etc.
    Channel access schemes, power management, MAC compression etc.
  Further consider whether to specify RF power transfer
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-23/1190r1
July 2023

## Slide 6
Par Scope Consideration
  Operation frequency should be specified and both S1G and 2.4GHz can be supported.
  Other detailed requirements, e.g., data rate, channel bandwidth, can be left for TG
  Both communication and positioning should be supported
  Co-existence should be considered and backward compatibility can be considered in some cases, e.g., deployment option 2.
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-23/1190r1
July 2023

## Slide 7
Suggested Consolidated PAR
This amendment defines modifications to both the IEEE 802.11 Medium Access Control layer (MAC) and Physical Layers (PHY) to enable operation of ambient powered device by defining
at least one mode of ultra-low power data communication link sub-1GHz or 2.4 GHz
at least one mode for certain type of AMP IOT devices to connect with legacy WLAN network in 2.4GHz band
at least one mode of wireless RF power transfer in sub-1GHz or 2.4GHz
at least one mode to support positioning function
This amendment shall provide coexistence and, at least for the second mode, provide backward compatibility with deployed devices compliant with IEEE Std 802.11™-2020 and operating in the same band.
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-23/1190r1
July 2023

## Slide 8
Summary
Issues including deployment options, issues to be standardized are presented.
Consolidated PAR is proposed.
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-23/1190r1
July 2023