## Slide 1: Overlapped Indication to Support Preemption
Date: 2023-07-07
Authors:

## Slide 2: Introduction
Reducing tail of latency distribution is a key component of UHR PAR [1]
  EHT features (e.g., R-TWT) focus on latency reduction of predictable Low-latency (LL) traffic
  Support of event-based LL traffic is missing [2]
UHR contributions for low latency include
  Preemption [2-5]
  LL traffic classification and enhanced QoS signalling [7-9]
  Enhanced LL scheduling methods [10-12]
Preemption is a good candidate to support event-based LL traffic [2-5]
  Basic concept is to suspend ongoing traffic to insert LL traffic
  Well suited when LL and non-LL traffic originate at TXOP holder (e.g., downlink)
  More challenging when STA with LL traffic is not the TXOP holder or responder (e.g., uplink)

## Slide 3: Problem of event-based LL traffic awareness
LL traffic originates at LL_STA that is not TXOP holder or responder
  LL_STA needs to wait until TXOP ends to start contention for channel access
  LL traffic arrival is unpredictable => AP cannot collect BSR in time
  The tail of latency distribution can be very long for large TXOPs and dense scenarios
TXOP Holder (AP)
TXOP responder
LL_STA
LL arrival
TB-PPDU
BAck
…
LL data
Channel access latency
TXOP
TF
BAck
TB-PPDU
TF

## Slide 4: Problem of event-based LL traffic awareness (existing solutions)
[6] MLO can allow LL_STA to perform channel access in different links
  Depends on MLD capabilities (e.g., number of links, STR, NSTR, PS mode)
  LL_STA still needs to contend for channel access
    It is likely that the TXOP holder uses several links to increase throughput
Reduce PPDU or TXOP size
  Short TXOP size reduces the time LL_STA needs to wait before contention
  [3] Short PPDUs with different IFS can allow LL_STA to contend before TXOP ends
Drawbacks and limitations
  Small PPDU or TXOP size can reduce efficiency of channel usage
  Contention delay cannot be avoided
    Latency tail distribution can be very long if many STA contend at specific times

## Slide 5: Proposal (1/3)
Overlapped LL indication frame (LL_IF)
  Short frame containing robust sequence that identifies LL_STA
  LL_STA can send LL_IF overlapped with a TB-PPDU
  LL_IF indicates to the AP an arrival of urgent LL traffic at LL_STA
TXOP Holder (AP)
TXOP responder
LL_STA
LL arrival
TB-PPDU
BAck
…
TXOP
TF
LL_IF
Fast LL traffic arrival awareness

## Slide 6: Proposal (2/3)
Basic overlapped LL_IF operation
  AP can indicate, within trigger frame (TF), to LL_STA that a LL_IF may be sent in the TB PPDU
  If LL_STA has an event-based LL traffic arrival, it sends LL_IF overlapping with the data field of the ongoing TB PPDU
  AP detects LL_IF with simple detector (e.g., matched filter)
  Once a LL_IF is detected, AP can decide (e.g., preemption, TXOP sharing, different link, deny,…)
TXOP Holder (AP)
TXOP responder
LL_STA
LL arrival
TB-PPDU
BAck
…
TXOP
TF
TF
LL data
Reduced channel access latency
LL_IF
Fast LL traffic arrival awareness
BAck
Indication LL_IF allowed
Uplink preemption example

## Slide 7: Proposal (3/3)
Main benefits
  Event-based LL traffic awareness without contention delay
  Controlled channel access since AP can decide how to allocate resources
  LL_IF can be designed to cause negligible impact to ongoing PPDU reception
Disadvantages
  Additional processing at the AP to detect LL_IF (small compared to PPDU demodulation)
  PPDU size may need to be limited to achieve very fast LL awareness
TXOP Holder (AP)
TXOP responder
LL_STA
LL arrival
TB-PPDU
BAck
…
TXOP
TF
TF
LL data
Reduced channel access latency
LL_IF
Fast LL traffic arrival awareness
Indication LL_IF allowed
BAck
Uplink preemption example

## Slide 8: LL_IF design as OFDM waveform
LL_IF should be a pre-agreed signal known to the AP that identifies LL_STA
  LL_IF can be defined as simple BPSK sequence (e.g., based on P matrix used for LTFs)
  LL_IF sequence can be mapped to a few active subcarriers (e.g., small RU) and OFDM symbols
P4 =
LL_IF example:
P4 replicated 6 times
4 OFDM symbols
24 active subcarriers
  Mapped into data subcarriers of 26-tone RU
Time (OFDM symbols)
26-tone RUs
106-tone RUs
Reserved tones
Time (OFDM symbols)
106
Tone-RU
26
Tone-RU
106
Tone-RU
Data field
Preamble
26-tone RUs
106-tone RUs
Reserved tones
LL_IF
Data field
Preamble
pilot
pilot
data
data
Frequency (Subcarriers/Tones)
Ongoing PPDU
Frequency (Subcarriers)
guard

## Slide 9: Synchronization aspects
OFDM modulated LL_IF requires synchronization to ongoing PPDU transmission
  LL_STA can synchronize to the preamble of ongoing PPDU when in range of ongoing PPDU
  LL_STA can synchronize to PPDU (e.g., TF) immediately preceding ongoing PPDU
TXOP responder
TXOP holder (AP)
LL_STA
Preamble
LL arrival
LL_IF
Available time to transmit LL_IF
Data
Sync. + decode
Switch RX-TX
Extra processing to detect LL_IF
Ongoing PPDU
TXOP responder
TXOP Holder (AP)
LL_STA
LL arrival
LL_IF
Data
…
Preamble
Prev. PPDU
Sync. + decode
Available time to transmit LL_IF
Switch RX-TX
Wait time
Extra processing to detect LL_IF
Ongoing PPDU

## Slide 10: Simulation results
Ongoing PPDU
  20 MHz Bandwidth, Channel type D
  MCS = 2, 4 GI = 0.8 us
  ~1dB loss at PER = 0.1 and MCS 4
  ~0dB loss at PER = 0.1 and MCS 2
SIR = 20dB (rx_PPDU/rx_LL_IF)
LL_IF impairments
  Residual CFO 200Hz
  Residual Time Offset ~Uniform(0,GI)
LL_IF design and results
  6x replication of P4 matrix
  24 active subcarriers (26-tone RU)
  4 OFDM symbols
  Detection Prob. > 0.7 for LL_IF SNR > 0dB
MCS 2
MCS 4

## Slide 11: Additional considerations and specification relevance
Signaling aspects
  There should be an agreement between STAs to control the usage of LL_IF
  Pre-agreement on sequences that will be sent as LL_IF to identify the LL_STA
  There can be explicit indications to allow or disallow the LL_IF overlap on specific PPDUs
  LL_IF transmission can be restricted to designated RUs
  LL_IF transmission power can be set to a specified limit or to achieve a SIR target
Regulatory aspects
  LL_IF can be transmitted without CCA if the following considerations are met
    It does not contain data
    Less than 50 transmissions within 50ms period
    Combined duration of all LL_IF transmissions within 50ms should be less than 2.5ms

## Slide 12: Summary and Conclusions
Event-based LL traffic should be supported by UHR
  EHT only supports predictable LL traffic
  Preemption is a good candidate to support event-based LL traffic
Event-based LL traffic suffers from arrival unawareness
  Solutions based on existing technologies may have long delays or low efficiency
An overlapped LL indication frame can provide fast LL traffic awareness
  Avoid contention delay and maintain efficiency
  Negligible impact to reliability of ongoing PPDU
  Once AP is aware of LL traffic can provide controlled channel access
  Extension to EDCA channel access can be done

## Slide 13: References
[1] 11-23/0480r1 UHR proposed PAR
[2] 11-23/1880r1 Latency and Reliability enhancements for UHR
[3] 11-23/0092r0 Preemption for Low Latency Application
[4] 11-23/0018r1 Low Latency Support in UHR
[5] 11-22/1393r0 Latency Reduction Scheme for UHR
[6] 11-19/1081r0 Multi-Link Aggregation: Latency Gains
[7] 11-23/0069r1 Considerations on Latency Improvement (LG)
[8] 11-23/0740r0 Dynamic QoS Feedback for UHR
[9] 11-23/0885r0 Considerations on QoS Enhancement in UHR
[10] 11-23/0771r0 Coordinated R-TWT Protection in Multi-BSS
[11] 22/1899r0, Multi-AP Operation for Low Latency Traffic Delivery - Follow up
[12] 22/1556r1, Multi-AP Coordination for Low Latency Traffic Delivery