## Slide 1: Enhanced Acknowledgement for Low Latency Communication
Date: 2023-08-25
Authors:

## Slide 2: Abstract
In this presentation we present an enhanced acknowledgement method to reduce delay of a lower latency traffic transmission.

## Slide 3: Early Acknowledgement of Low Latency Packets
Increased reliability and support of lower latency are two of the main improvement areas of the 802.11bn project.
An important part of the low latency communication is verifying that the packets arrive correctly.
With multi link communication and simultaneous transmit and receive (STR) capability, we need to allow to acknowledge MSDUs or A-MSDUs with low latency requirement before the end of the PPDU transmission.

## Slide 4: Early Acknowledgement of MPDUs
We assume that transmitter and receiver are multi-link and simultaneous transmit and receive capable. The payload is transmitted from the first link.
After the reception of the low latency MPDU, receiver sends a feedback frame to indicate reception status from the second link.

## Slide 5: Retransmission Option 1
If the feedback frame indicates the low latency MPDU is received in error. The second link could be used to transmit the MPDU received in Error.

## Slide 6: Retransmission Option 2
Another option is adding the MPDU received in error at the end of the PPDU, with dynamic PPDU modification.

## Slide 7: Early Indication of SIG Field Errors
Feedback frame could be utilized to indicate if there is an error in the PHY Header.
Notes: Mention RTS CTS or TXOP, indicate ppdu in all slides…

## Slide 8: Conclusion
In this contribution, we provide a feedback scheme to early indication of error for low latency transmissions.