## Slide 1: QoS Enhancements for Next Generation Wi-Fi Networks
Date: 2023-07-04
Authors:

## Slide 2: Abstract
In this presentation we consider the issue of head-of-line (HOL) blocking
We present some thoughts on possible directions to address the issue

## Slide 3: Background
UHR has considered several areas of improvement for next generation Wi-Fi networks [1]:
  Increased reliability of WLAN connectivity
  Lower latencies and deterministic latency support
  Increased manageability and mobility support
  Increased performance in congested environments
  Throughput enhancements
  Power savings enhancements
The approved PAR intends to consider at least one mode of operation capable of improving the tail of the latency distribution and jitter compared to EHT MAC/PHY operation [2]

## Slide 4: Background
Support for new use cases with extremely low latency applications have been proposed previously:
  A number of applications that can potentially have very low latency requirements have been considered and discussed by the group [3]-[5]
  Applications in these categories can have a last hop latency requirements on the scale of a few milliseconds [3], [4]
  Many such use cases have also been analysed in the RTA report
  For some of the applications near lossless performance is also expected
Use cases |  | Intra BSS latency [ms] | Jitter variance [ms] | Packet loss | Data rate [Mbps]
Real-time gaming |  | < 5 | < 2 | < 0.1 % | < 1
Cloud gaming |  | < 10 | < 2 | Near-lossless | < 0.1 (Reverse link) > 5Mbps (Forward link)
Real-time video |  | < 3 ~ 10 | < 1~ 2.5 | Near-lossless | 100 ~ 28,000
Robotics and industrial automation | Equipment control | < 1 ~ 10 | < 0.2~2 | Near-lossless | < 1
 | Human safety | < 1 ~ 10 | < 0.2 ~ 2 | Near-lossless | < 1
 | Haptic technology | < 1 ~ 5 | <0.2~2 | Lossless | <1
 | Drone control | < 100 | <10 | Lossless | <1 >100 with video

## Slide 5: In-order Delivery of Frames
In order delivery approach:
  IEEE 802.11 MAC is designed to deliver frames in order to higher layers.
  The MAC at the transmitter assigns sequence/packet numbers to transmitted frames (e.g., MSDU, A-MSDU, etc.)
  The numbering enables the receiver to identify the order of transmitted frames and perform in order delivery
  The receive reorder buffer holds the frame and passes them in order to higher layer in order. Such an in order delivery benefits applications where in order delivery is desirable.

## Slide 6: Head of the Line Blocking Issue
The in-order delivery approach can lead to a head of the line (HOL) blocking issue:
  A packet can get held in the reorder buffer if there is a hole preceding it
  The transmitter needs to re-transmit these missing frames
  This can cause a delay in the packet getting forwarded to higher layers
Prior works presented in UHR have considered allowing an out-of-order policy to address the HOL blocking issue [6]
In this contribution, we discuss a possible direction to address the HOL blocking issue while maintaining an in-order delivery policy

## Slide 7: Solution Overview
Addressing the HOL blocking issue requires two key procedures:
  A signaling procedure to inform the transmitter of the HOL blocking issue
  A recovery procedure to retrieve the frame(s) that lead to the HOL blocking issue
Procedures need to be able to do the recovery faster compared to the normal retransmission process
Multi-link operation can be leveraged to address this issue:
  An AP MLD and a non-AP MLD can have multiple links setup for communication
  The setup can be leveraged for addressing the HOL blocking issue

## Slide 8: Possible Solution Options
Option A: Cross link indication with same link recovery
Option B: Cross link indication with cross link recovery
Option C: Same link indication with same link recovery

## Slide 9: Option A: Cross Link Indication With Same Link Recovery
Suppose that STA1 has an ongoing transmission to AP1 that includes one or more frames that can face a HOL blocking issue.
An indication of the missing frames can be provided via AP2 or AP3. An example is shown in the above figure.
Upon receiving the indication, STA1 can include the missing frames in the ongoing transmission to AP1.
This can require dynamic PPDU modification. PPDU formatting approaches proposed for other features in the past can be used for this purpose [7].
AP1
AP2
AP3
STA1
STA2
STA3
Link 1
Link 2
Link 3
Ctrl frame carrying missing frame info
STA1 inserts missing frame(s) in the ongoing transmission
BA

## Slide 10: Option B: Cross Link Indication With Cross Link Recovery
Instead of transmitting missing frames as a part of the ongoing transmission on link 1, they can be transmitted on link 2.
AP1
AP2
AP3
STA1
STA2
STA3
Link 1
Link 2
Link 3
Ctrl frame carrying missing frame info
PPDU carrying missing frames
BA
BA

## Slide 11: Option C: Same Link Indication With Same Link Recovery
STA1 can break the ongoing transmission into multiple PPDUs with some preemption periods between the PPDUs (similar to preemption mechanism [8])
If a PPDU has one or more frames that can face a HOL blocking issue, AP can transmit a control frame in the interframe spacing. STA1 can insert the missing frames in one of the following PPDUs.
AP1
AP2
AP3
STA1
STA2
STA3
Link 1
Link 2
Link 3
PPDU1
PPDU 3 has a frame that can suffer from HOL blocking issue
BA
PPDU2
PPDU3
PPDU4
Ctrl frame carrying missing frame info
STA1 includes missing frame in one of the following PPDUs
Preemption periods between PPDUs

## Slide 12: Conclusion
UHR aims to lower latency support in next generation Wi-Fi networks
Reducing additional delays caused by HOL blocking issues can be important
In this discussion, we present two solution directions for achieving this objective

## Slide 13: References
[1] Beyond be – Proposed Next Step, IEEE 802.11-22/0708r3
[2] UHR proposed PAR, IEEE 802.11-23/480
[3] Considerations on UHR PAR and KPIs, IEEE 802.11-22/1919
[4] Cloud VR Use Case and Requirements, IEEE 802.11-22/0952
[5] 802.11bx: Enabling Metaverse -- Metaverse, AR/VR, and Wearables, IEEE 802.11- 22/0779
[6] Head of line blocking issue for Wi-Fi, IEEE 802.11-23/697r0
[7] Further Improve Latency Performance in 11be, IEEE 802.11-21/0670
[8] Preemption for Low Latency Application, IEEE 802.11-23/0092