## Slide 1
Requirements for TID obfuscation
Date: 2023-07-09
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1-404-229-1672 | carol@ansley.com

## Slide 2
Abstract
This submission considers ramifications of requirement 30, TID obfuscation.

## Slide 3: Summary
The many uses of TSID and TID would make obfuscating the TID/TSID everywhere burdensome and the small number of bits available to be obfuscated would provide only minimal increases in user privacy.

## Slide 4: Requirements
The following requirements all deal with changing a STA’s OTA MAC address.
30 | 11bi shall define a mechanism for a CPE Client and CPE AP to obfuscate the transmitted TID to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection.
31 | 11bi shall define a mechanism for CPE Clients and CPE APs to encrypt or obfuscate (TBD) a subset of MAC Header fields (specific fields TBD)

## Slide 5: TID Subfield discussion - background
The TID subfield within the QOS Control field of the MAC Header only has 4 bits for PV0 and 3 bits for PV1.
PV0: Table 9-12 from REVme, D3.0 is below:
PV1: The 3 LSBs of the TID as defined in 9.2.4.5.2 (TID subfield) for PV1 QoS Data frames (Type subfield equal to 0 and 3) transmitted by a QoS STA. (from 9.8.3.1 Frame Control Field).
In the end, the values to be obfuscated are only 3 bits, if Table 9-12 is still followed.
A TID and the associated TSID are only unique for the STA, not between STAs associated with an AP.
Access policy | Usage | Allowed Values
EDCA | UP for either TC or TS, regardless of whether admission control is required | 0–7
HCCA, SPCA | TSID | 8–15
HEMM, SEMM | TSID, regardless of the access mechanism used | 8–15

## Slide 6: Discussion
A TSID is also used in the TSPEC element which is in turn used in ADDTS, DELTS, ADDBA, DELBA.
TID used directly in several BlockAck variants (TID_INFO subfield).
The original presentation for Req. 30 only talked about the MAC Header.
Should all of these uses of the TSID and the TID be included in Req. 30 or should it only refer to the “TID” which is part of the MAC header?
Would it make more sense for the TID subfield in the MAC Header just be included in the fields that are encrypted or obfuscated in the MAC Header as part of Req. 31?

## Slide 7: Straw Poll
Do you support removing Req. 30 from the list of approved requirements and adding TID to the list of fields to be obfuscated in Req. 31?
Note based on prior agreements within the group, a motion is required to change the approved requirements in doc 21/1848r16.

## Slide 8: References
11-22/623r1 – Privacy Requirements
P802.11 REVme D3.0
11-21/1848r16 – TGbi Requirements Tracking