## Slide 1: Power Consumption Calculation
Date: 2023-07-11
Authors:

## Slide 2: Abstract
Document 11-23/876r0 presented an approach for X-Band operation. The were questions related to the actual power consumption.
This presentation shows some figures on the actual energy consumption inside the AMP STA and the required energy storage capacitor size.

## Slide 3: Link Budget Calculation
 | AMP-assisting STA | AMP STA
Transmit Power | 27dBm (500mW) | -25dBm (0.003mW)
Transmitter Ant. Gain. | 5dBi | 0dBi
Receiver Ant. Gain | 0dBi | 5dBi
Path Loss for 10m | 52dB (915MHz) | 60dB (2.4GHz)
RX Power at Receiver | -20dBm | -80 dBm
Parameters as presented in 11-23/876r0
Minimum signal level of -20dBm at AMP STA
Transmit power of 3µW for AMP STA

## Slide 4: Some Assumptions for the AMP STA
802.11b uplink waveform, 50 bytes @11Mbit/s  190µs TX duration
10µs PLL settling time
5mW power consumption when PLL [1] and/or TX is active (200µs)
  Main consumption is due to PLL
  Previous slide assumes TX power of only 3µW
   Minimize TX on-air time to save energy
1 µJoule for one uplink packet

## Slide 5: Energy Harvesting
Conversion efficiency 10% of the harvester [2]
Minimum reception level of -20dBm  10µW
 Minimum power of 1 µW available for the harvester
1 s to harvest 1 µJoule @ -20 dBm
0.1 s to harvest 1 µJoule @ -10 dBm

## Slide 6: Required Energy Storage Capacity
Stored energy on capacitor is given by
50% of the energy is actually usable, U=2V
Required capacitor size of C=1µF to store 1µJ

## Slide 7: Conclusions
This presentation calculated the required energy for an active transmitter in the AMP STA
The system requires approx. 1µJ per packet
The given numbers can be harvested from the field in a realistic timeframe
Only a tiny capacitor is required to store the energy

## Slide 8: Literature
[1] K. -F. Un et al., "A 0.12-mm2 1.2-to-2.4-mW 1.3-to-2.65-GHz Fractional-N Bang-Bang Digital PLL With 8- μ s Settling Time for Multi-ISM-Band ULP Radios," in IEEE Transactions on Circuits and Systems I: Regular Papers, vol. 66, no. 9, pp. 3307-3316, Sept. 2019
[2] A. Collado and A. Georgiadis, "Conformal Hybrid Solar and Electromagnetic (EM) Energy Harvesting Rectenna," in IEEE Transactions on Circuits and Systems I: Regular Papers, vol. 60, no. 8, pp. 2225-2234, Aug. 2013