## Slide 1: Comments received on P802.11bn PAR
Date: 2023-07-13
Authors:

## Slide 2: Abstract
This document contains comments received from:
Paul Nikolich (2 comments)
James Gilb (13 comments)
802.15 (7 comments)
802.3 ( 7 comments, included for completeness, originally in 11-23-1080)
802.1 (6 comments)
See 11-23-1080 for comments from 802.3
R4: Adds received re-direct comments from James Gilb, see slides 4, 6, 7, 10

## Slide 3: Nikolich: CSD (2 comments)
1) In 1.2.4.b I suggest replacing "The increased capabilities envisioned for the baseband and RF parts necessary to implement the proposed amendment are in line with the current progress in technology and not expected to impinge testability."
with
"The increased capabilities envisioned for the MAC, baseband signal processing and RF technologies necessary to implement the proposed amendment are in line with the current progress of those technologies as demonstrated by lab testing, modeling and simulations."
2) There appears to be a cut-and-paste error in the 1.2.5.a and 1.2.5b of the CSD (see below). I suggest swapping the text under (a) and (b).
1.2.5.a) Known cost factors.
WLAN equipment is accepted as having balanced costs. The development of Wireless capabilities to enhance the throughput and improve latency of WLAN network deployments will not disrupt the established balance.
1.2.5.b) Balanced costs.
Support of the proposed standard will likely require a manufacturer to develop a modified radio, modem and firmware. This is similar in principle to the transition between IEEE 802.11ax and IEEE 802.11be as well as in previous iterations of IEEE Std. 802.11 enhancements. The cost factors for these transitions are well known and the data for this is well understood.

## Slide 4: Gilb: PAR 2.1 (3 of 13 comments)
2.1 "Ultra High" violates the NesCom convention of not using comparative words rather than specific numbers. You need to specify somewhere what "Ultra High" means. (Also, it would be Ultra-High Reliability). 2.1 How is reliability defined? No where do I find out what type of reliability is being sought. You need a different title for this that matches the description in the scope. I don't see any proposed additions that address reliability of any kind.
Response: We understand that NesCom convention allows for an exception to this that must be explained. For this reason, we have provided in section 8.1 an explanation that is clarified following the comment. Changes are made also to clarify the definition of reliability as the 3 items described in section 5.2b, and to provide quantified target for these items. Redirect: In 8.1, there is the claim that "IEEE 802.11 standard today provide high reliability of MPDU transfer for most use cases and deployment scenarios". Perhaps the group can point out the location of the definition of reliability that IEEE Std 802.11 and how it currently meets this definition. As Landsford's definition of wireless states: "Wireless is a noisy, insecure, unreliable, piece of wire".

## Slide 5: Gilb: PAR – 5.2.b (5 of 13 comments)
- The three items specified use "increasing", "improving" and "improving" with no numerical targets. This would imply that any tiny change would justify adding the new feature. Replace these with numerical targets, e.g., 50% more throughput. - If you are going to compare to EHT MAC/PHY, there needs to be a documented measurement for the baseline, or at least some sort of agreed upon method. This method needs to be referenced. - How is "tail of the latency distribution and jitter" "improved"? What is the definition of "tail". At what value has the distribution fallen off enough for it to be the "tail"? Are you decreasing the integral of the tail? - Efficient use of the medium does not uniquely define what is being sought. Is it bits/Hz? idle time? Specify the type of efficiency that is being improved and the numerical target. - How is the power save "enhanced"? What is the characteristic that is being measured with respect to power save? In the need, battery life and lower energy bills are referenced, but the scope doesn't address either.

## Slide 6: Gilb: PAR – 5.2.b (5 of 13 comments) - response
- Response: Thank you. Changes are made in order to provide quantified values for the improvements, except for MPDU loss, for which there hasn’t been improvements in previous amendments. Redirect: The changes for throughput and latency are much improved, thank you. However The response doesn't address the issue with "reducing MAC Protocol Data Unit (MPDU) loss compared". This needs to be replaced with a numerical target. The claim that no other amendment improved MPDU loss is not relevant. Replace "reducing" with a numerical target and a description of the conditions under which MPDU loss is decreased. Also: The AP power save is not part of the attempt to improve reliability. I don't see why this is relevant to the claim of improved reliability. I think that you need to change the title to "Enhanced Performance For Extremely High Throughput MAC/PHY" which is what the scope actually addresses. I note that the comment to 802.15 is that "Power save doesn’t fall into the definition of reliability,", hence the PAR title doesn't correctly describe the scope.

## Slide 7: Gilb: PAR – (General and 8.1 -New comment)
New comments on PAR: If we accept the premise that the current standard provides high reliability, then there is nothing proposed in the scope that justifies "Ultra High". That would be probably be an order of magnitude improvement, at least. The justification in 8.1 is unpersuasive. 8.1 (editorial) Fix the numbered list with the strange character.

## Slide 8: Gilb: PAR – 5.5 (2 of 13 comments)
- The need for the project states "align with a symmetrical broadband speed of 10 Gb/s", but nothing in the scope says that this performance target will be met. Is this a requirement for the amendment? If so, add it to the scope. If not, remove from Need. - Expand "P2P" on first use.

## Slide 9: Gilb: PAR – 8.1 (3 of 13 comments)
- "For example, a user experiencing marginal connectivity at the edge of a network today might experience improved connectivity with the defined enhancements." Will connectivity actually be improved with the changes? If so, how is connectivity measured and by what measure will it be improved? - "Conversely, an application (for example AR/VR) where the user experiences feedback lag under the current baseline might see reduced lag with the defined enhancements." The word "Conversely" doesn't belong here. Both can be true. Also, "might see reduced lag" isn't measureable. At some point the lag isn't noticeable. Is this a real problem and how will the proposed project address it? - "(Basis Service Set)" should just be ", BSS," (it is Basic, not Basis, anyway).

## Slide 10: Gilb: CSD – New Comment
Comment: 1.2.4 a) - The text does not provide any information on demonstrated system feasibility. Which presentations show significant improvement in 802.11 performance? Response: Changes are made to clarify that there are presentations showing gains for some features to meet the PAR’s objectives and clarify that the study group is confident on the technical feasibility of at least some of them. Redirect: The changed text still does not indicate which presentations (e.g., links or document numbers) that specifically show feasibility of the proposed system. I am sure that there are presentations, but they are not explicitly listed here so that they can be reviewed.

## Slide 11: 802.15: PAR (5 comments)
  1) PAR, 5.2.b – fix suspect characters in the bullet list
  2) PAR, 5.2.b – The way 5.2b is written requires that all bullets must be achieved to complete the project – is that correct?
  3) PAR, 5.2.b – it is not clear how these items relate to “Ultra-High Reliability”. Please quantify “Ultra-High Reliability” and clarify the relationship between throughput, latency and efficiency and “Ultra-High Reliability”.
  4) PAR, 5.2.b – We assume “power saving” should be a bullet; please describe how power saving is related to reliability?
  5) PAR, 5.3 This standard appears to be dependent on 802.11be, which is not yet complete.

## Slide 12: 802.15: CSD (2 comments)
  5) CSD 1.2.3 states: “There is no other WLAN standard focusing on improving WLAN throughput at different SINR levels in scenarios of an isolated BSS and overlapping BSSs, improving the tail of the latency distribution and jitter, enhancing mobility between BSSs, and providing mechanisms for enhanced power save for AP STAs (including mobile APs) other than this amendment.” but the PAR states that the project is “Enhancements for Ultra-High Reliability”. Once again, the relationship between throughput, latency and efficiency and “Ultra-High Reliability” is not explained.
  6) CSD 1.2.3 : “There is no other WLAN standard focusing on improving WLAN throughput at different SINR levels in scenarios of an isolated BSS and overlapping BSSs” Please confirm this statement is correct and in what way do SINR levels differ? How does this differ from previous 802.11 standards that improve throughput?

## Slide 13: 802.3: PAR (2 of 6 comments)
2.1 – It isn’t clear if the project is addressing hardware reliability or transmission reliability. These are very different things and this should be significantly more clear.
5.2,b – While the project scope may be technically accurate, it is very difficult to actually figure out what the goals of the project are. Please consider this in any rewrite.

## Slide 14: 802.3: PAR (1 of 6 comments)
5.2.b – The project scope begins with an extremely difficult to parse run-on sentence. It would be helpful to know if these enhancements will apply to all 802.11 PHY types, or only selected PHY types (all PHY types is assumed in the following proposed revision of the project scope because of the listing of frequencies). Would the following better introduce the bulleted list: “This amendment defines modifications to both IEEE Std 802.11 physical layers (PHYs) and the IEEE Std 802.11 Medium Access Control (MAC). The modifications will add Ultra High Reliability capability to Wireless Local Area Network (WLAN) Basic Service Sets (BSSs) or overlapping BSSs by providing:”

## Slide 15: 802.3: PAR (3 of 6 comments)
5.2.b – It isn’t clear what the box after the list bullets was supposed to be (see posted PDF).
8.1, 2.1 explanation – This is the only hyphenated usage of ultra high, be consistent. (It appears that “Ultra High” is chosen to agree with the previously used “Extremely High” (including capitalization within a sentence.)
8.1, 5.5 explanation, 3rd paragraph – Typo? “(Basis Service Set)”.

## Slide 16: 802.3: CSD (1 comment)
1.2.1 – The answer is not responsive for this particular project. The Broad Market Potential response addresses wireless LAN in general, not the broad market for Ultra High Reliability.

## Slide 17: 802.1: PAR (2 comments)
IEEE 802.1 appreciates the detailed review by IEEE 802.3 and James Gilb, and concurs with their comments on the PAR.
In particular, if the title “Ultra High Reliability” is retained, IEEE 802.1 recommends that the scope be expanded to reflect the title. Notably the scope is lacking a clear description of ultra-high reliability. Alternatively, the title should be changed to reflect the contents of the current scope.

## Slide 18: 802.1: CSD (2 of 4 comments)
1.2.1 a) Broad Market Potential
• Editorial: In the fifth paragraph, change “The emerging of” to “The emergence of”
• We suggest introducing “Ultra High Reliability (UHR)” at this point (fifth paragraph) in the text.
• In the seventh paragraph:
– Editorial: Change “AR/VR headset” to “AR/VR headsets” (“headset” plural)
– Is “M2M” short for “mobile to mobile”? Please spell out the acronym.
1.2.1 b) Multiple vendors and numerous users
• This text focusses on WLAN only, with no mention of UHR. We suggest that, in the last line,
“continued progress of WLAN technology” also include mention of UHR.

## Slide 19: 802.1: CSD (2 of 4 comments)
1.2.4 b) Proven similar technology via testing, modeling, simulation, etc.
• Editorial: Change “several billions of” to “several billion”.
1.2.5 d) Consideration of operational costs (e.g., energy consumption).
• Editorial: Change “a significant operation cost benefits” to “a significant operational cost benefit”
(“benefit” singular)

## Slide 20: References