## Slide 1: TGbi – Proposal for sliding window MAC address rotation
Date: 2023-07-11
Authors:
Name | Affiliations | Address | Phone | email
A. De la Oliva | InterDigital, UC3M | Avda. De la Universidad 30, Leganes, Madrid, Spain | +34 91 6248803 | aoliva@it.uc3m.es
J. Levy | Interdigital |  |  | 

## Slide 2: Proposal
Sliding window of addresses:
  Two active MAC addresses: in use (MACu) and previous one (MACp)
  Epoch divided in two:
    First period of simultaneous use of MACu and MACp
      MACp used to close Block ACK transmissions, AMPDUs and retransmissions
    Second period (longer) of single use of MACu
Only two 48-bit registers are needed for A1
  The one in use and the previous one
  When a change period starts, a new MACu is decided, move current MACu to MACp, add new MACu to tuple.
Benefits
  Solves case of single STA present
  Requirements in terms of memory and queues bounded, including A1 filtering
epoch
Simultaneous use
MACp
MACu

## Slide 3: Considering stages
Before epoch transition: p x TBTT before the Epoch transition. Receive new MACu (MACu2) from higher layers
  Push currently in use MACu (MACu1) to MACp, old MACp is removed, new MACu (MACu2) set as MACu
  Station shall send MPDUs addressed only with MACp address.
  Station shall be ready to receive MPDUs addressed with MACu or MACp.
At epoch transition: duration ~ until all frames addressed with MACp are sent
  Retransmission of old MPDU uses param from old epoch.
  A-MPDU Aggregation, TXOP contains either only old MPDUs or only new MPDUs.
  Station may send buffered MPDUs already addressed with MACp address.
  Station shall send new MPDUs addressed with MACu address.
  Station may receive MPDUs addresses with MACu or MACp address
After epoch transition: long period until “Before epoch transition”
  Station shall send MPDUs addressed only with MACu address.
  Station shall be ready to receive MPDUs addressed with MACu or MACp.

## Slide 4: Summary
This approach is perfectly compatible with RCM and CFTC (soft change)
Requirements in terms of memory and queues bounded, including A1 filtering
No need for timers, just configure in advance the A1 filter