## Slide 1: TGbi – Proposal for sliding window MAC address rotation
Date: 2023-07-11
Authors:
Name | Affiliations | Address | Phone | email
A. De la Oliva | InterDigital, UC3M | Avda. De la Universidad 30, Leganes, Madrid, Spain | +34 91 6248803 | aoliva@it.uc3m.es
J. Levy | Interdigital |  |  | 

## Slide 2: Proposal
Sliding window of addresses:
  Two active MAC addresses: current (MACc) and previous (MACp)
  Epoch divided in two:
    First period where two MAC addresses for transmission are used simultaneously
      MACp used to close Block ACK transmissions, AMPDUs and retransmissions
    Second period (longer) of single use of MACc
Only two 48-bit registers are needed for A1
  The current one and the previous one
  When an epoch starts, a new MACc is decided, move current MACc to MACp, add new MACc to tuple.
Benefits
  Soft change of MAC addresses reduces performance penalty of hard change and better hides single STA in BSS
  Requirements in terms of memory and queues bounded, including A1 filtering
epoch
Simultaneous use
MACp
MACc

## Slide 3: Considering stages
(Preparation phase) p x TBTT (any way of indicating time) before the Epoch transition.
Receive new MACc (MACc2) from higher layers
  Station shall keep transmitting and receiving MPDUs addressed with MACc.
  Station shall get ready to transmit MPDUs addressed with MACc2.
  Station shall get ready to receive MPDUs addressed with MACc2.
(Transition phase) At epoch transition: duration ~ until all frames addressed with MACp are sent (or until some timeout)
  MACp=MACc, MACc=MACc2
  Retransmission of old MPDU uses param from old epoch.
  A-MPDU Aggregation, Block ACK keeps using the corresponding set of parameters, TXOP contains either only old MPDUs or only new MPDUs.
  Station may send buffered MPDUs already addressed with MACp address.
  Station shall send any packets arriving at MAC-SAP after the transition time using MACc address.
  Station may receive MPDUs addresses with MACc or MACp address
After all frames using MACp are sent (or until some timeout)
  Station shall send MPDUs addressed only with MACc address.
  Station is not expected to process any MPDUs addressed with MACp.

## Slide 4: Summary
This approach is perfectly compatible with RCM and CFTC (soft change)
Requirements in terms of memory and queues bounded, including A1 filtering
May need to define a timeout timer (e.g., 2s) to limit the transition phase e.g., a timer configurable by the AP (note the transition phase requires the receiver to monitor 2 sets of MAC addresses with two sets of parameters hence adding more processing/memory load to the receiver)

## Slide 5: Strawpoll
Do you agree on working on a solution considering a sliding window of 2 MAC Addresses for Rx and Tx?