## Slide 1
Discussion of MAC Address Transition
Date: 2023-07-09
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1-404-229-1672 | carol@ansley.com

## Slide 2
Abstract
This submission expands on ideas for OTA MAC Address transition management.

## Slide 3: Summary
Allowing OTA MAC addresses, such as the SA and DA, to change separately would improve the privacy of transmissions by making it more difficult to correlate the downstream and upstream transmissions to a STA.
Tracking the transition from one set of parameters to another is complicated. The use of two sets of queues could be a way to track this transition.

## Slide 4: Requirements
The following requirements all deal with changing a STA’s OTA MAC address.
6 | 11bi shall define a mechanism for a CPE Client to change its own OTA MAC Address when reassociating from a CPE AP to another CPE AP.
7 | 11bi shall define a mechanism for a CPE Client to initiate changing its own OTA MAC Address used with a CPE AP in Associate STA State 4 without any loss of connection.
8 | 11bi shall define a mechanism for a CPE AP to initiate changing the OTA MAC Addresses of a set of associated CPE Client’s in the BSS (those CPE Clients in Associate STA State 4) without any loss of connection.
12 | 11bi shall define a mechanism for a CPE Client and CPE AP to establish the CPE Client’s DS MAC Address without the CPE Client’s DS MAC Address being transmitted in the clear.
39 | 11bi shall define a mechanism for a BPE AP and a BPE Client to change the OTA MAC addresses, SN and PN they use for unicast transmissions.

## Slide 5: Buffer Management during Transitions
Several people have highlighted that a set period of time to end a MAC transition could be either overstate or understate the amount of time required for the transition.
Proposal:
  Track buffers to decide when ‘old’ MAC(s) can be discarded by using a dual set of buffers.
  Proposed Rules: (STA meant to cover AP or non-AP STA)
  STA is notified or determines that a transition interval has begun from old to new:
  Any new packets arriving at the MAC for transmission are queued to use the new parameter set including MAC, SN, AID, etc. in a new set of packet queues.
  Receive processing of incoming packets from WM is expanded to include old and new MACs, with related new parameter set.
  Existing packets in transmit buffers already constructed using old MAC and other old parameters are queued for transmission as is. Any retransmissions continue to use the existing packets.
  STA tracks emptying of old packets and sends a protected update frame when all old packets are emptied out of the old queues.
  Once the old buffers are empty, they will be available for the next transition as new buffers.

## Slide 6
STA
AP
STA associates/authenticates with AP and shared KEY is known to both, as well as initial STA OTA MAC (OLDMAC)
STA indicates to AP that it supports MAC Change While Associated (EDPMACChange = 1) (OLDMAC)
AP initiates MAC change by (method TBD)
Or
STA initiates MAC change by (method TBD)
STA transmits old traffic still in buffers with OLD parameters.
STA transmits new traffic to AP using (NewSMAC) as SA=TA
AP transmits old traffic still in buffers with OLD parameters.
AP transmits new traffic to STA using (NewDMAC2) as DA=RA
Example change sequence
Note that initial STA OTA MAC may be a randomized MAC address, TGbh content may provide a translation from the initial OTA MAC address and the MAC address the AP should use for packets heading into the DS
To DS | From DS
1 | 0
To DS | From DS
0 | 1

## Slide 7: List of Proposed Parameters:
EDPActive – indicates that STA or MLD supports EDP features
EDPMACChange – indicates that STA or MLD supports EDP MAC change feature(s)
  Optionally, includes whether STA supports TA/RA with separate MACs for enhanced privacy
EDPBPIActive – indicates that STA or MLD supports BPI features
Other features that might be optionally activated?

## Slide 8: References
[1] 11-22/114r3 – Enhanced Random and Changing MAC Address
[2] The Dark Side(-Channel) of Mobile Devices: A Survey on Network Traffic Analysis, IEEE Communications Surveys & Tutorials, Vol. 20, Issue 4. pp 2658-2713, 2018.