## Slide 1: NB with LBT
Author:
Name | Affiliation | Address | Email
Menzo Wentink | Qualcomm | Utrecht, The Netherlands | mwentink qti qualcomm

## Slide 2: Introduction
These slides cover some scenarios that may illustrate how NB with LBT can be beneficial for NB and Wi-Fi
Three configurations are considered
  Wi-Fi / NBFH
  NBFH / NBFH
  NB-UWB / NBFH

## Slide 3: Wi-Fi / NBFH experiments

## Slide 4: Wi-Fi / NBFH experiments
These experiments show duty cycled Wi-Fi traffic in the presence of several NBFH links
Wi-Fi has the following duty cycle
  0.5 s on, 2 s off
There are also some improvements to the eDAA scanning algorithm relative to prior submissions
  two sweeps over the entire 500 MHz per CCA evaluation (instead of one sweep per CCA evaluation as per prior simulation results)
    two sweeps per 0.5 s is actually quite high, in practice this may imply scanning just over certain center frequencies, which may impose problems when OFDMA is used by Wi-Fi

## Slide 5: Wi-Fi / NBFH simulation parameters
Wi-Fi settings
  Tx power: 23 dBm at AP (LPI), 21 dBm at STA (LPI)
  packet size: 2 ms
  downlink traffic, full buffer
  channel width: 160 MHz
  max bitrate: 2402 Mbps at HE MCS 11, 160 MHz, 2x996-tone RU, Nss = 2, 800 ns GI
  frame exchange: RTS/CTS/A-MPDU/BA
  start time: 5 s
NBFH settings
  Tx power: 14 dBm (VLP)
  dwell time: 625 us
  hop width: 4 MHz (30 Mbps max PHY rate, Nss = 1)
  hopping pattern: random, 125 hops (500 MHz total)
  eDAA settings: 0.5 s between CCAs
  CCA trigger settings: 7 us CCA before each hop, FBE, trigger threshold 3, 20 MHz segments
  start time at ~0.5 s intervals starting at 0 s
  downlink traffic, full buffer
Channel model
  AWGN channel with a breakpoint at 5 m
    pathloss = 40.05 + 20log10(f/2.4) + 20log10(min(d, b)) + (d > b) * (35log10(d/b))
    where f = 5.18 GHz, d = distance, b = breakpoint = 5 m

## Slide 6: Wi-Fi / NBFH topology
nb_r1252_dc_3u3d_r4a_r1
LPI Wi-Fi link
downlink traffic
AP
STA
VLP NBFH links
VLP NBFH links

## Slide 7: Wi-Fi-only (no NBFH)
nb_r1252_dc_3u3d_r4a_r1
(this plot is not defined for this experiment)

## Slide 8: Wi-Fi / NBFH (eDAA)
nb_r1252_dc_3u3d_r4b_r1

## Slide 9: Wi-Fi / NBFH (LBT with CCA trigger)
nb_r1252_dc_3u3d_r4c_r1

## Slide 10: Observations (Wi-Fi / NBFH)
eDAA appears to be inadequate as a coexistence mechanism
  the response time is too long
  no protection of ongoing NB transmissions
LBT with CCA trigger works quite well
  quick response to other traffic
  quick reuse of the channel when other traffic is no longer present
  low latency and stable throughput, both for Wi-Fi and NB

## Slide 11: NBFH / NBFH experiments

## Slide 12: NBFH / NBFH experiments
The following experiments show results for 7 NBFH links in relative close proximity, with more pathloss on each of the links relative to the prior experiments
  the higher pathloss causes that colliding hops will not be received at any of the receivers

## Slide 13: NBFH simulation parameters
NBFH settings
  Tx power: 14 dBm (VLP)
  dwell time: 625 us
  hop width: 4 MHz (30 Mbps max PHY rate, Nss = 1)
  hopping pattern: random, 125 hops (500 MHz total)
  eDAA settings: 0.5 s between CCAs, 60% occupancy threshold, 20 MHz segments
  CCA trigger settings: 7 us CCA before each hop, trigger threshold 3, 20 MHz segments
  start time at ~0.5 s intervals starting at 0 s
  downlink traffic, full buffer
Channel model
  AWGN channel with a breakpoint at 5 m
    pathloss = 40.05 + 20log10(f/2.4) + 20log10(min(d, b)) + (d > b) * (35log10(d/b))
    where f = 5.18 GHz, d = distance, b = breakpoint = 5 m

## Slide 14: NBFH / NBFH topology
nb_r1501_nbnb_3u3d_r1
7 NBFH links

## Slide 15: NBFH / NBFH (eDAA)
nb_1501_nbnb_edaa_r1
(500 MHz hopping BW)

## Slide 16: NBFH / NBFH (LBT with CCA trigger)
nb_r1501_nbnb_3u3d_r1
(500 MHz hopping BW)

## Slide 17: NBFH / NBFH (eDAA)
nb_1501_nbnb_edaa_r2
(300 MHz hopping BW)

## Slide 18: NBFH / NBFH (LBT with CCA trigger)
nb_r1501_nbnb_3u3d_r2
(300 MHz hopping BW)

## Slide 19: Observations (NBFH / NBFH)
NBFH can benefit from using LBT
  interference to ongoing NB transmissions is avoided

## Slide 20: NB-UWB / NBFH experiments

## Slide 21: NB-UWB introduction
Narrowband assisted ultrawideband (NB-UWB) has been proposed in 802.15.4ab as a mechanism to boost link budget for UWB
  UWB packets are transmitted as multiple shorter fragments, each using a lower duty cycle in the 1 ms measurement interval, which allows for higher transmit power
  fragments can be combined at the receiver
The NB protocol exchange is used to synchronize the UWB transmissions and to exchange measurement data
  Poll / Response / Responser report / Initiator report
An exemplary NB-UWB frame exchange is shown below

## Slide 22: NB-UWB settings
The following NB-UWB settings were used in the simulations
  slot time: 1 ms
  ranging round: 2 initial NB slots + 8 UWB slots + 4 NB report slots = 14 ms
  ranging block: 6 rounds = 84 ms
  continuously repeated blocks (continuous ranging session)
  duty cycle for 1 responder: 3% per node
  NB bandwidth: 2.5 MHz
  NB Tx power: 14 dBm
The simulated scenario is UNII-3 where 80 MHz is assumed to be occupied by Wi-Fi and 40 MHz is shared by NBFH and NB-UWB

## Slide 23: NB-UWB / NBFH simulation parameters
NB-UWB settings
  Tx power: 14 dBm
  slot time: 1000 us
  channel width: 2.5 MHz
  PSD: 10 dBm/MHz
  fixed NB channel
  Tx duty cycle: 3% per node (6% total)
  start time: 0 s
  11.9 ranging rounds per second target
NBFH settings
  Tx power: 14 dBm
  dwell time: 625 us
  hop width: 1 MHz
  PSD: 14 dBm/MHz
  40 hops in 40 MHz, random hopping pattern
  start time: 5 s
Channel model
  AWGN channel with a breakpoint at 5 m
    pathloss = 40.05 + 20log10(f/2.4) + 20log10(min(d, b)) + (d > b) * (35log10(d/b))
    where f = 5.18 GHz, d = distance, b = breakpoint = 5 m

## Slide 24: NB-UWB / NBFH coexistence setup
NBFH
NB-UWB

## Slide 25: NB-UWB / NBFH (scheduled NB-UWB, no LBT)
nau_r1708_r2a
NB-UWB metrics when NBFH is active:
~8 rounds/s
(30% less rounds)
3.0 ms Tx time per node per round
(20% more Tx time per round)
NBFH starts here
30% less rounds
20% more Tx time per round

## Slide 26: NB-UWB / NBFH (scheduled NB-UWB, LBT)
nau_r1708_r2b
NB-UWB metrics when NBFH is active:
~10.2 rounds/s
(6 % less rounds)
2.51 ms Tx time per node per round
(0.4% more Tx time per round)
NBFH link starts here
6% less rounds
0.4% more Tx time per round

## Slide 27: Observations (NB-UWB / Wi-Fi)
The NB-UWB protocol has little resilience against frame loss
  several protocol frames have no acknowledgement
  there are no retries
  frame loss can be caused by collisions with hops of a nearby NBFH link
LBT helps protect the NB-UWB protocol frames
  the number of successful ranging rounds is increased when LBT is used
LBT also reduces power consumption at the NB-UWB device
  NB-UWB transmissions are suppressed when high interference might cause them to fail anyway, reducing unnecessary transmit time

## Slide 28: Appendix Overview of NB channel access mechanisms

## Slide 29: LBT for NB
Listen before Talk (LBT) for NB uses a CCA before every hop
  fixed LBT before every scheduled transmission
  could also be referred to as Frame Based LBT (FB-LBT)
With some extra measures, the CCA time could be relatively short
  details are in the next slide on LBT with CCA trigger
  without extra measures, the CCA time should be in the order of 187 us, so that access will not happen during Wi-Fi backoffs and SIFS intervals
    the potentially high frequency of the NB CCAs makes it necessary that the CCA time is not too short
    but a long CCA time is difficult to integrate into the existing NB architecture

## Slide 30: LBT with CCA trigger
CCA trigger uses a short CCA (e.g. 7 us) before every hop, but disables a 20 MHz segment when multiple consecutive CCA-busies ('triggers') occur in the segment, until several consecutive CCA-idles occur in the segment
  the NB node keeps a tally of consecutive CCA busy events ('triggers') in each segment that it hops in:
    +1 when the CCA before a hop inside the segment is busy
    –1 when the CCA before a hop inside the segment is idle
  when the number of triggers ≥ 3 the segment is blocked, otherwise it can be used (provided that the CCA before hops in that segment is idle)
  the trigger count is capped between 0 and 6, which implies a hysteresis of 4 consecutive CCA idles before the segment is released

## Slide 31: eDAA
Enhanced Detect and Avoid (eDAA) was proposed in ETSI BRAN as an enhanced version of DAA as defined in EN 300 328 (2.4 GHz), but with
  0.5 s between CCAs
  evacuation in 20 MHz blocks
  two options for channel restoration:
    option 1: after 0.5 s when CCA is clear
    option 2: after 2.5 s without CCA (exponentially increasing)
eDAA can use an offline sweep to determine a spectrum map
  the sweep can be in one go or in portions during the 0.5 s between CCA checks
  every 0.5 s eDAA analyzes the spectrum map and disable 20 MHz segments where WB is detected
    in the sims, WB is considered to be present when >60% of a 20 MHz segment has a CCA busy
  the use of a spectrum map avoids any issues between NB links, but it does not appear to be an improvement for coexistence with WB

## Slide 32: References

## Slide 33: References
NBFH
  IEEE 11-23-0453-00-coex-nb-overview
  IEEE 11-23-0454-00-coex-impact-of-bt-on-wlan-performance
  IEEE 11-23-0455-00-coex-wi-fi-deferral-for-nb-signals
  BRAN(21)109h004r2_EN_303_687_NB_Proposals_for_DAA_Optimisation
  BRAN(21)109h007_NB_coexistence_with_WB_in_6_GHz
  ETSI EN 300 328 (2.4 GHz)
  ETSI EN 301 893 (5 GHz)
  ETSI EN 303 687 (6 GHz)
NB-UWB
  15-21-0409-01-04ab-narrowband-assisted-multi-millisecond-uwb
  15-21-0593-00-04ab-more-on-nba-mms
  15-23-0119-00-04ab-coexistence
  15-22-0381-02-04ab-nba-uwb-ranging-text-proposal-for-15-4ab-tfd