## Slide 1: Discussion on AMP Power link
Date: 2023-08-08
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Yinan Qi |  |  |  | v-qiyinan@oppo.com
Doc.: IEEE 802.11-23/1356r0
July 2023

## Slide 2: Abstract
During the previous discussion, there has been proposal [1] to study and specify at least one mode to support RF energy harvesting.
In this submission, detailed aspects on the power link for AMP will be discussed.
Doc.: IEEE 802.11-23/1356r0

## Slide 3
Scenarios
In different use cases, it can use different node to provide the RF power. Based on the discussion of the typical use case[2], the RF power may be provided by:
  The AP that communicate to the AMP STA
  An non-AP STA that communicate to the AMP STA
  A dedicated intermediate power node as shown in the following Figure 1.
Weijie Xu (OPPO)
Slide 3
Doc.: IEEE 802.11-23/1356r0
July 2023
Figure 1: Use intermediate node to extend coverage of power link
Advantages of providing RF power using a dedicated power node:
  Extend the coverage of power link with low cost deployment
  Resolve the blocking issue in real deployment
  Ease the implementation of the AP, especially when backscattering is used.

## Slide 4
Requirement
Functionality of the power link
  Provide RF power to the AMP STA
  Additional control signaling?
Requirement of the RF power link
  Shall meet the regulation requirements
    Frequency bands/Channel bandwidth
    Maximum transmission power
    ACLR
    Frequency hopping
      In S1G, there is hopping requirement
    Maximum duration of one transmission
    Maintain coexistence with other transmission
    Etc.
  Provide sufficient coverage
    10-30 meters indoor
Weijie Xu (OPPO)
Slide 4
Doc.: IEEE 802.11-23/1356r0
July 2023

## Slide 5
Operation of power link
Control the power link if an intermediate node used
  The network shall be able to activate or deactivate the power link for power saving and interference management
  The power link is operated based on network’s configuration
    Maximum transmission power, transmission duration, operation frequency, waveform, duty cycle etc.
AMP power node
AMP AP AMP STA
When backscattering is used, the incident carrier for backscattering shall be present when the AMP STA is scheduled to do backscattering.
  When the incident carrier is send by an intermediate node, the transmission timing of incident carrier shall be well managed.
Weijie Xu (OPPO)
Slide 5
Doc.: IEEE 802.11-23/1356r0
July 2023

## Slide 6
Summary
In this submission, the following aspects on power link for AMP were discussed
  Scenarios
  Requirements
  Operation of power link
Weijie Xu (OPPO)
Slide 6
Doc.: IEEE 802.11-23/1356r0
July 2023

## Slide 7: Reference
IEEE 802.11-23/1190r4, Further Discussion on AMP PAR
IEEE 802.11-23/0436r0 Technical Report on support of AMP IoT devices in WLAN
Doc.: IEEE 802.11-23/1356r0
May 2023