## Slide 1: Discussions on Non-primary Channel Access
Date: 2023-09-08
Authors:
Name | Affiliations | Address | Phone | email
Shawn (Sanghyun) Kim | WILUS Inc. | 216 Hwangsaeul-ro, Seongnam-si, Gyeonggi-do, Korea | +82-31-712-0523 | shawn.kim@wilusgroup.com
John (Ju-Hyung) Son |  |  |  | john.son@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com
Greg Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
September 2023
Sanghyun Kim (WILUS), et al.

## Slide 2: Problem
Even if a STA supports wide bandwidth operation (e.g., 160/320 MHz), the STA cannot access idle secondary subchannels while the primary 20 MHz subchannel is BUSY
Due to this dependency on the primary 20 MHz subchannel, the channel accessibility of idle subchannels for the current Wi-Fi STAs is limited
September 2023
Sanghyun Kim (WILUS), et al.

## Slide 3: Non-primary channel access [1-7]
Several contributions have been submitted to tackle the dependency issue on the primary 20 MHz channel
  These contributions propose mechanisms that allow the backoff process to continue on the auxiliary primary 20 MHz channel (A20) when the primary 20 MHz channel (P20) is busy
September 2023
Sanghyun Kim (WILUS), et al.
6
5
4
3
OBSS TXOP
(Primary 20MHz is occupied)
Frame exchanges on the secondary channels
A20
2
1
0
Frame exchanges
2
1
0
P20
BO on APCH
(due to BUSY PCH)

## Slide 4: Regulation issues
According to the ETSI regulation, changing the backoff channel is permitted only once per second in multi-channel operation
  If a STA continues its backoff procedure on A20 while P20 is busy, it must perform the backoff procedure on A20 for at least 1 second
Short summary of the ETSI regulation (4.2.7.3.2.3 Multi-channel operation) [8]
  Option 1 (Per-20 MHz independent CCA)
    Device may use any combination/grouping of channels, if it satisfies the channel access requirements for an initiating device on each such operating channel
  Option 2 (Wideband channel access of Wi-Fi)
    Device that uses a combination/grouping of adjacent 20 MHz channels that is a subset of the 40/80/160 MHz channels may transmit on any of the 20 MHz channels, if:
      The device has gained the right to the primary operating channel as defined in 4.2.7.3.2.6 and
      The device performs CCA of at least 23 us immediately before the intended transmission on each of the other operating channel
    The choice of the primary operating channel
      Option A: Chosen randomly whenever the CW corresponding to a completed transmission on the current primary operating channel is set to its minimum value
      Option B: Arbitrarily determined and not changed more than once per second
September 2023
Sanghyun Kim (WILUS), et al.

## Slide 5: Example of regulatory-compliant non-primary channel access
Once a STA accesses the channel through A20, it must adhere to the following rules for at least 1 second:
  Access the channel through A20
  An AP MLD may indicate channel information used for backoff through the other APs when an AP performs channel access through A20
    A STA that has obtained backoff channel information of its associated AP can change its CCA channel accordingly
September 2023
Sanghyun Kim (WILUS), et al.
OBSS TXOP
(P80 is occupied)
Frame exchanges on S80
Frame exchanges
Frame exchanges on S80
…
Frame exchanges
OBSS TXOP
Frame exchanges
At least 1 second long
OBSS TXOP
(P80 is occupied)
(P80)
P20
(S80)
A20

## Slide 6: Limitations of the previous example
During the time AP is operating on secondary channels, Beacon Tx/Rx should be performed on A20
  APs operating on the 2.4/5 GHz band can only transmit 20 MHz Beacon frames following the baseline specification
  Therefore, legacy STAs might lose the connection
There might be MPDU loss for non-AP STAs that realize late that the AP is operating on APCH
  If a non-AP MLD receives management frames from the AP MLD at a delayed time, it will experience a delay in following the AP's operating channel
  Furthermore, STAs that have not pass the 1 second since the last backoff channel change cannot immediately do channel access on the AP’s new primary channel
Performing nonprimary channel access in a way that satisfies the regulations seems to increase complexity and cause connectivity issues for both legacy and UHR STAs
September 2023
Sanghyun Kim (WILUS), et al.

## Slide 7: Proposal: Non-primary channel access using MLO
Utilizing MLO to mitigate P20 dependency problem
  An AP MLD and a non-AP MLD setup multiple links with the same operating channels
    One AP of the multiple APs operates on the Primary Link and the other APs operate on the Auxiliary Links
      Auxiliary Link is not a standalone link (similar to the nonprimary link of the NSTR mobile AP MLD)
    Only one link is active at anytime
      An AP MLD and its associated non-AP MLDs perform frame exchanges through the active link
September 2023
Sanghyun Kim (WILUS), et al.
AP1
AP2
AP3
AP MLD
Primary
AP(Link)
Auxiliary
AP(Link)
160 MHz
Auxiliary
AP
160 MHz
Primary
AP
A20
(P20 of the auxiliary AP)
P20
Operating channel of the APs

## Slide 8: Illustration of the proposed solution
September 2023
Sanghyun Kim (WILUS), et al.
P80 subblock of Auxiliary AP
(S80 of Primary AP)
2
1
0
160 MHz TXOP
(TXOP1)
OBSS TXOP
2
1
0
80 MHz TXOP
(TXOP2)
2
1
0
160 MHz TXOP
(TXOP3)
Active duration of the Auxiliary Link
(P20 of Primary AP is occupied)
Active duration of the
Primary Link
Active duration of the
Primary Link
P80 subblock of Primary AP
(S80 of Auxiliary AP)
P20
A20
P20 : Primary 20 MHz of Primary AP
A20 : Primary 20 MHz of Auxiliary AP (Auxiliary 20 MHz)
Primary
AP
Auxiliary
AP
AP MLD
STA1
STA2
Non-AP MLD
Primary
AP
Auxiliary
AP
AP MLD
STA1
STA2
Non-AP MLD
Primary
AP
Auxiliary
AP
AP MLD
STA1
STA2
Non-AP MLD
INACTIVE
INACTIVE
INACTIVE

## Slide 9: Brief analysis of the proposed solution
No regulation issues (relevant to P20 changes)
  The proposed solution alters the link used for accessing operating channels instead of changing the primary 20 MHz channel of a STA
Limited hardware complexity
  Since MLD utilizes a single backoff channel (of the link in active state), the hardware complexity in terms of channel access would be reduced
  As only one link is in an active state, MLD can utilize a single radio for both the primary and the auxiliary link
    A STA operating on an inactive link might do nothing for that link
September 2023
Sanghyun Kim (WILUS), et al.

## Slide 10: Discussions
Wasted Link ID?
  An MLD can operate on up to 15 links, while the number of non-overlapping 320/160 MHz operating channels is limited. Therefore, even if some Link IDs are used by the Auxiliary APs, there should be no shortage of Link IDs in typical scenarios
    There are only three non-overlapping 320 MHz channels
    There are less than ten 160 MHz channels in 5/6 GHz band
Power consumption?
  Only one link among the Links (a pair of Primary and Auxiliary Link(s)) is in active state, so power consumption is limited
    When the Links share a single radio, power consumption is not affected by the number of links
    Even if an Auxiliary Link use its own radio, power consumption of the link would be limited because the link is not a standalone link
      A STA operating on an inactive link may support limited capability for that link
September 2023
Sanghyun Kim (WILUS), et al.

## Slide 11: Summary
High dependency on the Primary 20 MHz subchannel of the Wi-Fi results in inefficient channel access for wideband channel access
By configuring multiple links that share the same operating channel, it is possible to reduce the dependency on the Primary 20 MHz channel
September 2023
Sanghyun Kim (WILUS), et al.

## Slide 12: Reference
[1] 11-23/34r0 Non-primary Channel Utilization (Sindhu Verma, Broadcom)
[2] 11-23/631r1 secondary channel usage and secondary 20MHz channel backoff (Liwen Chu, NXP)
[3] 11-23/797r1 Non-primary channel access (Yongho Seok, MediaTek)
[4] 11-23/961r0 UHR secondary channel access (Minyoung Park, Intel)
[5] 11-23/962r0 UHR secondary channel access evaluation (Dibakar Das, Intel)
[6] 11-23/1112r0 Thoughts on Secondary Channel Access (Insun Jang, LG)
[7] 11-23/1288r0 Non-primary Channel Utilization Follow-up (Sindhu Verma, Broadcom)
[8] ETSI EN 301 893v2.1.1, 5 GHz RLAN; Harmonised Standard for access to radio spectrum https://www.etsi.org/deliver/etsi_en/301800_301899/301893/02.01.01_60/en_301893v020101p.pdf
September 2023
Sanghyun Kim (WILUS), et al.