## Slide 1: non-collocated AP MLD framework further discussion

## Slide 2: Background
FTTR/G.fin(Fibre-to-the room/Fibre based in-premises networking) products widely deployed in residential environment to improve user’s experience.
  provides low latency and high reliability via fibre backhaul connection
  composed by one MFU and several SFUs deployed in different places
  each MFU and SFU has one AP MLD that provides wireless connection

## Slide 3: Motivation
We’re looking forwards to the next generation of FTTR product containing the UHR technology.
  higher manageability of the whole network
  seamless roaming for mobility device
  seamless Wi-Fi sensing to improve accuracy
  multiple links for in-door location
  simplify the design of AP MLD and reduce Wi-Fi chip set cost
  try to reuse current EHT AP MLD framework as much as possible
  Non-collocated AP MLD is the best candidate framework with the following merit

## Slide 4: the merit of non-collocated AP MLD(1)
simplify the design of AP MLD
    3 radios on one 11be chipset is already complicated, we don’t look for more radios integrated into one chipset to serve the high-ends non-AP MLD(e.g., EMLSR non-AP MLD may support more than 3 links)
    new AP MLD framework allow AP vendor to deploy multiple dual-radio AP MLDs in different places to provide a batch of links, to meet all kinds of high-ends non-AP MLD and IOT device requirements .
seamless roaming
  allow non-AP MLD to set up any links at any place for the seamless traffic delivery during movement
multi-link for Wi-Fi location and seamless Wi-Fi sensing
  possible to have multi-session for the location and Wi-Fi sensing under MLO framework

## Slide 5: the merit of non-collocated AP MLD(2)
compatible with other M-AP schemes:
  compatible with C-OFDMA,C-SR,C-TDMA,C-TWT scheme etc. if more than two links operating on the same channel.
  no fairness issue, UHR AP MLD High MAC coordinates the media resource access
  less overhead issue on the MAP coordination signaling, MAP coordination signaling can be delivered with wired backhaul,like Fibre backhaul in FTTR product.
compatible with all kinds of 11be non-AP MLD and single link STA operation
  compatible with single link STA
  compatible with 11be STR non-AP MLD
  compatible with 11be NSTR/EMLSR/EMLMR non-AP MLD on the non-real-time operation

## Slide 6: one example between UHR non-AP MLD and non-collocated AP MLD
backhaul
backhaul
(SFU)EHT AP MLD2
AP1.1
2.4 GHz
AP2.1
5 GHz
AP2.2
6 GHz
AP3.1
5 GHz
AP3.2
6 GHz
UHR AP MLD high MAC
AP1.2
6 GHz
(MFU)EHT AP MLD1
(SFU)EHT AP MLD3
UHR AP MLD
L1
L2
L3

## Slide 7: The extension in discovery procedure
UHR AP MLD assigns a unique MLD index for each EHT AP MLD
EHT AP MLD assigns the link ID for the affiliated AP as it does in 11be
UHR non-AP MLD can distinguish all the links via UHR link ID= <MLD index, link ID>
one flag should be set in the RNR to indicate whether two reported APs within different EHT AP MLDs belongs to the same UHR AP MLD or not.
All APs broadcast the same UHR AP MLD MAC address in ML element

## Slide 8: one example of non-collocated AP MLD discovery
backhaul
backhaul
EHT AP MLD2(MLD index=1)
AP1.1
2.4 GHz
AP2.1
5 GHz
AP2.2
6 GHz
AP3.1
5 GHz
AP3.2
6 GHz
UHR AP MLD high MAC
AP1.2
6 GHz
EHT AP MLD1(MLD index=0)
EHT AP MLD3(MLD index=2)
UHR AP MLD
link ID=0
link ID=1
link ID=0
link ID=1
link ID=0
link ID=1
UHR link ID =(1,0)

## Slide 9: the extension in MLO setup procedure
UHR non-AP MLD may set up multi-link with different EHT AP MLDs belonging to the same UHR AP MLD
  (re)association request may carry multiple ML elements
authentication, association, 4HS frames are transparently delivered over EHT AP MLD
  authentication, association, 4HS shall be exchanged between UHR non-AP MLD and UHR AP MLD high MAC
  one signaling in authentication frame sent by non-AP MLD to indicate it’s a UHR non-AP MLD or EHT non-AP MLD, so that the EHT AP MLD can decide to handle it locally or forward to UHR AP MLD high MAC

## Slide 10: one example of setting-up procedure in non-collocated AP MLD

## Slide 11: AID assignment in non-collocated AP MLD framework
There will be some challenge for 12-bit AID field in larger scale non-collocated AP MLD network
  thousands of STAs may associate with the same non-collocated AP MLD in larger scale network
  only allow maximum 2K STAs association at the same time according to current length of AID field
AID field needs some extension and is also compatible with legacy STA/non-AP MLD
  UHR AID =<MLD index, AID>
  UHR AP MLD high MAC assigns and recycles MLD index of each EHT AP MLD.
  multiple EHT AP MLDs coordinate to assign a common AID to the set-up link of UHR non-AP MLD
  non-AP MLD has the same AID on different set-up links

## Slide 12: one example of the AID assignment by non-collocated AP MLD
backhaul
backhaul
EHT AP MLD2(MLD index=1)
AP1.1
2.4 GHz
AP2.1
5 GHz
AP2.2
6 GHz
AP3.1
5 GHz
AP3.2
6 GHz
UHR AP MLD high MAC
AP1.2
6 GHz
EHT AP MLD1(MLD index=0)
EHT AP MLD3(MLD index=2)
UHR AP MLD
link ID=0
link ID=1
link ID=0
link ID=1
link ID=0
link ID=1
AID=100
AID=100
UHR AID=<1,100> or <2,100>
UHR STA

## Slide 13: PPDU delivery with NSTR/EMLSR/EMLMR non-AP MLD
Due to the latency in the backhaul, run-time coordination will encounter some challenge.
  start time/end time alignment is hard to support for NSTR non-AP MLD
  another aspect, less commercial AP MLD support ending time alignment
  therefore, non-collocated AP MLD frame may not support ending time alignment
  non-run time coordination in the backhaul make it possible for the non-overlap PPDU delivery on single link
  two EHT AP MLDs coordinate a non-overlap time slot for PPDU delivery on single link when STA operates in NSTR/EMLSR/EMLMR mode
  also,support UL traffic delivery on more than 1 link when the STA operates in NSTR mode as it is in 11be.
  TSF synchronization among different EHT AP MLDs in UHR AP MLD?
  No requirement.

## Slide 14: one example of the PPDU delivery between NSTR/EMLSR/EMLMR non-AP MLD and non-collocated AP MLD
UHR
non-AP MLD
UHR
AP MLD
STA1
STA2
AP1(EHT AP MLD1)
AP2(EHT AP MLD2)
T1
T2
T3
UHR
non-AP MLD
UHR
AP MLD
STA1
STA2
AP1(EHT AP MLD1)
AP2(EHT AP MLD2)
T1
T1
Fig.1 single link PPDU delivery between NSTR/EMLSR/EMLMR non-AP MLD and non-collocated AP MLD
Fig.2 multi-link UL traffic delivery between NSTR non-AP MLD and non-collocated AP MLD
time slot negotiation on backhaul

## Slide 15: summary
introduce the current FTTR product framework and next generation of FTTR development direction
describe the motivation of non-collocated AP MLD framework
introduce a simple approach to have non-collocated AP MLD framework based on EHT AP MLD framework
the extension for non-collocated AP MLD in discovery, association, AID assignment and PPDU delivery procedure

## Slide 16
THANK YOU 

## Slide 17: reference
[1] 11-23-0480-00-0uhr-uhr-proposed-par.pdf
[2] 11-22-1910-03-0uhr-seamless-roaming-for-uhr.pptx
[3] 11-22-1512-00-0uhr-multi-ap-coordination-for-uhr.pptx
[4] ITU-T G.9940(G.fin-SA) High speed fibre-based in-premises transceivers – system architecture

## Slide 18: SP1
Do you agree UHR group should have some further study on the non-collocated AP MLD framework?
  Y:
  N:
  A: