## Slide 1: Secondary Channel Usage Follow-up
Date: 2023-08-21
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap
Through the subchannel switch, the AP and STAs can use the nonprimary subchannel (a subchannel other than the subchannel with primary 20MHz channel) when the primary subchannel is busy.
  At least on the nonprimary subchannel the medium access recovery is needed.
    The method defined in 11be can be used if losing the medium synchronization at both sides is not specially processed.
With the SST, the usage of the nonprimary subchannel is ok even if the associated STAs don’t support subchannel switch.
The RU index, BW negotiation etc. need more thought.

## Slide 3: Medium Access of Primary Subchannel
The OBSS TXOP may one of the following:
  The Duration in the MAC header can be used to protect part of the remaining time of a TXOP.
  When the Duration is used to protect the remaining time of a TXOP and the frame exchanges can’t use whole reserved time of the TXOP, CF-End may be used to release the unused remaining TXOP time.
With such OBSS’s behavior, the AP/STA that does the subchannel switch may create the collision with the frame exchanges on primary subchannel in the OBSS.
  The subchannel switch under SST has no such issue.
The method to address such issue:
  1), an AP announces its activation of subchannel switch.
    With such announcement, the OBSS may use whole TXOP protection.
  2), an AP/STA does the medium access recovery when switching back to the primary subchannel from nonprimary subchannel.

## Slide 4: Different Switch Time
The different device may require the different time for the subchannel switch (subchannel switch time).
When switching to a new subchannel (primary or nonprimary), an AP/STA can’t transmit a PPDU to a peer device before the peer device’s subchannel switch time based on the common understanding of the time point when the subchannel switch starts.

## Slide 5: Threshold for Subchannel Switch
If the TXOP duration in the primary subchannel is from the neighbor BSS (or from TDLS link) and is short, the STA/AP may not do the subchannel switch.
  The failed frame exchange with a STA that doesn’t do the subchannel switch may the AP’s further subchannel switch.
One solution could be to define the threshold of the TXOP duration.
  If the OBSS’s TXOP duration is shorter than the threshold, the STA/AP will not do the subchannel switch.
However it is difficult for AP and STA simultaneously switch from one non-primary subchannel to another non-primary subchannel.
  The simple solution to allow one non-primary subchannel in a BSS.

## Slide 6: RU Index in MU PPDU by using non-primary Subchannel
When the RU index is based on the backoff 20MHz channel and more than one non-primary subchannel exists, the AP and STAs (or the different STAs) may assume the different RU index values for same RU.
Primary 20MHz
channel
80MHZ channel 1
(subchannel1)
(primary subchannel)
80MHZ channel 2
(subchannel2)
80MHZ channel 3
(subchannel3)
80MHZ channel 4
(subchannel4)
Backoff 20MHz
channel 2
Backoff 20MHz
channel 3
Backoff 20MHz
channel 4
BSS operating channel
STAs that switch to subchannel2 assume the
RU index based on Backoff 20MHz channel 2.
STAs that are in subchannel2 assume the
RU index based on Backoff 20MHz channel 1.
The two TB PPDUs have the same BW values with different channel puncture.

## Slide 7: RU Index in MU PPDU by using non-primary Subchannel
Solution option 1:
  The TB PPDU (MU PPDU) BW and the covered high priority 20MHz backoff channel will decide the RU index.
Solution option 2:
  The TB PPDU (MU PPDU) that doesn’t cover the primary 20MHz channel will use one nonprimary subchannel.
Primary 20MHz
channel
80MHZ channel 1
(subchannel1)
(primary subchannel)
80MHZ channel 2
(subchannel2)
80MHZ channel 3
(subchannel3)
80MHZ channel 4
(subchannel4)
Backoff 20MHz
channel 2
Backoff 20MHz
channel 3
Backoff 20MHz
channel 4
BSS operating channel
STAs that switch to subchannel2 assume the
RU index based on Backoff 20MHz channel 2.
STAs that are in subchannel2 assume the
RU index based on Backoff 20MHz channel 1.
The two TB PPDUs have the same BW values with different channel puncture.

## Slide 8: Dynamic BW Negotiation by using non-primary Subchannel
When an AP and a STA switch to non-primary 20MHz channel and do the dynamic BW negotiation for multiple non-primary subchannels, the clarification about how to select the narrower BW should be added.
Option 1:
  The single non-primary subchannel is used when the primary subchannel is not covered, or the dynamic BW negotiation is disallowed when the primary subchannel is not covered.
    The simple solution is that 11bn only allows one non-primary subchannel.
Option 2:
  The different priority of non-primary subchannels are defined, and the narrower BW of dynamic BW negotiation is given to the high priority non-primary subchannel.
Primary 20MHz
channel
80MHZ channel 1
(subchannel1)
(primary subchannel)
80MHZ channel 2
(subchannel2)
80MHZ channel 3
(subchannel3)
80MHZ channel 4
(subchannel4)
Backoff 20MHz
channel 2
Backoff 20MHz
channel 3
Backoff 20MHz
channel 4
BSS operating channel
RTS
CTS