## Slide 1: Seamless Roaming for UHR Follow-Up
Date: 2023-08
Authors:

## Slide 2: Summary of this Presentation
Collected more feedback from offline discussions
This version clarifies the following aspects:
  General direction
  “AP MLD” vs “Single Mobility Domain (SMD) AP MLD”
  More details on 3 Phases of seamless roaming
  Context transfer and standardization
  Targeting scenarios

## Slide 3: General Direction
It seems that most are interested in achieving the following to enhance roaming in UHR
  Avoid re-authentication, reassociation and re-establishment of security keys, PN, SN, BA sessions, etc. to keep the roaming delay and interruption minimum
  Leaving the AP MLD untouched so it continues to serve pre-UHR STAs (or UHR STAs that do not support seamless roaming)
  Some context transfer is needed during transition
  Either the client or the network can initiate seamless roaming
  Prefer not to have two non-colocated APs serving the non-AP MLD concurrently for an unbounded time

## Slide 4: AP MLD vs SMD AP MLD
Need to keep the AP MLD, which is still needed to serve pre-11bn clients
Create an MLD-like entity (SMD AP MLD) that manages all the APs (colocated or not) and maintains the following context with an 11bn client:
  Authen/assoc/security/PN/SN/BA sessions, etc
  The entity can be physically located anywhere, including in one of the APs
  An 11bn non-AP MLD that supports this feature associates with this entity directly (and not to the AP MLDs)

## Slide 5: 3 Phases of Seamless Roaming
Phase 1 - Preparation
  New target AP(s) will be discovered and added by the non-AP MLD or SMD AP MLD
  Detection of roaming condition: either by the client or the network
Phase 2 - Transition
  Initiation of roaming: either by the client or the network
  Serving AP transfers the context (and optionally forward DL packets – depending on the capability of the backhaul) to the target AP
  Serving AP attempts to complete the buffered DL packets (and any DL in-flight packets from the Gateway to the serving AP). STA attempts to finish the UL packets with the serving AP
  Data path switched to the target AP
  Depending on the network configuration, there may be a short overlap in time where the STA is served by both the serving AP and the target AP e.g., a single radio STA could be served by both APs that are operating on the same primary channel
  STA starts to use the target AP for both UL and DL traffic
Phase 3 – Post-Transition
  STA will only communicate with the target AP and the spec can define a time-out after which the old AP is removed, along with any context of the non-AP MLD kept at the old AP

## Slide 6: Context Transfer & Standardization
During Phase 2 (transition), context needs to be transferred from the serving AP to the target AP
Context may include: security, PN, SN, BA sessions, QoS, etc
802.11 spec will focus on the requirements needed for the air interface protocol to support seamless roaming:
  May specify the type of information (at a high level) to be exchanged between the APs to cover the most common use cases
  Since there are many different backhaul architectures, it may be difficult to capture all the cases. Should keep it at high level so not to preclude/contradict any existing backhaul architectures

## Slide 7: Target Scenario
Some offline feedback indicated allowing both serving and target APs to serve the STA concurrently even after roaming could create complexity
=> Agreed that 11bn not to allow concurrent transmissions (from multiple non-colocated APs to the STA) outside of the transition phase (Phase 2 in this slide)

## Slide 8: Conclusion
We see there are lots of commonalities between several proposals from different members and most are trying to achieve the following goals:
  Either the APs or the STA can initiate seamless roaming
  Keep using the same encryption key
  No reauthen, reassoc, and no need to re-establish the BA sessions
  Should be able to operate without resetting the PN and SN
  1bn should limit concurrent serving by non-colocated APs to only during the roaming phase

## Slide 9: Appendix
Recap of the seamless roaming proposal

## Slide 10: Seamless Roaming
An SMD AP MLD controlling all the APs (colocated or not)
Affiliated APs
(non-colocated)
SMD AP MLD (logical entity, physically could be
co-located with any of the AP below for each client)
AP1
AP2
AP3
APn
STAx
STAy
Router
Data path
Note: SN/PN assignment, encryption are still performed at each AP inline with the existing MLO architecture
…