## Slide 1: Expedited Wake-up in Unscheduled AP MLD Power Saving
Date: 2023-09-11
Authors:

## Slide 2: Abstract
A power saving operation of AP is included in the 11bn proposed PAR [1].
  …This amendment provides a mechanism to reduce power consumption for Access Points (APs) (including mobile APs)…
In UHR SG, unscheduled AP MLD power saving was discussed [2].
  “In order to save AP MLD power, the simplest way is to have only one link operating in the active mode and other links operating in the PS mode”
However, a multi-link channel access procedure for AP MLD power saving has not been discussed.
When an AP MLD is performing unscheduled power saving operation, the following problems may occur:
  1. Channel access overhead
  2. NAVSyncDelay
This submission discusses expedited link wakeup methods to improve multi-link transmission efficiency in AP MLD power saving operation.

## Slide 3: Background: Unscheduled AP MLD Power Saving
Example [2]: An AP MLD using unscheduled power saving with 2 links
  AP 1 (Link 1): Always active state
  AP 2 (Link 2): Power saving state

## Slide 4: Issue 1: Efficient multi-link access
Example: An AP MLD using unscheduled power saving with 2 links.
  The STA MLD may want to use link 2 instantly.
  Explicit link 2 wake up frame exchanges is not efficient.

## Slide 5: Issue 2: NAVSyncDelay
Example: An AP MLD using unscheduled power saving with 2 links.
  When the AP MLD wants to use link 2, AP 2 of the AP MLD should switch its power state from doze to awake.
  NAVSyncDelay should be applied to AP 2 and the frame transmission delay of AP 2 will be increased.

## Slide 6: Expedited Link Wake-up
Case 1: An AP MLD using unscheduled power saving with 2 links
  STA 1 of the STA MLD indicates ‘AP 2 wake-up request’ in its frame transmitted in link 1.
  AP 1 of the AP MLD responses to STA 1’s request.
    Acceptance or rejection of the request
  When the AP MLD accepted the STA MLD’s request, the STA 2 can perform a channel access in link 2

## Slide 7: Expedited Link Wake-up (Cont’d)
Case 2: When STA MLD is operating on NSTR link pair
  STA 1 of the STA MLD indicates ‘AP 2 wake up request’ in its frame transmitted in link 1.
  A NAV is set by the STA 2’s CTS frame transmission
  AP 1 of the AP MLD responses to STA 1’s request.
    It accepts or rejects the request
  When the AP MLD accepted the STA MLD’s request, the STA 2 can transmit PPDU. STA 1 and STA 2’s PPDU transmission is synchronized.

## Slide 8: Expedited Link Wake-up (Cont’d)
Case 3: AP 2 requests medium synchronization
  ‘AP 2 wake up request’ can be indicated by current AAR operation
  For example, STA 1 can indicate ‘AP 2 wake up request’ with AAR
  AP 1’s BA frame can indicate ‘Sync request’
  Based on the ’Sync Request’, STA 2 transmits CTS frame to AP 2

## Slide 9: Summary
In this submission, multi-link channel access procedure for unscheduled AP MLD power saving operation was discussed.
  The non-AP MLD can request AP MLD’s power saving links within one TXOP.
  The non-AP MLD can request AP MLD’s power saving links with AAR from 11be or similar indication.
With the proposed operations, multi-link channel access efficiency in unscheduled AP MLD power saving can be improved

## Slide 10: References
[1] 11-23/0480r3: UHR proposed PAR, https://mentor.ieee.org/802.11/dcn/23/11-23-0480-03-0uhr-uhr-proposed-par.pdf
[2] 11-23/0225r0: Considering Unscheduled AP Power Save, https://mentor.ieee.org/802.11/dcn/23/11-23-0225-00-0uhr-considering-unscheduled-ap-power-save.pptx