## Slide 1: Follow-up on peer-to-peer communication for UHR
Date: 09-14-2023
Authors:

## Slide 2: Abstract
In [1],[2], we highlighted some of the potential technologies for improved peer-to-peer (P2P) operation.
Extension of the Channel Usage procedure was identified for improving P2P support in UHR[3]
In this contribution, we provide some details and extensions for [3]

## Slide 3: Recap (1/2)—Advertisement of Recommended P2P Channels
An AP can announce a set of channels in its BSS that are recommended for P2P communications
  These advertised channels would be more conducive to P2P communication.
    For example, the AP can minimize the use of those channels for its infrastructure communication.
  The AP can announce/advertise the Recommended P2P Channels in its BSS by including the related information in the Beacons and Probe Response frames it transmits.
    For example, the AP can include Channel Usage elements for this advertisement
  The P2P channel recommendation can be updated over time.
Motivation for the AP: By incentivizing the P2P STAs to keep their P2P transmissions within the recommended set of channels, the AP can essentially reduce the uncontrolled P2P transmission on the channels that the AP uses for infrastructure BSS operation (for UL/DL communication, for example)
    This, in essence, can help the AP in ensuring infrastructure STAs’ QoS requirements.
Motivation for the P2P STAs: The guidance from the AP would enable the P2P STAs to embark on a cleaner channel (with less interference from the infrastructure) faster for their P2P communications by using the recommended channels
  Help faster setup of a P2P link (or P2P group)
  Help faster switch of a P2P operating channel

## Slide 4: Recap (2/2)—Advertisement of Recommended P2P Transmission Windows
Similarly, an AP can announce a set of recommended time windows that would be more conducive for P2P transmission.
  During these recommended P2P Transmission Windows, the AP can minimize infrastructure transmission
    Motivation for AP: Reduces non-infrastructure transmission outside these P2P Transmission Windows and improves the manageability of the network.
    Motivation for P2P STAs: Thus provides incentives for the P2P STAs to use the P2P transmission windows for their P2P communication and encounter less interference from the infrastructure communication
The AP can announce a series of recommended P2P Transmission Windows in the Beacon and Probe Response frames
  Existing signaling tools (e.g. TWT) can be reused for this purpose.

## Slide 5: Need for extended support (1/2)
  The P2P STAs can follow the P2P channel resource recommendation from the AP for their P2P needs.
  This helps in parking on a channel for P2P that would have less interference from the BSS maintained by that AP.
  However, in an OBSS environment, the P2P link is still likely to face interference from the OBSS network
    P2P channel recommendation from the first AP may be independent of the recommendation from the OBSS AP.
The P2P link between STA1 and STA2 follows the channel recommendation from AP1 but still suffers from interference from BSS2.

## Slide 6: Need for extended support (2/2)
  It is becoming a common scenario where two P2P STA are associated with different infrastructure APs.
  It’s challenging to maintain both the UL/DL and P2P flows in such situations
    If in the respective base-channels (i.e. APs’ channels), hard to schedule the P2P sessions. Troublesome for LL traffic.
    If trying to go off-channel, hard to find a common off-channel they are clean from both infrastructure networks.
STA1 is associated with AP1; STA2 is associated with AP2; STA1 and STA2 forms a P2P link (not TDLS).

## Slide 7: Multi-AP Coordination for channel usage enhancements (1/2)
  For efficient P2P communication, it would be good if the APs corresponding to the overlapping BSS coordinate with each other. Upon coordination--
    The APs can designate a common set of channels for P2P
      Help facilitate off-channel P2P operation
    The APs can create a common schedule for P2P
      Help facilitate base-channel P2P operation

## Slide 8: Multi-AP Coordination for channel usage enhancements (2/2)
  After negotiation, the participating APs can advertise the P2P channel resources.
    The advertisement can be either only on channel guidance or only on schedule guidance or both

## Slide 9: Summary
Tighter coordination between the infrastructure and P2P networks would be important to ensure QoS support for WLAN systems.
In this presentation, we extend the contribution [3] on channel usage to multi-AP coordination framework.
  Facilitates improved QoS for P2P communications

## Slide 10: References
[1] IEEE 802.11-22/1528r1, “Enhanced Device Connectivity with Robust QoS Support”, R. Shafin et.al., Sept 2022.
[2] IEEE 802.11-22/932r0, “Thoughts on Beyond 802.11be”, W.B. Lee et.al., July 2022.
[3] IEEE 802.11-23/294r1, “Channel Usage Enhancements for P2P in UHR”, R. Shafin et.al., May 2023.