## Slide 1: Buffer Status Report in Multi-AP
Date: 2023-08-30
Authors:
Name | Affiliations | Address | Phone | Email
Pei Zhou | TCL |  |  | zhoupei36@gmail.com
Zhanjing Bao | TCL |  |  | 

## Slide 2: Introduction
  In UHR, multi-AP coordination is considered as an important feature to increase not only throughput but also reliability
  UHR PAR [1]: Technical solutions to meet the needs of cutting edge applications should address both deployments with a single isolated BSS and deployments with multiple non-collocated BSSs in dense environments where in-band and optionally out-of-band (including via IEEE 802.3) AP coordination can be available (e.g., enterprise, residential).
  Currently, there are several multi-AP coordination schemes discussed in both 802.11be and UHR
    C-TDMA, C-OFDMA, C-SR, C-BF, J-TX, etc.
  [2] proposed a C-TDMA procedure by reusing the EHT TXS framework. The object is to enhance coordination among APs in time to improve the reliability of the network in latency, throughput and fairness
    Observation: Before TXOP sharing, the sharing AP needs to determine how much time allocate to shared AP(s).
  [3] proposed a Coordinated AP Time/Frequency Sharing procedure in 802.11be for worst case-latency improvement and throughput fairness
    SP #3: Define a mechanism for the TXOP owner AP to solicit feedback from the set of APs to learn the resource needs and the intent to participate in a coordinated AP transmission.
  Other multi-AP coordination schemes (C-SR, C-BF, J-TX, etc) may also need to know the resource needs in advance
    For example, the sharing AP may prioritize inviting the shared AP(s) with low latency traffic to perform C-SR, C-BF, J-TX, etc.
  Therefore, the precondition to perform multi-AP coordination is to obtain resource needs from shared APs.

## Slide 3: Possible methods for obtaining resource needs
Sharing AP can use the following methods to obtain Shared APs’ resource needs, and then determine how much resource should be allocated to each Shared AP (e.g., for C-TDMA and C-OFDMA) or invite which shared AP(s) to participate in coordinated transmission (e.g., for C-SR, C-BF and J-TX).
Method 1: Based on Shared AP’s resource request
  Each Shared AP indicates its required resources (e.g., time duration, BW/RU) to Sharing AP
    Shared AP can actively include its required resources in an unsolicited frame
    Shared AP can include its required resources in a frame solicited by Sharing AP
  Sharing AP allocates required resources to each Shared AP
Drawback:
  If the total amount of resources requested by Shared APs exceeds what Sharing AP can provide, Sharing AP doesn’t know how to execute the resource allocation
  An arbitrary Shared AP may request more resources than needed, which will cause fairness issue to other Shared APs
Method 2: Based on Shared AP’s Buffer Status Report (BSR)
  Shared AP reports its BSR (with potential modifications) to Sharing AP
  Sharing AP evaluate all Shared APs’ BSR and determine the resource allocation
  In our opinion, method 2 is preferred to assist Sharing AP in multi-AP coordination.

## Slide 4: Re-cap: BSR in single BSS
A non-AP STA delivers buffer status reports (BSRs) to assist its AP in allocating UL MU resources
A non-AP STA reports its buffer status to the AP with which it is associated in the QoS Control field in QoS Null and QoS Data frames and in the BSR Control subfield (if present) in QoS Null, QoS Data, and Management frames
  QoS Control field
    The buffer status reported in the QoS Control field consists of a queue size value for a given TID
    The AP PS Buffer State subfield indicates the PS buffer state at the AP for a STA.
  BSR Control field
    The buffer status reported in the BSR Control field consists of an ACI bitmap, delta TID, a high priority AC, and two queue sizes
Currently, there is no BSR exchange procedure between APs (e.g., between Sharing AP and Shared APs)

## Slide 5: Proposal(s): C-BSR in UHR multi-AP
In multi-AP coordination, if Sharing AP wants to allocate proper resource to proper Shared APs, the following enhancements may need to be made:
  Shared AP can report its “C-BSR” to Sharing AP by the following methods
    Unsolicited C-BSR
    Solicited C-BSR (by Sharing AP’s BSRP Trigger frame)
  (Shared) AP’s C-BSR (Coordination BSR) should include the following
    Multiple (or all) associated non-AP STAs’ UL buffer status
    DL buffer status for multiple (or all) associated non-AP STAs
    Both of the above
  Note: The detailed C-BSR format needs further study.

## Slide 6: Summary
We highlighted the necessities to share C-BSR between APs in multi-AP coordination
We proposed the methods to share C-BSR between APs
  Unsolicited C-BSR
  Solicited C-BSR
We proposed the potential contents that need to be included into the C-BSR
  Multiple (or all) associated non-AP STAs’ UL buffer status
  DL buffer status for multiple (or all) associated non-AP STAs

## Slide 7: References
[1] 11-23-0480-03-0uhr-uhr-proposed-par
[2] 11-23-0041-00-0uhr-considerations-on-coordinated-tdma
[3] 11-19-1582-02-00be-coordinated-ap-time-and-frequency-sharing-in-a-transmit-opportunity-in-11be