## Slide 1: CFO Impact and Pilot Design for dRU Follow up
Date: 2023-09-10
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
In [1], we compared two pilot design methods and investigated performance considering various values of residual CFO
In this contribution, we introduce an alternative pilot design method which is based on option 2 shown in [1] and offers an improved performance
In addition, we provide further simulation results and our thoughts to address comments from the last presentation

## Slide 3: Recap on Pilot Design in [1]
Option 1: define new pilot position
  For a 26-tone dRU, 26 distributed tones are allocated and then two tones among them are selected as pilot tones
  We use the 7th and 20th tones in each 26-tone dRU as the pilot tones
Option 2: maintain conventional pilot position
  For a 26-tone dRU, 24 distributed tones are allocated as data tones and then two tones among the conventional pilot tones are additionally allotted as pilot tones
  The pilot tones of x-th 26-tone rRU are used as the pilot tones for x-th 26-tone dRU

## Slide 4: Alternative Pilot Design
In [1], we showed that the performance of option 2 is worse than option 1
  Two pilots of each 26-tone dRU in option 2 are closely located resulting in less accurate residual CFO compensation
To achieve a better performance, we employ an alternative method where two pilot tones located far enough away are selected out of the conventional ones for each 26-tone dRU
  Specifically, in 20 MHz, there are 18 conventional pilot tones (pilot tone index 1 ~ 18) and each pilot tone is allocated to the n-th 26-tone dRU
    Where n is equal to mod(pilot tone index-1, 9) + 1
Pilot tone 1
…
Pilot tone 2
Pilot tone 3
Pilot tone 10
Pilot tone 11
Pilot tone 12
…
Allocated to the 1st 26-tone dRU
Allocated to the 2nd 26-tone dRU
Allocated to the 3rd 26-tone dRU

## Slide 5: Performance Comparison (1/3)
We investigate PER performance for dRU with three options as well as rRU considering various residual CFO values
Assumptions
  20 MHz UL TB PPDU with nine 26-tone dRUs / nine 26-tone rRUs
  SISO under Channel D NLoS
  1000 data bits per each STA
  MCS 0/3/5/8 with LDPC coding
  Residual CFO for each STA: [+rCFO –rCFO +rCFO –rCFO …]
    Different rCFO values are considered depending on the MCS level
  Pilot position for dRU
    Option 1: 7th and 20th tones in each 26-tone dRU
    Option 2: pilot tones of x-th 26-tone rRU for x-th 26-tone dRU
    Option 3: alternative pilot design in the previous slide
  PERs for the first 26-tone dRU and first 26-tone rRU are provided

## Slide 6: Performance Comparison (2/3)
Simulation results
  MCS 3
    When rCFO = 0 Hz, dRU provides a significant performance gain
    dRU has a wider performance gap between with and without the residual CFO
      dRU still outperforms rRU even though a certain amount of residual CFO is present
    When rCFO > 0 Hz, Option 1 and option 3 have similar performance and offer better performance than option 2
PERs for MCS 0 / 5 / 8 are shown in Appendix and the trend is similar
SNR is defined as the average signal to noise power ratio per tone
Note that in [1], SNR is defined as the average signal to noise power ratio in 20 MHz for the STA assigned to the first rRU / dRU

## Slide 7: Performance Comparison (3/3)
When there is no residual CFO, dRU achieves quite better performance than rRU, no matter what the pilot option is
  That is because dRU can obtain a significant frequency diversity gain
As the amount of the residual CFO increases, dRU performance deteriorates much faster
  That is because dRU is more vulnerable to the residual CFO
  However, its performance is still better than that of rRU
In addition, thanks to the higher transmit power for dRU, dRU performance can be further enhanced
Option 1 and option 3 have similar performance and provide better performance than option 2
  Even though we maintain the conventional pilot tones for dRU tone plan, we can achieve comparable performance

## Slide 8: Received Comments (1/3)
Performance with a randomly generated residual CFO
  Assumptions are the same except that the residual CFO for each STA is randomly generated between –rCFO and +rCFO
  The trend is similar but the gap between the cases with and without the residual CFO becomes narrower

## Slide 9: Received Comments (2/3)
Reasonable residual CFO value given SNR
  Basically, when a STA transmits a TB PPDU, we can assume that CFO is pre-compensated by using a DL PPDU which conveys the Trigger frame that solicits the TB PPDU
  Thus, the amount of the residual CFO in the TB PPDU can be affected by the condition of the channel on which the Trigger frame is transmitted (similar to the condition of the channel where TB PPDU is transmitted)
    E.g., CDF of the absolute value of the residual CFO after compensating the CFO in a DL PPDU at *18 dB (average SNR per tone) when considering the CFO of 20 ppm in 5 GHz
Average: 447 Hz
Median: 347 Hz
Maximum: 2951 Hz
Minimum: <1 Hz
*10 % PER is achieved for option 1 and option 3

## Slide 10: Received Comments (3/3)
Reasonable residual CFO value given SNR (cont.)
  It may be difficult to choose a specific residual CFO value which can be considered reasonable at a certain SNR for the simulation to show the TB PPDU performance
  Having said that the residual CFO values used in our simulation are quite similar to the average and median values
  Also, depending on the implementation, it may be possible that the STA can measure the CFO by using any preceding DL PPDUs and can minimize the amount of the residual CFO when transmitting TB PPDU
  In addition, the residual CFO values used in our simulation may be sufficient to show the performance tendency
Tone indices for each 26-tone dRU
  We are open for various design methods for a dRU tone plan and we think that it would be better to discuss a general design way for now

## Slide 11: Conclusion
We have introduced the alternative pilot design method based on the conventional pilot tones and its performance has been compared with the previous options presented in [1]
  The alternative method exhibits comparable performance
We have also provided simulation results with randomly generated residual CFO
  The trend is similar to the case where the residual CFO value is fixed
In addition, we have investigated the CDF of the residual CFO
  Depending on the implementation, the residual CFO can be minimized and the used residual CFO values may be enough to identify the tendency of the dRU performance
After evaluating various design methods for a dRU tone plan, we can further discuss details on exact tone indices

## Slide 12: References
[1] 11-23-1115-00-0uhr-cfo-impact-and-pilot-design-for-dru

## Slide 13: Appendix
Simulation results
  MCS 0
    The performance for option 1 is quite bad when rCFO = 1 KHz

## Slide 14: Appendix
Simulation results
  MCS 5
    Trend is similar

## Slide 15: Appendix
Simulation results
  MCS 8
    When rCFO = 200 Hz, it seems that all of the cases cannot achieve 10 % PER