## Slide 1: Considerations on Multi-AP Operation
Date: 2023-09-11
Authors:

## Slide 2: Abstract
In this contribution, we share some considerations on multi-AP operation, including the support of selecting multi-AP transmission schemes and the support of scheduling the multi-AP transmission.

## Slide 3: Introduction
In PAR of P802.11bn, the Ultra High Reliability (UHR) capability has been defined to improve Rate-vs-Range enchantment, reduce latency, and reduce power consumption for AP, compared to Extremely High Throughput (EHT) MAC/PHY operation.
Multi-AP operation (aka. Multi-AP coordination/transmission) has been discussed as one of the key candidate features to meet the requirement of UHR capability.

## Slide 4: Multi-AP Operation – Recap (1) [1~8]
Multi-AP operation may include several phases/procedures between OBSSs.
  Multi-AP setup phase:
    Exchanging information between multiple APs;
    Grouping multiple candidate APs, e.g., AP candidate sets,
  Multi-AP coordination phases
    Exchanging information between sharing AP and shared AP(s),
    Multi-AP selection phase: sharing AP selects shared AP(s),
    Multi-AP channel sounding phase (optional): APs perform sounding jointly/individually with STA(s).
    Multi-AP data sharing phase (optional): sharing AP shares data to shared AP Multi-AP data transmission phase:
    Using UL/DL multi-AP transmission schemes, such as: coordinated spatial reuse (CSR), coordinated OFDMA/TDMA, coordinated beamforming (CBF), joint transmission/reception (JT/JR), etc.

## Slide 5: Multi-AP Operation – Recap (2) [1~8]
Multi-AP operation procedures may be performed for long-term or short-term operations:
  Long-term operation: e.g., one or more beacon interval(s) level
  Short-term operation: e.g., one or more transmission opportunity (TXOP) level
The multi-AP transmission may be carried in a multi-AP data transmission phase, preceded by one or more multi-AP coordination phases, including a multi-AP selection phase.
Some multi-AP operation procedures may repeat optionally for follow-up or new transmissions.

## Slide 6: Multi-AP Transmission Scheme Selection
The multi-AP selection phase may include frame exchanges to allow a sharing AP (AP1) to determine whether a candidate shared AP (AP2) may participate in a multi-AP transmission.
  For example, AP1 designates AP2 for the multi-AP transmission and determines the specific multi-AP transmission scheme based on the capabilities of AP2 for supporting multi-AP transmission schemes.
However, the existing procedure relies on the sharing AP determining a multi-AP transmission scheme without consideration of whether the selected scheme can be adequately performed by the shared AP.
  The limitation may not be optimal for the multi-AP transmission, and it results in a waste of resources.

## Slide 7: Preferred Multi-AP Transmission Scheme
The shared AP (AP2) provides the sharing AP (AP1) a preferred multi-AP transmission scheme.
The sharing AP may consider the preferred multi-AP transmission scheme when selecting a multi-AP transmission scheme by the sharing AP.
The sharing AP announces to the shared AP the multi-AP transmission scheme.

## Slide 8: Multi-AP Transmission Scheduling
A multi-AP selection phase may be performed before each multi-AP data transmission.
A sharing AP (AP1) may perform AP (re)selection to select one or more suitable shared APs (AP2) within an AP candidate set to participate in a multi-AP transmission.
After a sharing AP selects a shared AP for a multi-AP transmission, the shared AP may become unavailable before the beginning of the multi-AP data transmission. (e.g., AP power saving)
The shared AP may not be able to participate in the multi-AP transmission and resources allocated to the shared AP may be lost.

## Slide 9: Shared AP Unavailability Window
The shared AP (AP2) signals to the sharing AP (AP1) an unavailability window, during which the shared AP is unavailable to participate in a multi-AP transmission.
The sharing AP schedules the multi-AP transmission to avoid the unavailability window of shared AP.

## Slide 10: Multi-AP Transmission Window
The sharing AP (AP1) signals to the shared AP (AP2) a multi-AP transmission window.
The shared AP responds the sharing AP a decision of participating or not in the multi-AP transmission window.

## Slide 11: Summary
In this contribution, we shared some thoughts on multi-AP coordination. We proposed the method of selecting multi-AP transmission schemes and the methods of scheduling the multi-AP transmission.

## Slide 12: References
[1] 11-18-1982-01-0eht-consideration-on-multi-ap-coordination-for-eht.pptx
[2] 11-19-0448-01-0eht-multi-ap-transmission-procedure.pptx
[3] 11-19-1102-00-00be-a-unified-transmission-procedure-for-multi-ap-coordination.pptx
[4] 11-19-1129-02-00be-consideration-on-multi-ap-coordination.pptx
[5] 11-19-1143-03-00be-efficient-operation-for-multi-ap-coordination.pptx
[6] 11-19-1895-02-00be-setup-for-multi-ap-coordination.pptx
[7] 11-20-0596-01-00be-ap-candidate-set-follow-up.pptx
[8] 11-20-0617-03-00be-multi-ap-operation-basic-definition.pptx
[9] 11-22-1512-00-0uhr-multi-ap-coordination-for-uhr.pptx
[10] 11-22-1515-00-0uhr-a-candidate-feature-multi-ap.pptx
[11] 11-22-1530-01-0uhr-multi-ap-coordination-for-next-generation-wi-fi.pptx
[12] 11-22-1899-00-0uhr-multi-ap-operation-for-low-latency-traffic-delivery-follow-up.pptx
[13] 11-23-0226-02-0uhr-coordination-of-r-twt-for-multi-ap-deployment.pptx
[14] 11-23-0293-00-0uhr-follow-up-on-twt-based-multi-ap-coordination.pptx
[15] 11-23-0297-00-0uhr-rtwt-for-multi-ap.pptx
[16] 11-23-0860-00-0uhr-further-thoughts-on-coordinated-twt.pptx