## Slide 1: Coordinated Transmission ID
Date: 2023-09-03
Authors:
Name | Affiliations | Address | Phone | email
Yanchun LI | Huawei | Huawei Industrial Base, Bantian, Longgang District, Shenzhen 518129 P.R. China. | (+86)13127744874 | liyanchun@huawei.com
Yan Zeng | Huawei |  |  | 
Xiang Wang | Huawei |  |  | 

## Slide 2: Introduction
BSS color has been introduced to IEEE 802.11 in 11ax.
BSS color allows the PHY to infer the relevant BSS/source/destination of the PPDU
  If a home AP is not involved in any current transmission, the home AP or STA is able to reuse the channel.
  BSS color collision detection allows each of the nearby APs to have an unique BSS color locally.
However, coordinated transmission such as JT, Coordinated BF, Coordinated OFDMA with overlapped 20MHz channel(s), etc, involves aligned transmission from multiple APs. It causes problems over the air. This contribution discussed these problems.

## Slide 3: Recap BSS color in 802.11ax
BSS color allows power saving at mobile STAs.
  Ignore irrelevant PPDU over air.
BSS color allows the efficient spatial reuse of spectrum.
AP1:
AP2:
STA1
STA2
AP1:
AP2:
Preamble (BSS color =A)
Payload
PPDU
(BSS color =B)
STA2 can have concurrent transmission if PD level is below OBSS_PD_threshold
backoff

## Slide 4: Recap multi-AP transmissions
Considering that AP1 and AP2 serve STA1 and STA2, they transmit their preambles simultaneously on overlapping 20MHz channel(s).
STA2
AP1:
AP2:
STA1
Case 1: Joint transmission
Case 2: Coordinated BF
STA2
AP1:
AP2:
STA1
e.g.
With nulling to suppress inter-BSS interference

## Slide 5: When BSS coloring meets multi-AP transmissions
STA2
BSS coloring in multi-AP transmission which allows spatial reuse can be beneficial for throughput, e.g.
AP1:
AP2:
Preamble from AP1 and AP2
Payload
AP3:
STA1
STA3
(2) STA2 hears Preamble from AP1 and AP2. It understands AP3 is idle and initiate EDCA uplink transmission to AP3.
(1) AP1 and AP2 have coordinated BF/joint transmission etc. to STA1/2 with PPDU:

## Slide 6: The issue when BSS coloring meets multi-AP transmissions
For coordinated transmissions with multi-AP concurrent Tx:
  Case A: Each AP uses different BSS color leads to preamble collision.
AP1:
AP2:
(adjacent to AP1)
Payload
Payload
STA2
AP1:
AP2:
STA1
U-SIG
Preamble
NAV,
BSS color =B, etc.
NAV,
BSS color =A, etc.
Preamble
L-LTF
L-LTF
① L-LTFs are aligned, the estimated channel will be h1+h2 due to pilot contamination effect.
② However, the channel which AP1’s U-SIG signal pass through is not h1+h2 but h1, with superposed interference from AP2 (coded waveform with BSS color=B). The mismatch will dramatically increase PER for U-SIG.
These preambles have different waveform in U-SIG (due to BSS color difference).
Assume AP1 uses BSS color A
AP2 uses BSS color B

## Slide 7: The issue when BSS coloring meets coordinated multi-AP transmissions (conti.)
  Case B: AP can also use BSS color =0, besides each AP’s unique BSS color. However, it will disallow spatial reuse.
It is important to allow successful transmission of BSS color and also indicate relevant BSS information clearly.
Preamble (NAV,
BSS color =0)
Payload
CCA busy

## Slide 8: Summary
We discussed the issue of BSS coloring for coordinated transmissions.
A coloring scheme without ambiguity can allow coordinated multi-AP transmission while also allow spatial reuses.

## Slide 9: Straw Poll
Do you agree that in coordinated multi-AP transmission, BSS color should provide clear indication of the APs involving this transmission?
  Y
  N
  A

## Slide 10: References
[1] https://mentor.ieee.org/802.11/dcn/22/11-22-1394-01-0uhr-virtual-bss-and-multi-ap-transmissions.pptx