## Slide 1: Discuss Requirements of MLD
Date: 2023-09-05
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | po-kai.huang@intel.com
Danny Alexander |  |  |  | 
Ido Ouzieli |  |  |  | 
Johannes Berg |  |  |  | 
Ilan Peer |  |  |  | 
Daniel F Bravo |  |  |  | 
Robert Stacey |  |  |  | 
Notes: September 2012

## Slide 2: Background
There is a debate on whether we should mandate MLD for 11bi
  A question “Should CPE and BPE devices be MLD-compliant?” is included in [1]
The debate starts to delay the progress of 11bi on spec texts writing
We discuss this issue in this presentation

## Slide 3: Original Motivation for the discussion
Due to the change of STA MAC address while associated, a non-MLD device will need to change the encryption of data frame when the MAC address is changed
However, change of data frame encryption may not be viable for certain architectures with external key-holder [2]
As a result, it is required to have a mechanism similar to the one introduced in 11be that uses MLD MAC address in AAD for the encryption of data frame
The observation then leads to discussion whether we should just mandate MLD without defining another similar mechanism or define another mechanism similar to MLD
The debate then propagates to most of the features in 11bi

## Slide 4: Discuss implication of 11bi features
Generally, there are two groups of 11bi features
  Group 1: features that only need software change
    Minimize Probe Request element
    802.1X authentication using authentication frame
    Password identifier privacy
    PMKID privacy
    Key negotiation in Authentication to protect (Re)Association Request/Response
    Encrypt (Re)Association Request/Response
    Include DS MAC address in encrypted (Re)Association Request
    Introduce protected version of current unencrypted management frame
    Protected action frame to request capabilities and operation parameters
  Group 2: features that require hardware change
    Change of STA MAC address/SN/PN/AID while associated
    Many Other parameters change while associated and BPN features
The question in hand seems to be only related to the features in group 2. Further, implementation of group 1 features does not mean implementation of group 2 features is required
  Due to the possibility that hardware support depends on hardware refresh cycle
As a result, we propose that we allow MLD and non-MLD for group 1 features and focus the discussion on the following revised question
  Shall 11bi devices that support STA MAC address change while associated support MLD?

## Slide 5: Illustration for MLD with STA MAC address change
Initial connection for a non-AP MLD
  Authentication frame exchange with STA MAC address 1, MLD MAC address 1
  Derive PTKSA using MLD MAC address 1
  Encrypt association request with DS MAC address 1 and encrypt association response
  AAD Swap based on MLD MAC address 1
  Change STA MAC address from 1 to X (similarly for other links if exists)
  …
  Disassociation
Follow up connection for a non-AP MLD
  Authentication frame exchange with STA MAC address 2, MLD MAC address 2
  Derive PTKSA using MLD MAC address 2
  Encrypt (re)association request with DS MAC address 1 and encrypt (re)association response
  AAD Swap based on MLD MAC address 2
  Change STA MAC address from 2 to X (similarly for other links if exists)
  …
  Disassociation
11bi STA MAC address change while associated can be an independent feature [3]

## Slide 6: Illustration for non-MLD with STA MAC address change
Initial connection for a non-AP STA
  Authentication frame exchange with STA MAC address 1
  Derive PTKSA using STA MAC address 1
  Encrypt association request with DS MAC address 1 and encrypt association response
  AAD Swap based on ???
  Change STA MAC address from 1 to X (questions on PTKSA still based on STA MAC address 1?)
  …
  Disassociation
Follow up connection for a non-AP STA
  Authentication frame exchange with STA MAC address 2
  Derive PTKSA using STA MAC address 2
  Encrypt (re)association request with DS MAC address 1 and encrypt (re)association response
  AAD Swap based on ???
  Change STA MAC address from 2 to X (questions on PTKSA still based on STA MAC address 2?)
  …
  Disassociation
11bi STA MAC address change while associated needs to solve the questions above

## Slide 7: Discuss two options for non-MLD
Two options are on the table for AAD swap:
  Option 1: Simply mandate support of MLD for 11bi device that support STA MAC address change while associated
  Option 2: Develop some mechanisms to solve the questions
Discussion on option 1:
  Simplify the hardware support on AP since MLD support is mandatory in 11be and increase the chance for wide support of the feature
  MLD support for client is there in 11be based on discussion with chip vendor even for low cost client
  Simplify the spec work and no need to duplicate texts of similar features
  Client can setup only one link using MLD and no need to implement most of the optional features
  Hardware features usually take longer to be adopted and by that time, 11be is likely already the mainstream when the hardware support is available, which means that option 2 may not be useful anymore.
  Before hardware support is there, group 1 features can be rolled out first to start provide privacy benefits
Discussion on option 2:
  Can change STA MAC address while associated without implementing MLD
  Need to implement MLD like AAD swap, which requires additional hardware change for non-MLD
Option 1 seems to be a better direction for 11bi

## Slide 8: Conclusion
We think the question “Should CPE and BPE devices be MLD-compliant?” included in [1] should be changed to “Shall 11bi devices that support STA MAC address change while associated support MLD?”
We propose the following:
  Software related features can be done for both MLD and non-MLD
  Mandate MLD support if 11bi devices support STA MAC address change while associated

## Slide 9: Straw Poll
Do you support the following:
  11bi devices that support any of the following features and do not support STA MAC address change and related features while associated can be MLD or non-MLD
    Minimize Probe Request element
    802.1X authentication using authentication frame
    Password identifier privacy
    PMKID privacy
    Key negotiation in Authentication to protect (Re)Association Request/Response
    Encrypt (Re)Association Request/Response
    Include DS MAC address in encrypted (Re)Association Request
    Introduce protected version of current unencrypted management frame
    Protected action frame to request capabilities and operation parameters

## Slide 10: Straw Poll
Do you support the following:
  11bi devices that support STA MAC address change while associated shall support MLD

## Slide 11: Reference
[1] 11-23/892r2 Requirements and Issues Tracking
[2] 11-20/1545r1 MLD security considerations
[3] 11-23/873r2 Client Frame Tracking Countermeasures