## Slide 1: Proposals for PMKID Requirement
Date: 2023-09-05
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | po-kai.huang@intel.com
Ido Ouzieli |  |  |  | 
Johannes Berg |  |  |  | 
Ilan Peer |  |  |  | 
Robert Stacey |  |  |  | 
Notes: September 2012

## Slide 2: Background
11bi has the following requirement related to PMKID[1]
11bi shall define a mechanism to prevent an eavesdropper distinguishing whether reassociation exchanges between CPE Clients and CPE APs use identical PMK or distinct PMK
There are proposals [2,3] in the past for PMKID privacy
  The fundamental idea is to derive new PMKID to be used next time after each successful PTKSA establishment
  There are questions in the past about how to deal with FT
We propose to follow the principles in [2,3] and fill the details for FT

## Slide 3: Proposal
After each PTKSA establishment, derive PMKID by following the existing formulas and using KDK [2]
  For example, for AKM 5 and 6, do the following change
  PMKID = Truncate-128(HMAC-SHA-256(PMKKDK, “PMK Name” || AA || SPA))
For FT, after each PTKSA establishment, derive new PMKR0Name by following above principles
PMKR0Name = Truncate-128(Hash(“FT-R0N” || PMK-R0Name-Salt))
Change to PMKR0Name = Truncate-128(HMAC(KDK,“FT-R0N”)) ,
where HMAC is the same as the HMAC to derive PMKID under FT for each AKM see 12.7.1.6.3 (PMK-R0)
No change for PMKR1Name derivation
PMKR1Name = Truncate-128(Hash(“FT-R1N” || PMKR0Name || R1KH-ID || S1KH-ID))

## Slide 4: Spec texts proposal
General descriptions on the features
Update formulas in corresponding places
PMKSA will consist of latest derived PMKID
PMK-R0 security association will consist of latest derived PMKR0Name
Update FT to say R1KH to communicate PMKR0Name with R0KH (in 13.2.2 (Authenticator key holders))
  Target FTR uses existing procedure to derive PMKR1Name from indicated PMKR0Name to find PMK-R1, if can not identify PMK-R1, contact R0KH like today to retrieve PMK-R1 (see 13.8.1 (Overview))

## Slide 5: Other considerations
PMKID sharing among APs
  No definition in the spec today about PMKID sharing among APs anyway
Indicated PMKID does not lead to key establishment for whatever reasons
  Simply go to full authentication like today
Keep the derived PMKID/PMKR0Name for how long
  View it as context for PMKSA/PMK-R0 SA and follow existing rules
Allow PMKID to be included in authentication frame
  Since key establishment is happening in authentication frame exchange to encrypt (re)association request/response.

## Slide 6: Conclusion
This presentation intends to finish the proposals of enhancing PMKID privacy in [2]
The fundamental principle is to derive PMKID/PMKR0Name using KDK and following existing formula of HMAC and input string

## Slide 7: Reference
[1] 11-23/892r2 Requirements and Issues Tracking
[2] 11-23/1697r0 MAC Privacy and PMKSA Caching
[3] 11-23/0168r0 Varying PMKID and SAE password ID