## Slide 1: Evaluation for the Relay Transmission
Date: 2023-09-10
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St San Diego, CA 92131 |  | sanggook.kim@lge.com
September. 2023

## Slide 2: Introduction
In [1], we introduced the relay operation in UHR to provide improved SNR and range extension.
  We considered the various points to apply the relay operation in UHR and addressed the scenario for relay transmission.
According to [2], better end-to-end QoS is achievable through relay operation.
  A relay transmission can provide the end-to-end throughput gain.
In this contribution, we evaluate the performance of relay transmission in aspect of latency.

## Slide 3: Link analysis
Relay transmission
  The MCS of PPDU1 and PPDU2 is determined by reflecting the SNR of the transport channel
  SNR = Tx power – PL – Noise floor
    Tx power : 20dBm for AP, 20dBm or 15dBm for relay STA
    Noise floor = -174+Noise_Figure+10*log10(BW)
      Noise_Figure = 7dB
    PL : 11ax pathloss model for residential scenario [3]
  In some analysis, 11dB obstacle/Wall is assumed for AP to end-STA transmission.
AP
Relay STA
End –STA
(i.e. Non-AP STA)
PPDU1
PPDU2
Obstacle (i.e. Wall)

## Slide 4: Relay operation
In a BSS, end-STA has a poor SNR because it is located around the boundary of BSS or due to obstacles located between AP and end-STA.
  The End-STA which is located boundary has following SNR. Please refer the appendix
    w/o obstacle ( 70 ~ 100 m)
      20MHz : 7~13 dB, 80MHz : 2 ~ 7 dB
    w/ one obstacle ( 50 ~ 70m )
      20MHz : 2 ~ 7dB, 80MHz : - 4 ~ 1dB
  Due to the impact of obstacle, we can confirm the range of transmission is reduced in aspect of SNR.
AP
Relay STA
End –STA
(i.e. Non-AP STA)
Obstacle (i.e. Wall)

## Slide 5: Required SNR per MCS
The below table indicates the required SNR to achieve the 10% PER per MCS in TGnD.
MCS | Required SNR for 20MHz [dB] | Required SNR for 80MHz [dB]
0 | 6.8 | 4.8
1 | 9.5 | 7.4
2 | 14.3 | 12.3
3 | 16.5 | 14.5
4 | 19.8 | 17.8
5 | 23 | 20.6
6 | 25.5 | 22.8
7 | 27.5 | 25.5
8 | 29.5 | 27.8
9 | 32.5 | 30.7
10 | 35.3 | 32.8
11 | 38.6 | 35.9
Note: The PER was measured by applying a 3088-byte data size.

## Slide 6: Procedure for relay transmission
Basic frame exchange including between AP and non-AP STA(s)
Frame exchange for relay transmission among AP, Relay STA, and non-AP STA(s).

## Slide 7: Analysis of latency
Parameters
The assumption is that the end-non-AP STA may be located at a distance supported by MCS0 for direct transmission. And, Relay STA is located in the middle between AP and end-STA.
Data Size | 3088 byte (considering the 2MPDU in A-MPDU with MAC overhead) [4]
Fc | 5Ghz
BW | 20MHz/ 80MHz
Duration of Block ACK | 68 us [4]
SIFS | 16 us
Duration of Preamble | 56.8us
PPDU format | 11be MU-PPDU for SU transmission
Nss | 1
GI | 1.6 us
LTF | 4x EHT LTF

## Slide 8: Analysis of latency
Case 1 : Relay STA has the same TX power as AP
  Case 1-1 : No obstacle
  Case 1-2 : One obstacle
 | AP to non-AP STA |  | AP to relay STA / relay STA to non-AP STA | 
BW | 20MHz | 80MHz | 20MHz | 80MHz
GI | 1.6 us | 1.6 us | 1.6 us | 1.6 us
MCS (SNR) | MCS0 (8) | MCS0 (6) | MCS3(18) | MCS3(16)
Total time for transmission | 3136.8 us | 820.2 us | 1724.4 us ( 45% gain ) | 626.4 us ( 23% gain)
 | AP to non-AP STA |  | AP to relay STA / relay STA to non-AP STA | 
BW | 20MHz | 80MHz | 20MHz | 80MHz
GI | 1.6 us | 1.6 us | 1.6 us | 1.6 us
MCS (SNR) | MCS0 (8) | MCS0 (6) | MCS7 (29) | MCS8 (28)
Total time for transmission | 3136.8 us | 820.2 us | 885.6 us (72 % gain) | 396 us (52%)
Note: in each case, the distance of non-AP STA is different. we assumed that non-AP STA exists in a location with an SNR that supported by the MCS0

## Slide 9: Analysis of latency
Case 2 : Relay STA has a 15dBm as a TX power
  Case 1-1 : No obstacle
  Case 1-2 : One obstacle
 | AP to non-AP STA |  | AP to relay STA / relay STA to non-AP STA | 
BW | 20MHz | 80MHz | 20MHz | 80MHz
GI | 1.6 us | 1.6 us | 1.6 us | 1.6 us
MCS (SNR) | MCS0 (8) | MCS0 (6) | MCS3(18)/ MCS2(14) | MCS3(16)/ MCS1(11)
Total time for transmission | 3136.8 us | 820.2 us | 2010.6 us ( 42% gain) | 813.6 us (1% gain)
 | AP to non-AP STA |  | AP to relay STA / relay STA to non-AP STA | 
BW | 20MHz | 80MHz | 20MHz | 80MHz
GI | 1.6 us | 1.6 us | 1.6 us | 1.6 us
MCS(SNR) | MCS0 (8) | MCS0 (6) | MCS7(29)/MCS5(24) | MCS8(28)/MCS6(23)
Total time for transmission | 3136.8 us | 820.2 us | 957.6 us (69% gain) | 410.4 us (50% gain)
Note: in each case, the distance of non-AP STA is different. we assumed that non-AP STA exists in a location with an SNR that supported by the MCS0

## Slide 10: Summary
We investigate the performance of relay operation.
  In a poor SNR environment, Relay can clearly improve the end-to-end QoS as show in previous slides.
  In addition, even though obstacle is not considered between AP and non-AP STA, we can improve the effective SNR of end-non-AP STA by using the relay STA.
  Thus, Relay operation may require additional procedures such as end-to-end ACK/BA, but overall transmission time can be reduced by improving SNR and throughput also can be improved.

## Slide 11: Reference
[1] 11-23-0042-00-0uhr-Thought for Range Extension in UHR
[2] 11-22-1908-01-0uhr-uhr-rate-vs-range-enhancement-with-relay
[3] 11-14-0980-16-00ax-simulation-scenarios
[4] 11-14-0571-12-00ax-evaluation-methodology

## Slide 12: Appendix 1
SNR per distance according to different TX power

## Slide 13: Appendix 2
SNR per distance with one obstacle