## Slide 1: Summary of AMP SG
Date: 2023-09-11
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Doc.: IEEE 802.11-23/1529r0
September 2023

## Slide 2: Abstract
  The aim of this presentation is to provide a comprehensive overview of the progress of AMP SG, covering below aspects
      Requirements
      Deployment topologies
      Operation modes
      Coexistence
Doc.: IEEE 802.11-23/1529r0

## Slide 3
Use Cases
    Use cases have been proposed in [1]
      UC1 Smart manufacturing: inventory, asset tracking/positioning, and environment/production line sensing and monitoring
      UC2 Data Center: environmental monitoring, facility monitoring and asset management
      UC3 Smart home: asset management, home environment monitoring and home security.
      UC4 Logistics and warehouse: goods tracking and inventory check
      UC5 Smart agriculture: monitoring of soil moisture, soil fertility, temperature, wind speed, plant growth etc., and controlling of the agricultural facilities
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-23/1529r0
September 2023
Categories | Sensor | Positioning/ranging | Identification
UCs | UC#1、UC#2、UC#3、UC#4、UC#5、UC#7、UC#8 | UC#1、UC#3、UC#4、UC#6、UC#8 | UC#1、UC#2、UC#3、UC#4、UC#5、UC#8
      UC6 Indoor positioning: positioning in giant shopping mall, factories, warehouses, etc.
      UC7 Smart Power Grid: sensing of sound, heat, pressure, etc., smart meter to achieve awareness of device/equipment status
      UC8 Fresh Food supply chain: Route the RTI, sense temperature etc.
    Use case categories

## Slide 4
Requirements [2]-[4]
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-23/1529r0
September 2023
 | Coverage (dBm) | Maximum payload size (bit) | Peak device power consumption (mWatts) | Device density (per m2) | Horizontal Positioning accuracy (m) | Peak data rate (Kbps) | Others
UC1: Smart Manufacturing | Type1: -30 Type2: -82 | 256 | 1 | Baseline: 1.5 Optional: TBD | 3 | 51.2 kbps | 
UC2: Data Centre | Type1: -30 Type2: -82 | 256 | 1 | 3 | 1-3 | 51.2 kbps | 
UC3: Smart Home | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC4: Logistics and Warehouse | Type1: -30 Type2: -82 | 256 | 1 | Baseline: 1.5 Optional: TBD | 3 | 51.2 kbps | 
UC5: Smart Agriculture | Type1: -30 Type2: -82 | 256 | 1 | 1 | 10 | 51.2 kbps | 
UC6: Indoor Positioning | Type1: -30 Type2: -82 | 256 | 1 | 0.25 | 1-3 | 51.2 kbps | 
UC7: Smart Power Grid | Type1: -30 Type2: -82 | 256 | 1 | 10-2 | 10 | 51.2 kbps | 
UC8: Fresh Food Supply Chain | Type1: -30 Type2: -82 | 256 | 1 | Baseline: 1.5 Optional: TBD | 3 | 51.2 kbps | 
Note 1: Coverage is calculated based on AWGN Channel Note 2: Type 1: RF powered AMP device; Type 2: non-RF powered AMP device, e.g., thermal, solar, etc. Note 3: Others include requirements only applicable to a subset of use cases Note 4: Some use cases, e.g., UC4, may need higher device density in certain scenarios Note 5: The proposed peak data rate is only the minimum peak data rate, higher peak data rate can be considered, .e.g., 250kbps, 1Mbps. |  |  |  |  |  |  | 

## Slide 5
Traffic Characteristics
  AMP communication has the following traffic characteristics:
      Very small payload such as ID or sensor data, typically ranging from 96~256 bits
      Extremely low duty cycle for most of the typical use cases
          The traffic interval typically ranges from tens of minutes (e.g. 15min) to several hours or even days
      High frequency traffic (e.g. in some use cases such as logistics) is normally isolated and constrained within a specific region, e.g., factory, warehouse, etc., and AMP traffic will be the dominant service traffic in such isolated area.
      Extremely low channel occupation as analysed in [5] and aggregated channel occupancy percentage is less than 0.5%.
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-23/1529r0
September 2023

## Slide 6
Device Constraints [6]
  Limited power
      Very low power density of Ambient powers, ranges from x uW to x mW
      Limited energy storage
        Small capacitor for RF energy harvester (nJ-uJ)
        Actual devices are usually less efficient and energy consumption of 30 nJ is reasonable
  Low complexity
      Low-complexity frequency generation needs to be supported
        It is proposed to support calibrated clock accuracy of 40 ppm
        To reduce the power consumption and the complexity, it is expected to support AMP STA that has an oscillator with an accuracy of 1000 ppm
        Even lower accuracy clock can be used for idle time
      Low complexity transceiver
        WUR-like receiver
        Ultra-low complexity transmitter
      Limited memory and limited power budget for the memory
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-23/1529r0
September 2023
Notes: 802.11-23/1140r0

## Slide 7
Topology 1: Direct AMP communication
  The AMP STA communicates directly with the AP [7]
  RF power transfer can be provided by the AP
      Not necessarily if other ambient power is used
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-23/ 1529r0
September 2023
AMP DL
AMP UL
RF power transfer (Optionally)
AP
AMP STA

## Slide 8
Topology 2: Direct AMP communication with assisting Node
  The AMP STA communicates directly with the AP [7]-[8]
    Using AMP new interface or legacy interface, e.g., 802.11b/n, etc.
  An assisting node can:
    Provide RF power for the AMP STA
      The power RF power transfer link can be at same or different frequency with the communication link
    Send wake-up signal to the AMP STA
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-23/1529r0
September 2023
AMP DL
AMP UL
RF power transfer/Wake-up etc.
AP
AMP STA
Assisting Node

## Slide 9
Topology 3: Direct AMP communication with relay Node
  A relay node communicates directly with AMP STA and then forwards the data to the AP [8]
  An AMP interface or legacy interface can be used between the relay node and the AMP STA
      The relay node can provide RF power for the AMP STA
      The power RF power transfer link can be at same or different frequency with the communication link
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-23/1529r0
September 2023
DL
UL
RF power transfer/Wake-up etc.
AP
AMP STA
Relay Node
AMP DL
AMP UL

## Slide 10
Operation Mode @ Sub-1 GHz
  Both DL and UL communication in sub-1 GHz:
    DL air-interface: new air-interface with WUR-like design (i.e. MC-OOK) with scaling, e.g., SCS 312.5kHz  31.25kHz, OFDM symbol duration 4us  40us, etc.
    UL air-interface: new air-interface with OOK/FSK/PSK
    RF power transfer (when RF power is used)
      Fixed AP or mobile AP, e.g., cell phone, as RF energy source
      Same S1G band as communication link
      Assisted Node can be optionally deployed for additional power source
Yinan Qi (OPPO)
Slide 10
Doc.: IEEE 802.11-23/1529r0
September 2023

## Slide 11
Operation Modes @2.4GHz
  Two modes of operation@2.4GHz have been discussed.
  Mode 1: Both DL and UL communication in 2.4GHz: e.g. WUR(DL)+DSSS(UL) [7]
    DL air-interface: Reuse WUR design as much as possible
    UL air-interface: DSSS for backward compatibility
      E.g., DPBSK, 1Mbps
    RF power transfer in other frequency band(e.g. Sub-1 GHz) or Energy harvesting can be up to implementation (if other ambient power is used)
  Mode 2: AMP STA compatible to existing WiFi network [8]
    The AMP STA is able to communicate with the AP with existing technology e.g. 802.11b/n.
      AMP client STA can use a power optimized transceiver and operates in low duty cycle to communicate with existing AP.
      Adding DL wake-up receiver (similar to 11ba) can further reduce the power consumption and reduce the DL response latency.
Yinan Qi (OPPO)
Slide 11
Doc.: IEEE 802.11-23/1529r0
September 2023

## Slide 12
Benefits of AMP operation@2.4GHz
  A unified frequency band all over the world is beneficial to reduce the cost of AMP device via leveraging of market scale effect.
  It is also beneficial to support AMP application that may need to operate across different countries and regions.
    E.g. international logistics, supply chain management, personal belongings tracking etc.
  For both Mode 1 and Mode 2, it is possible to reuse the hardware of the existing AP since no new PHY waveform is introduced.
  In addition, it is possible to support AMP service by leveraging usage of the existing WiFi infrastructures in Mode 2.
Yinan Qi (OPPO)
Slide 12
Doc.: IEEE 802.11-23/1529r0
September 2023

## Slide 13
Coexistence (1)
  Comparing to other technologies, 802.11 AMP technology can better co-exist with existing .11 devices
    It is an obvious trend to develop AMP technology in different standard organizations.
    Some Ambient IoT tehcnologies@2.4GHz have already been developed to fulfill the urgent market need.
    Developing AMP technologies with 802.11 that can well coexisted with existing 802.11 devices greatly benefit the whole 802.11 ecosystem
  AMP AP can provide protection for AMP client transmission and coexists well with existing .11 devices
    E.g. legacy preamble, TXOP sharing with client, etc.
    Flexibly scheduling of AMP traffic based on the channel condition in a controllable manner
Yinan Qi (OPPO)
Slide 13
Doc.: IEEE 802.11-23/1529r0
September 2023

## Slide 14
Coexistence (2)
  AMP client has a much smaller interference footprint comparing to typical 802.11 and other technology device operated in 2.4GHz band
    Transmission time and power is highly constrained by harvested energy.
      The harvested power from wireless power transfer is likely in the order of several uWs or tens of uW
      Even at the very low transmission power of -25dBm, the active Tx consumes power in the order of several mW
      Due to the energy limitation, AMP client has to operate at very low duty cycle (e.g., <1%)
      Low transmission power also limit the effective interference range
    Leverage waveform from existing technology like MC-OOK, DSSS, etc.
Yinan Qi (OPPO)
Slide 14
Doc.: IEEE 802.11-23/1529r0
September 2023

## Slide 15
Summary
  Progress of SG has been provided covering requirements, topology, operation mode and coexistence.
  Work of SG has completed and TG should be setup to further study and standardization.
Yinan Qi (OPPO)
Slide 15
Doc.: IEEE 802.11-23/1529r0
September 2023

## Slide 16: Reference
IEEE 802.11-23/0436r8, Technical Report on support of AMP IoT devices in WLAN
IEEE 802.11-23/1005r0, Discussion on Requirements for AMP Use Cases
IEEE 802.11-23/1063r0, Further Discussion on Requirements for AMP Use Cases
IEEE 802.11-23/1073r0, Device Density in Logistics
IEEE 802.11-23/1354r0, AMP Device Channel Occupancy Analysis
IEEE 802.11-23/1140r0, Considerations for AMP Devices
IEEE 802.11-23/1190r4, Further Discussion on AMP PAR
IEEE 802.11-23/1195r0, Thoughts on AMP IOT and PAR
Doc.: IEEE 802.11-23/1529r0
September 2023