## Slide 1: TG bh Using the Status field for “Not Recognized” “No Agreement” and “Duplicate IRM” CIDs 7, 21, 114, 224, 135, 257
Date: 2023 Sept
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise, FL |  | gsmith@srtrl.com

## Slide 2: Intro
Comments have been made on D1.0 that raise concerns with:
What does a STA or AP do if “not recognized”
What if the IRM and Device ID do not agree? CIDs 135, 224, 257
  AP thinks that the IRM and the Device ID are not identifying the same STA.
What if STA gives a Duplicate IRM? CIDs 7, 21, 114
  STA provides a new IRM that is already in the APs stored list.
The TG has agreed to include a Status field in both the Device ID and the IRM IEs.
This presentation looks at using the Status field to address these concerns and to present options for way ahead.

## Slide 3: Recap - 4w HS
When a STA associates using 4w HS
Device ID
  STA sends Device ID in msg 2
  AP sends Status field in msg 3
IRM
  AP sends status field in msg 3
  STA sends new IRM in msg 4
TA = IRM
STA
AP
Msg 1
Msg 2
Device ID
Msg 3
Device ID Status, IRM Status
Msg 4
New IRM

## Slide 4: “Not recognized” – Device ID
TA = RCM
STA
AP
Msg 1
Msg 2
Device ID
Msg 3
Device ID KDE,
Msg 4
“Not Recognized” AND new device ID
Proposal is that AP treats STA as a new entry and provides a new device ID

## Slide 5: “Not recognized” - IRM
TA = IRM
STA
AP
Msg 1
Msg 2
Msg 3
IRM KDE,
Msg 4
“Not Recognized”
Proposal is that AP treats STA as a new entry.
New IRM

## Slide 6: IRM OK, Device ID not recognized
TA = IRM
STA
AP
Msg 1
Msg 2
Device ID
Msg 3
Device ID KDE,
Msg 4
“Not Recognized” AND new device ID
Both AP and STA are clear as to what happened
AP had IRM in store, but not the device ID.
IRM KDE “recognized”
IRM KDE “new IRM”

## Slide 7: Mismatch- What happens?
STA is using an IRM to associate
STA sends a Device ID in msg 2,
AP has both the IRM and the device ID in store, BUT FOR DIFFERENT STAs – “MISMATCH”
What has happened? STA or AP error? Can it happen?
AP has to have both a valid IRM and a valid Device ID stored, but not for same STA
Proposal #1
Send status code “not recognized” in BOTH KDEs
AP provides new device ID (msg 3)
STA provides new IRM (msg 4)
STA and AP know what happened, and simply start again.
Same instructions as per ‘not recognized’.
?

## Slide 8: Text for “Not Recognized”
Device ID
If an AP sets Device ID element or Device ID KDE with the Device ID status field set to 1 indicating “Not Recognized”, then the AP may also provide, in that same Device ID element or Device ID KDE, a new device ID.
Note: An AP might set a Device ID status field to 1 indicating “Not Recognized” for any reason if the AP cannot unequivocally identify the non-AP STA shared identity state.
IRM
The non-AP STA, on receipt of an IRM Status field of value 1, indicating the AP has not recognized the IRM, may either continue to associate to the AP and provide a new IRM in an IRM KDE in message 3 of the 4-way handshake or, when using FILS authentication, including an IRM element in the Association Request frame, in or disassociate.
Note: An AP might set an IRM status field to 1 indicating “Not Recognized” for any reason if the AP cannot unequivocally identify the non-AP STA shared identity state.

## Slide 9: What about a “Mismatch” status code?

## Slide 10: “Mismatch” Proposal #1 Use “Not recognized”
TA = IRM
STA
AP
Msg 1
Msg 2
Device ID
Msg 3
Device ID KDE,
Msg 4
“Not Recognized” AND new device ID
IRM KDE “Not recognized”
IRM KDE “new IRM”
Same “rule” as before – If “not recognized” assume a restart
Simple rule.

## Slide 11: If we had Mismatch
TA = IRM
STA
AP
Msg 1
Msg 2
Device ID
Msg 3
Device ID KDE,
Msg 4
“Mismatch” AND new device ID
IRM KDE “Mismatch”
IRM KDE “new IRM”
“Rule” as before – assume a restart
i.e., same rule but now an added status. Need to describe/ define the ‘mismatch’ condition

## Slide 12: Text required if “Mismatch” status code
Device ID Text
When a non-AP STA receives an AP Identity frame with the Identifier Status equal to “Not Recognized” or “Mismatch”, it must assume that no shared identity state exists with the AP or ESS (as per the concepts of 12.2.10) or , in the case of “Mismatch” no common Devise ID and IRM shared identity exists, and the non-AP STA must (re)establish any desired, shared identity state per the procedures previously described. If an AP sets Device ID element or Device ID KDE with the Device ID status field set to 1 indicating “Not Recognized”, or set to 2 indicating “Mismatch”, then the AP may also provide, in that same Device ID element or Device ID KDE, a new device ID, thus establishing a new shared identity.
Note 1: An AP might set a Device ID status field to 1 indicating “Not Recognized” for any reason if the AP cannot unequivocally identify the non-AP STA shared identity state.
Note 2: An AP might set a Device ID status field to 2 indicating “Mismatch” if the device ID provided by the non-AP STA does not correspond to the non-AP STA indicated by the IRM.

## Slide 13
IRM Text
In the case that the non-AP STA has also provided a device ID and the AP does not recognize the device ID and the IRM as shared identities for the same non-AP STA, the IRM Status field of the IRM KDE or IRM element is set to 2 to indicate a mismatch. The non-AP STA, on receipt of an IRM Status field of value 1 or 2, indicating the AP has not recognized the IRM, or that there is a mismatch, may either continue to associate to the AP and provide a new IRM in an IRM KDE in message 3 of the 4-way handshake or, when using FILS authentication, including an IRM element in the Association Request frame, thus establishing a new shared identity,in or disassociate.
Note: An AP might set an IRM status field to 1 indicating “Not Recognized” for any reason if the AP cannot unequivocally identify the non-AP STA shared identity state.
Plus new line in the Status code
Add line to Table 9-322aq and Table 9-322ar and edit row three.
2 Mismatch IRM and Device ID recognized but as shared identities for different STAs
3-255 Reserved

## Slide 14: Proposed
In TG discussions there was a view to reject the “mismatch” comments as not easy to agree what is going on or how to define it.
Even if we have a “mismatch” status code the result is the same.
Straightforward rule for Device ID or IRM to assume restart is they get a “not recognized” status. AP can set it easily in all situations.
Recommend “not recognized” approach

## Slide 15: What about FILS?
Order is:
FILS Authentication Request
FILS Authentication Response (Keys established)
FILS Association Request STA sends new IRM AND device ID
FILS Association Response AP sends Device ID and IRM elements
- Device ID “Not recognized”
AP sends Device ID status AND new Device ID in Association Response
- IRM “Not recognized”
AP sends IRM status in Association Response (already has new IRM)
Same “rule” – “not recognized” or “mismatch” provide new device ID/IRM and treat as new.

## Slide 16: What about PASN?
Order is
STA to AP Authentication Msg 1 (Clear)
AP to STA Authentication Msg 2 (encrypted)
STA to AP Authentication Msg 3 (encrypted)
Procedure: Device ID
Temp ID sent in Msg 1 (in the clear).
AP sends ID KDE in msg 2, with Status field
  AP always provides NEW (temporary) ID in msg 2 to be used in next PASN Authentication.
If “not recognized”, No real difference, STA/AP just know it is a restart.
Procedure: IRM
IRM = TA
AP sends IRM KDE in msg 2, with Status field
STA sends new IRM in msg 3
If “not recognized” in msg 2, No real difference, STA sends new IRM in msg 4 and AP/STA know it is a restart.
“Mismatch” is therefore covered.
Is ‘Mismatch ‘ a real thing for PASN? Would a STA use both? Are we happy with the Temp ID (for me this is NOT Device ID)

## Slide 17: Summary
If Device ID status is “not recognized”, the new device ID provided in same KDE or element.
If IRM status is “not recognized”, the new IRM is sent as normal, but STA understands this is a new start.
Works for 4w HS, FILS and PASN.
If we had a special “mismatch” status, nothing is actually changed or gained, except that the definition of when to use “mismatch” is now required. i.e., a lot more text required.
Propose to go with “not recognized” approach

## Slide 18: Probabilities of Duplicate IRM
Probabilities: 100 stored IRMs - 1 in 14 billion
1000 stored IRMs – 1 in 141 million
10000 stored IRMs – 1 in 1.4 million
Doing it twice? Astronomical.
What do these probabilities mean?
If AP has 1000 STAs registering per day, and 1000 stored IRMs, how long before 0.5 chance of duplicate? – 192 YEARS
10,000 stored addresses and 1000 STAs per day? – 1.92 years
So, need to solve this is very dependent upon how many STAs do we expect an ESS to store. In any event it’s rare.

## Slide 19: “Duplicate IRM” 4w HS
New IRM is sent in msg 4, AFTER the IRM status has been sent by the AP in msg 3.
Hence, too late.
SOLUTION #1
STA sends the new IRM in msg 2
AP sends status in msg 3 “Duplicate”
STA sends new IRM in msg 4.
Problem - still does not work for FILS
SOLUTION #2
STA associates, AP sends action frame with IRM IE status field set to “Duplicate”
STA sends action frame with new IRM in the IRM IE

## Slide 20: Solution #3 Simply use “Duplicate”
STA A provides new IRM in msg 4 or Association Request (FILS)
AP sees that it is a duplicate (previously provided by STA B)
AP tags that Address as a “duplicate”
STA B comes back.
AP notes the duplicate address and sends “duplicate” as status code
STA B provides new IRM, assumes a re-start.
Address is still tagged as a duplicate until another STA tries to use it
STA A comes back,
AP notes the duplicate address and sends “duplicate” (aside could just send “not recognized” no difference)
STA A provides new IRM, assumes a re-start.
Address is now cleared in AP

## Slide 21: Text for Option #3
The non-AP STA, on receipt of an IRM Status field of value 1, indicating the AP has not recognized the IRM, may either continue to associate to the AP and provide a new IRM in an IRM KDE in message 3 of the 4-way handshake or, when using FILS authentication, including an IRM element in the Association Request frame, thus establishing a new shared identity with the AP, or disassociate. If an AP has stored the same IRM for two non-AP STAs, then if a STA uses that IRM to associate or authenticate then AP shall set the IRM status field to 1 indicating “Not Recognized”.

## Slide 22: Solution #1, #2 or #3
#1
Works great for 4w HS.
Would require FILS to send a new Association Request
  Might work but undefined behavior at the moment.
#2
Works for 4w HS, FILS and PASN
Requires new Action frames (is it worth it for very rare event?)
#3
Simple and does not create any new “rule”
Does require STA to start again (but this is very rare)
Propose to use “duplicate” status so that STA knows why, but effect is the same so could use “not recogized”

## Slide 23: Proposal
Same procedure as “not recognized”. Add text to say that AP sends ‘not recognized’ if duplicate IRM. Keeps everything simple and just one rule.
Device ID – Always provide a new device ID in KDE or element together with status “not recognized”,
IRM - Always provides a new IRM anyway, just assumes a restart for “not recognized”.
IRM duplicate
Option 1 – simply use “not recognized” when STAs return
Option 2 – add new action frames to tell STA to provide another IRM

## Slide 24: Straw Polls
Do you agree that no special “mismatch” case need be defined, and “not recognized” status is sufficient?
Y/N/A
For duplicate IRM do you prefer (remember this is rare event:
  Addition of Action frames?
  Wait for next association and use “duplicate” status with same rule as “not recognized”?
    Requires new status code and repeat of same rule as per “not recognized”
  Wait for next association and use “not recognized” status?
    STA knows what to do, but not why (same rule as “not recognized”)
A/B/C/no view