## Slide 1: AIML Use Cases Considerations
Date: 2023-09-11
Authors:

## Slide 2: Abstract
This submission covers the privacy aspects of the Roaming enhancements use-cases discussed at the AIML TIG

## Slide 3: Current Practices
Scenario:
  STA (identified as a MAC address, associated to an AP) requests from the AP a neighbour list (surrounding APs, their channel, BSSID)
  STA roams (to one of the recommended APs or another one), and the AP records this context transfer
Privacy Aspects:
  The AP knows the STA MAC address, the next AP to which the STA roamed, and the STA signal (on AP1 and AP2) at roam time
  An eavesdropper may know the STA MAC, the current AP and the next AP to which the STA roamed

## Slide 4: Proposed Practices
Scenario:
  STA (identified as a MAC address, associated to an AP) requests from the AP a neighbour list (surrounding APs, their channel, BSSID)
  STA roams (to one of the recommended APs or another one), and the AP records this context transfer
  The AP adds this record to a count pile (i.e., without the need to record the STA MAC) of previous roams
  AP provides the count pile to new STAs entering the cell
  Optionally, AP provides 802.11v+top pile when a STA reaches a target RSSI threshold (mid-point between cells)
Privacy Aspects:
  The AP knows the STA MAC address, the next AP to which the STA roamed, and the STA signal (on AP1 and AP2) at roam time
  An eavesdropper may know the STA MAC, the current AP and the next AP to which the STA roamed
  The AP and the STA know the count pile (percentage of STAs roaming to which neighbour)

## Slide 5: Conclusions
  STAs are identified by their MAC address
    The association and roaming pattern information is already available at the network infrastructure level
  The proposed use case doesn’t require to know the device’s true identity
    Roaming patterns can still be learned by using either randomized MAC addresses (e.g., RCM / 802.11bh IRMA) or even hashed/encrypted version of the STA MAC addresses (e.g., the data analysis described in IEEE 802.11-23/0433r2 , is exclusively based on anonymized data)
  There is a trade-off between accuracy and privacy
    Roaming patterns based on longer paths can provide more accuracy (path length is implementation-specific)
    Use of MAC randomization allows STAs to mitigate privacy concerns

## Slide 6: References
[1] IEEE 802.11-23/0475r4 - Proposed IEEE 802.11 AIML TIG Technical Report Text for the AIML-based Roaming Enhancements Use Case
[2] IEEE 802.11-23/0433r2 - AIML-based Roaming Enhancements Use Case