## Slide 1: Progress On Password Identifiers
Date: 2023-09-13
Authors:

## Slide 2: Abstract
An attempt to move forward to support a critical use case

## Slide 3: What’s The Problem?
Traditionally, shared key authentication was per SSID
  Every STA in the ESS used the same PSK
  SAE inherited this unfortunate architecture
Many use cases want to use multiple PSKs per SSID
The 11i PSK protocol (aka WPA2-PSK) was hackable
  Vendors sold product which supported multiple PSKs under a single SSID
  The AP would do a dictionary attack against itself in 4way HS to determine which PSK the STA used
  This is (intentionally!) not possible with SAE
New PHYs are prohibiting the 11i PSK protocol
  It will be impossible to support the use cases which require multiple credentials
  This will hinder adoption of new PHYs (or encourage their insecure use)

## Slide 4: Where Are Now?
Password identifiers have been part of IEEE Std 802.11 for years
  Handset vendors UI concerns compelled RSNXE bit use
  Privacy concerns have prevented their adoption into certification programs
  Lack of adoption in certification programs have led to non-implementation
  This is not a viable solution to address the multi-credential use case
Proposal for adding privacy to password identifiers
  Use HPKE to encrypt the STA’s identity in the AP’s public key
  Add AP’s public key to beacons and probe responses
  Use new IE to hold protected password identifiers vs old kind

## Slide 5: Where Are We Now?
Opposition to privacy proposal
  Don’t know how to age out public keys
  TOFU is bad
  …. something ….
Proposal to use 802.1X with an EAP method that supports username/password instead of using SAE
  TOFU is even worse– reduces security to that of WPA2-PSK
  If this addressed the use case it would be used already
  802.1X/EAP for unique password credentials should be rejected
Need to come up with a viable solution
  HPKE-based proposal is simplest and most secure
  How can we move forward?

## Slide 6: What Next?
Would removing the public key from the beacon help?
  Define an ANQP exchange to ask for/receive AP’s public key
  This still has TOFU issues, but still better than 802.1X/EAP
Would using a new AKM exclusively for this help?
  A “transition” mode would probably require the new AKM plus AKM 24
  UI would be cleaned up because if it’s the old AKMs, don’t include the “identity” widget, if it’s this new one, include it.
  Easier to ignore if you don’t want to implement this– if the AKM is not supported it’s not gonna show up to a user, reduces the problem of misconfiguration

## Slide 7: Straw Poll #1
“Removing the public key from beacons and using ANQP to distribute public keys would improve the HPKE-protected password identifier scheme”
Y:
N:
A:

## Slide 8: Straw Poll #2
“Using a unique AKM exclusively for protected password identifiers would improve the HPKE-protected password identifier scheme”
Y:
N:
A:

## Slide 9: Backup

## Slide 10: Assuming + Response to Straw Polls
“I would support the HPKE-protected password scheme if it used ANQP to distribute public keys and used a new AKM for its exclusive operation”
Y:
N:
A: