## Slide 1: Dynamic Polarization Spatial Multiplexing and Beamforming WLANs: Smashing the Age-old MIMO Paradigm
Date: 2023-09-12
Authors:

## Slide 2
Breakthrough Walsh-sequenced Polarization MIMO combines unbounded order spatial stream Multiplexing with steerable high directivity Beamforming to yield EHT-based Dynamic Polarization Multiplexing and Beamforming WLANs transporting, for instance, up to 92 Gbps Fiber Replacement Backhaul in a 320 MHz channel at 6 GHz beyond 18 km. “DPMXBF” merits serious consideration as a TGbn PHY.
Abstract

## Slide 3
Proposed “DPMXBF” 802.11 PHY
32 IEEE802.11be RF spatial streams
  32x32 MIMO Polarization Multiplexing
  32x32 MIMO Beamforming
  5-7 GHz UNII Operation
  4096 QAM
  320 MHz BW
  92,224 Mbps peak Data Rate
  > 550 m WLAN Free Space Range
  > 2.8 km Fixed Wireless Access FS Range
  > 18 km Fiber Replacement Backhaul FS Range
Dynamic Polarization WLANs

## Slide 4: Dynamic Polarization MIMO Reciprocally Interference-Free Cochannel Propagation of Countless WLAN Spatial Streams in Terrestrial DLOS Channels
DPMXBF Propagation Channel Model
[HDP] represents the DPMXBF medium transfer function as well as the WLAN Polarization Multiplexer
If [HDP] is non-singular, it has an inverse [HDP]-1 representing the WLAN Polarization Demultiplexer
The analysis following will verify [HDP] non-singularity and gauge its computational tractability

## Slide 5: [HDP] Characterization
  “n” Tx selectable Dual-Pol Antennas (“DPAs”) “Polarization Differentiate” n RF Spatial Streams [S] (i.e., Si, i = 1, 2 … n) with n distinct, corresponding Walsh-m (m>n) sequences [DPC] to yield [DPS]
  Transmit Beamforming (TxBF) aggregates the DPSi for high directivity transmission toward n Rx DPAs
  The n Rx DPAs “Differentiated Polarization Filter” [DPS] with the identical TxBF Walsh-m sequences for high directivity detection by the RxBFs, yielding the DP polarization multiplexed [S*] (i.e., S*ij, i, j = 1, 2 … n)

## Slide 6: [HDP] Operation
As the DPCi comprise Walsh binary orthogonal sequences,
ALL S*i=j = 1 and ALL S*i≠j = r, where r (in theory) equals 0.5

## Slide 7: [HDP] Polarization Multiplexer Representation
  In practice, however, the [HDP] DP Propagation Channel correlation index r corresponds to the cross-pol isolation measured between a realizable Rx DPA’s selectable orthogonally polarized elements
    For example, commercially available X-band Dual-Pol antennas spec xpol iso at -25dBc typical
    Therefore, [HDP] can be expressed as
    [HDP] is non-singular (as well as deterministic, time-invariant and uniform), meaning there exists an [HDP]-1 DP WLAN Polarization Demultiplexer that is also deterministic, time-invariant and uniform (!)

## Slide 8: [HDP]-1 WLAN Polarization Demultiplexer Representation
    So, given a DPMXBF Propagation Channel represented by
    There exists a DPMXBF Polarization Demultiplexer represented by

## Slide 9: DPMXBF WLAN Polarization Demultiplexer Implementation
    The DPMXBF Tx-Rx Transfer Function [S’] = [S*] x [HDP]-1 (= [S]) may be equivalently expressed computationally as well as by hardware (i.e., the physical DP WLAN SDMX) by:
    and
    The DP Polarization Demultiplexer reduces to a trivial hardware implementation

## Slide 10: Comprehensive Dynamic Polarization WLAN Model
[HDP] DPMXBF Propagation Channel
[HDP-1] DPMXBF WLAN SDMX

## Slide 11: Dynamic Polarization Applications
    Ultra-High-Capacity WLAN Mesh Dual Platform Dynamic Polarization Routers 3x faster than today’s best WiFi-7 devices
      PMP 32nd order Dynamic Polarization (“DP-32”) WLAN AP/ Meshnode distributes 92 Gbps/ relays 46 GHz at 6 GHz across 180o Pairs with a PMP WiFi-6 “AP Drop” distributing 4.1 Gbps at 2.4 and 5 GHz across 360o
      P2P DP-32 WLAN Client receives 5.8 Gbps at 6 GHz beyond 560m Pairs with a PMP WiFi-6 “Client Drop” also distributing 4.1 Gbps at 2.4/5 GHz across 360o
    Ultra-High-Capacity Fixed Wireless Access Today’s FWA is 95% 5G, Dynamic Polarization could flip it ALL to WiFi
      PMP DP-32 FWA AP distributes up to 92 Gbps at 6 GHz across 60o
      P2P DP-32 FWA Client receives up to 5.8 Gbps at 6 GHz beyond 2.8 km
    Fiber Replacement Backhaul P2P WiFi-7 Backhauls (using 1 m Dishes) transport 5.8 Gbps at 6 GHz beyond 10 km
    P2P DP-32 FRBH Nodes transport up to 92 Gbps at 6 GHz beyond 18 km

## Slide 12
Node Type | Element Directivity | SDPA Gain
WLAN AP/MN | 180o | 20.5 dBi
FWA AP | 60o | 30.5 dBi
FRBH N | 30o | 36.5 dBi
DP-32 AP/Meshnode SDPA-32 Phased Array
SDPA Beamwidth (WxH): 16.9o x 16.9o
DP-32 SDMux
Contemplated 92 Gbps DP-32 Access Point/ Meshnode (32 EHT Spatial Streams)
92/69 Gbps 6/5 GHz DP-32 AP/MN
TTD xBF

## Slide 13: Contemplated 5.8 Gbps DP-32 Client (2 EHT Spatial Streams)
Node Type | Element Directivity | SDPA Gain
WLAN Client | 180o | 20.5 dBi
FWA Client | 90o | 26.5 dBi
DP-32 Client SDPA-32 Phased Array
SDPA Beamwidth (WxH): 16.9o x 16.9o
DP-32 SDMux
TTD xBF
5.8/4.3 Gbps 6/5 GHz DP-32 Client

## Slide 14: Contemplated Dynamic Polarization WLAN Mesh Network
Link Obstruction | 6 GHz RF Attenuation
Outdoor Foliage | 1 dB/ meter
Indoor Drywall | 2 dB/ Wall
Exterior Stucco | 6 dB/ Wall
Exterior Masonry | 15 dB/ Wall
Link Type | Data Rate | Range | NW Capacity
AP – MN MN - MN AP/MN - C | 92.2 Gbps 46.1 Gbps 5.8 Gbps | 565 m/ Free Space 422 m/ 3 m Foliage 222 m/ 1 ID + 1 ES | >40k concurrent Users

## Slide 15: Contemplated Dynamic Polarization FRBH + FWA Network
Link Obstruction | 6 GHz RF Attenuation
Outdoor Foliage | 1 dB/ meter
Link Type | Data Rate | Range | NW Capacity
FRBH N - N | 92.2 Gbps | 18.0 km/ Free Space | 
FWA AP – C | 92.2 Gbps 83.0 Gbps 76.9 Gbps | 2.8 km/ Free Space 3.2 km/ 3m Foliage 3.3 km/ 5m Foliage | >40k Subscribers provided 5x Oversubscription

## Slide 16: Contemplated Dynamic Polarization Metro Wireless
Link Type | Data Rate | Free Space Range | NW Capacity
12x FWA AP – C | 1107 Gbps 996 Gbps 922 Gbps | 0 – 2.8 km 2.8 - 4.5 km 4.5 – 5.8 km | >480k Subscribers provided 5x Oversubscription

## Slide 17: DPMXBF WLANs Summary
    Polarization Multiplexing, a new, way-out-of-left-field reformulation of MIMO (Spatial) Multiplexing boosts 802.11 speeds to nearly 100 Gbps at well-beyond kilometer ranges
    DPMXBF deserves consideration as an integral PHY for the nascent 802.11bn standard