## Slide 1: TGbi – Proposal for MACc/MACp Extension
Date: 2023-09-11
Authors:
Name | Affiliations | Address | Phone | email
Jerome Henry | Cisco |  |  | jerhenry@cisco.com
Domenico Ficara | Cisco |  |  | dficara@cisco.com
Javier Contreras | Cisco |  |  | jacontre@cisco.com
Ugo Campiglio | Cisco |  |  | ucampigl@cisco.com

## Slide 2: Proposal from 11-23/1246r1
Sliding window of addresses:
  Two active MAC addresses: current (MACc) and previous (MACp)
  Epoch divided in two:
    First period where two MAC addresses for transmission are used simultaneously
      MACp used to close Block ACK transmissions, AMPDUs and retransmissions
    Second period (longer) of single use of MACc
Only two 48-bit registers are needed for A1
  The current one and the previous one
  When an epoch starts, a new MACc is decided, move current MACc to MACp, add new MACc to tuple.
Straw Poll
  Y:14
  N:0
  Abs: 5
  No answer: 7
epoch
Simultaneous use
MACp
MACc

## Slide 3: MACc/MACp Considerations
During an epoch, a single STA uses a single MAC
There is a temptation for eavesdropper to attempt to fingerprint a STA during an epoch
  Epoch boundaries are easy to spot
There is a temptation for STAs and networks to minimize epoch duration to limit fingerprinting efficiency
The Epoch boundary is compute-intensive on the AP (needs to renew all STAs’ MACs)
  However, there is not much more compute work if the AP renews one MAC for a STA, vs renewing 2 MACs for the same STA – the STA-count-per-radio reduces linearly
  APs need HW change anyway to support 2 MACs, not much more needed to support n

## Slide 4: MACc/MACp Extension Proposal
At epoch boundary, the STA gets N MACs (thus N MACc and N MACp)
  N could be negotiated at association
During the epoch, the STA can freely use any of its N MACc
  The AP maps all of them to the same STA
  An eavesdropper has a much harder time mapping them all to the same STA
  The STA may also use rules for MACc choice (e.g. MACc1 for voice flow, MACc2 for management frames, or time-linear change, etc.) – the STA may not have to share its choice reasoning with anyone
As proposed in 11-23/1246r1, at epoch boundaries the MACs are changed, with a sliding window tolerance

## Slide 5: Summary
MAC change at epoch boundaries are compute-intensive, in particular on the AP
Changing one MAC or more than one MAC has low compute difference, and acceptable memory impact
Allowing more than one MAC per STA per epoch improves privacy, at low computation cost

## Slide 6: Strawpoll
Do you agree on working on a solution for MAC address changing, in which the STA is allowed to use more than one MAC per epoch?
Y:
N:
Abs:
No answer: