## Slide 1: Integrated mmWave Design Considerations
Date: 2023-11-03
Authors:

## Slide 2: Motivation
The scope of the IMMW SG, as defined in [1] and [2], is to develop a PAR and a CSD
“… for a new 802.11 MAC/PHY amendment which specifies carrier frequency
operation between 42.5 and 71 GHz and leverages MAC/PHY specifications in the Sub 7
GHz bands.”
The integrated sub-7 GHz and mmWave approach offers the possibility of:
  Substantial enhancement in Wi-Fi network capacity, increased throughput, and reduced latency with the opening of new wideband channels that allow for a high degree of spatial reuse
  Allowing for a single baseband processor support 2.4/5/6/60 GHz communications
  Easier integration and load balancing between sub-7 GHz and 60 GHz links
  Enhancing system reliability by mitigating impact of on/off nature of 60 GHz links

## Slide 3: Defining “Integrated”
From UHR SG contributions:
  “Goal to reuse the 2.4/5/6 GHz design in 60 GHz to keep complexity within the bounds of lower band 802.11” [3]
  “…60 GHz interface to mainstream Wi-Fi, reusing as much as possible low band baseband and design…” [4]
  “…reuse existing lower band Wi-Fi solution (Modem/PHY, MAC and SW) and upclock it…” [4]
  “…all devices operating in mmWave shall be MLO-capable and shall have at least one affiliated STA/AP in the lower band in addition to the one in the mmWave band” [4]
  “We foresee that a multi-link device with both mmwave and low frequency bands is the future” [5]
  “Reusing the baseband and designs of low band as much as possible is a good direction to go” [6]
  “…standardize multi-link (ML) with bands in sub-7 GHz combined with bands in the 45-72 GHz range” [7]
We recommend defining integrated mmWave within the IMMW PAR, and limiting the effort’s scope, by incorporating the following requirements:
  mmWave PHY derived from sub-7 GHz PHYs
  Incorporate mmWave links into the MLO architecture
  mmWave operation requires an enabled sub-7 GHz link

## Slide 4: IMMW Adoption
The success of integrated 802.11 systems depends significantly on the ability to offset the substantial area and complexity of mmWave RF/antenna technology. This can be achieved in part through the implementation of a baseband processor (PHY/MAC) that seamlessly supports both sub-7 GHz and mmWave frequencies, while keeping additional complexity (w.r.t. a sub-7 GHz only processor) at a minimum.
To this end, we recommend the following design elements:
  Design to reduce complexity and power consumption as highest priority
  Support asymmetric links (that is, STAs may have different antenna array sizes)
    Push higher complexity to AP, smaller antenna arrays at client
  Goal should be opening new wideband channels (160, 320, and possibly 640 MHz) and *not* defining a PHY that supports (single-stream) data rates higher than those defined for sub-7 GHz
    For example, keep maximum rate at approximately from 0.5 to 2 Gbps
  Define bare minimum set of features and options. Reduce IMMW's scope ruthlessly
    Example: Single-user operation only

## Slide 5: Incorporating mmWave into MLO Architecture
Incorporating mmWave into the MLO architecture is key for the success of integrated mmWave:
  Integration of sub-7 GHz and mmWave required to reduce connection loss/increase reliability (due to mmWave link blockage, for example) and to power save
  Load balancing between sub-7 GHz and mmWave to reduce latency and enhance throughput while maintaining reliable connection
  Use of lower bands to reduce mmWave management overhead (association, BF training support…)
    Potentially avoid definition of a control PHY (see 11ad/ay)
Some challenges associated with incorporating mmWave into the MLO architecture:
  Sustain seamless connectivity even when one of the links (60 GHz) is susceptible to outages (blockage, beamforming training)
  TBD

## Slide 6: Other Goals
Define a lightweight but robust beamforming procedure
  Beamforming training adds overhead and increases power consumption.
  Critical to define a beamforming procedure that is less complex and has lower overhead than those in IEEE 802.11ad/ay – ideally with the same or increased robustness level.
    For example, use assumption of asymmetric links (if/when appropriate).
Provide adequate MAC efficiency
  Technical challenges related to timing (IFS) depending on MLO architecture (EMLSR, for example).
  MLO design elements (previous slide).
Define effective power management protocols

## Slide 7: For Further Consideration
PAPR reduction techniques
  High PAPR of OFDM signals lead to poor energy efficiency.
  Possible techniques: Filtering, subcarrier assignment… literature in the area is vast.
  Certain techniques/approaches could be implementation-dependent; that is, standard support may not be necessary.
    Topic for further analysis.
  At the same time, it is critical to not significantly deviate from sub-7 GHz PHY definitions/structure.

## Slide 8: For Further Consideration
Consider supporting sensing and ranging applications
  Added value to IMMW technology.
  Evaluation of additional definitions and extra complexity (beyond/building upon 11bf and 11az) required.
Facilitate coexistence with 60 GHz radar

## Slide 9: Conclusions
The success of integrated 802.11 systems depends significantly on the ability to offset the substantial area and complexity of mmWave RF/antenna technology. This can be achieved in part through the implementation of a baseband processor that seamlessly supports both sub-7 GHz and mmWave frequencies.
PHY/MAC complexity leads to larger silicon area and power consumption. It is critical to keep the scope of the project as narrow as possible, and limit the number of features and procedures defined in the future IMMW specification.
Define integrated mmWave with the following requirements (1) mmWave PHY derived closely from 11ax/be/bn; (2) Integrate mmWave links into the MLO architecture; and (3) mmWave operation requires a 2.4/5/6 GHz connection.

## Slide 10: References
[1] 23/0481r2, “Integrated mmWave Study Group Creation “, March 2023.
[2] 23/0188r6, “802.11 March 2023 WG Motions”, March 2023.
[3] 22/0729r1, "802.11 GEN8 Study Group", May 2022.
[4] 22/1595r1, "Some questions to answer in the SG“, Sept. 2022.
[5] 23/1083r1, "Next Generation SG formation", Jul. 2022.
[6] 23/0066r2, "Thoughts on Utilizing mmWave", March 2023.
[7] 22/1865r1, "Considerations on the PHY for 60 GHz", Nov. 2022.