## Slide 1: Relay for 11bn
Date: 2023-12-07
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St San Diego, CA 92131 |  | sanggook.kim@lge.com
Nov. 2023

## Slide 2: Introduction
The main goal of UHR is to achieve Ultra High reliability, with respect to throughput, latency, packet loss, and power consumption, as described in the UHR proposed PAR document[1].
For the RvR (Rate-vs-Range) improvement, which is one of the main objectives of UHR, Relay has been introduced and discussed throughout various presentations[2~10].
In this document, we review the relay operation discussed in UHR SG and we propose to apply the relay in 11bn to achieve the improvement for purpose of RvR and range extension.

## Slide 3: Relay communication
Relay was addressed to achieve improved performance in the aspect of RvR and the range extension in [2,3].
A Relay STA decodes the signal received from an AP and forwards it to an Destination STA(i.e. non-AP STA).
  Relay provides better link quality to both an AP and an Destination STA than a direct link between an AP and an Destination STA.
AP
Relay STA
Destination STA
(i.e. Non-AP STA)

## Slide 4: Considerations for Relay
In the relay topology, to provide the improved End-to-End QoS, the various consideration points in terms of RvR or Range extension should be taken into account.
In the next slides, we take a close look at things that need to be considered in common or separately when relaying for RvR or Range extension.
AP
Relay STA
Destination STA2
(i.e. Non-AP STA)
Destination STA3
(i.e. Non-AP STA)
Destination STA1
(i.e. Non-AP STA)

## Slide 5: Single-hop relay
As described in [2], to reduce the complexity of relay protocol, we can consider relay communication with single-hop relay.
With single-hop relay, the following gains can be considered.
  Simple and easy to manage.
    It does not require a complex routing algorithm like mesh networking.
  Low latency
    There are no additional delays due to multiple intermediate nodes.
  Less error accumulation
    It can prevent the error caused by the previous hop from causing more errors and accumulating with the hops.
AP
Relay STA
Destination STA
(i.e. Non-AP STA)

## Slide 6: Relay transmission with a TXOP
In Relay communication, the Relay STA transmits the signal to an Destination STA after receiving the data from the AP.
  To prevent the latency due to channel access of Relay STA for relay transmission and to perform the relay transmission efficiently, Relay transmission can be performed in one TXOP.
  To perform a relay transmission in a TXOP, as introduced in [2~7], Enhanced TXOP sharing can be considered.
    TXOP sharing for a relay is performed by the AP, and the Triggered TXOP sharing(TXS) defined in 11be or modified TXOP sharing method may be taken into account for relay communication.
    In addition, Whether a TXOP for relay transmission will be shared with the Destination STA requires further investigation.
TXS TF
AP
Relay STA
SIFS
CTS
···

## Slide 7: Channel information between Relay STA and an Destination STA
To provide the improvement of end-to-end QoS, it needs to measure the channel information between Relay STA and Destination STA.
To measure the channel information between a Relay STA and an Destination STA, the new channel sounding as described in [3, 4] can be considered.
  It is initiated by AP and as an initiation frame, a trigger frame can be considered.
    Here, a trigger frame may be designed newly because this frame is used to indicate the sounding information to STAs have the role of transmitter or receiver, respectively.
  Example of a sounding procedure for Relay STA and Destination STA [3,4]
In addition, even in a relay transmission for range extension, a sounding procedure may be able to be performed to measure the channel between Relay STA and Destination STA to improve the end-to-end QoS.
AP
Relay STA
Non-AP STA(s)
SIFS
Sounding PPDU
SIFS
Feedback
SIFS
Triggering of channel estimation
Report request

## Slide 8: Management frame relay
The non-AP STA located out of AP’s coverage can not receive the signal from the AP.
  Additionally, the signal from that STA can not reach AP.
To achieve range extension for communication for the corresponding STA, the Relay STA can forward the received management/control frame from the AP to the corresponding STA.
  For example, the management frame such as beacon frame, probing frame, and association frame may be applied.
    Some capability information or elements may be added to the management frame.
  Regarding the forwarding or retransmission of the management frame through relay STA, we need further study.
AP
Relay STA
Destination –STA
(i.e. Non-AP STA)
Management
frame
R_Management
frame

## Slide 9: Discovery of Destination STA
As in [3,4], to apply the relay efficiently in AP coverage, the appropriate non-AP STA should be detected before the relay communication.
  For that, the following can be considered.
    One thing is a discovery of non-AP STA existing near relay STA
      It can be initiated by AP or relay STA. and, to process it, a new frame exchange can be defined as described in [3].
    Another thing is a check of Non-AP STA’s signal reception status.
      It may be measured by AP or relay STA with conventional frame exchange.
  For example, non-AP STA for relay communication can be discovered with following procedure.
  Also, since a non-AP STA may have mobility, it can be done periodically.
Additionally, this procedure for discovering an appropriate Destination STA for efficient relay communication may be applied to relay transmission for Range extension.
AP
Relay STA
Non-AP STA(s)
PPDU
SIFS
Report Respond
SIFS
Triggering frame
Performing detection
Report Request
SIFS

## Slide 10: Performance enhancement
The relay communication provides the improvement of both throughput and latency.
  As described in [2], in an aspect of throughput, the transmission with a relay provided a 20% to 200% end-to-end throughput gain compared with direct transmission.
  In addition, the transmission with a relay provides a low latency for end-to-end transmission.
    As shown in [10], due to the better link quality of the relay link than a direct link, it is possible to use the high-order MCS for transmission.
      It causes the reduction of latency
    In channel conditions with obstacle/interference, we can get a gain of about 50%.

## Slide 11: Summary
To achieve improved reliability in terms of throughput, latency, and range extension, we propose to apply the relay communication in 11bn.
In addition, for efficient relay transmission and to obtain the maximum gain, the following should be considered.
  Support of one-hop relay.
  Relay communication in a TXOP
  The channel sounding between Relay STA and Destination STA
  The extended transmission of management/control frame
  Discovery of Destination STA

## Slide 12: Straw poll 1
Do you agree to define a relay protocol in 11bn to improve throughput, and coverage as well as latency?
  The details for the relay protocol are TBD.
  Y/N/A:

## Slide 13: Reference
[1] IEEE 802.11-23/0480r3 UHR proposed PAR
[2] IEEE 802.11-23/1908r1 UHR rate-vs-range enhancement with relay
[3] IEEE 802.11-23/0042r0 Thought for Range Extension in UHR
[4] IEEE 802.11-23/1138r1 Features to consider for efficient Relay operation
[5] IEEE 802.11-23/1139r0 Relay transmission in UHR
[6] IEEE 802.11-23/1146r1 Relaying for Low Latency Traffic in UHR
[7] IEEE 802.11-23/1175r0 UHR relay follow up
[8] IEEE 802.11-23/1450r1 Consideration on UHR Relay Architecture
[9] IEEE 802.11-23/1517r0 Follow up on the Relay Transmission
[10] IEEE 802.11-23/1518r0 Evaluation for the Relay Transmission