## Slide 1: Follow-up on a non-AP STA initiated TXOP sharing
Date: 2023-11-13
Authors:
Name | Affiliations | Address | Phone | email
Shawn (Sanghyun) Kim | WILUS Inc. | 216 Hwangsaeul-ro, Seongnam-si, Gyeonggi-do, Korea | +82-31-712-0523 | shawn.kim@wilusgroup.com
John (Ju-Hyung) Son |  |  |  | john.son@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com
Greg Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
November 2023
Sanghyun Kim (WILUS), et al.

## Slide 2: Abstract
November 2023
Sanghyun Kim (WILUS), et al.
Enhancement on the TXOP sharing procedure for the TXOP obtained by the non-AP STAs has been discussed in [1][2][3]
In this contribution, the followings are provided
  Channel access of a non-AP STA that intends to share its TXOP with AP
  Control frame transmitted by the non-AP STA
  Response frame transmitted by the AP
  Management of the shared TXOP
Additionally, discussions on the questions raised for the non-AP STA initiated TXOP sharing are provided, along with the motivation behind the non-AP STA initiated TXOP sharing

## Slide 3: Recap: Non-AP STA initiated TXOP sharing [1]
November 2023
Sanghyun Kim (WILUS), et al.
A non-AP STA shares its TXOP with its associated AP
During the shared TXOP, the AP manages frame exchange sequence (DL MU, UL MU or M-AP operations)
AP may expand BW of the shared TXOP by invoking a backoff procedure
AP
3
Response frame (P80)
2
1
0
Non-AP STA
Ctrl frame
(on P80)
0
IDLE
320 MHz PPDU
(e.g., MU-RTS)
MU & M-AP operations
TXOP
TXOP shared by the non-AP STA (P80)
TXOP of AP (320 MHz)
TXOP has been terminated
TXOP

## Slide 4: Motivation of the non-AP STA initiated TXOP sharing
When an AP gains the medium access, it can manage frequency/time resources considering requirements of each non-AP STA, thereby mitigating congestion of the medium
  Under this design philosophy, Trigger-based UL MU and MU-EDCA procedures were introduced in 11ax
  However, when UHR BSS utilizes large MU-EDCA parameters for increasing AP’s channel accessibility, the non-AP UHR STAs become disadvantageous compared to legacy OBSS STAs
    While the portion of the AP as a TXOP holder within a BSS may increase, but the overall portion that the UHR STAs acquire TXOP may decrease instead
Non-AP STA initiated TXOP sharing was proposed to allow UHR STAs compete under similar conditions as legacy OBSS STAs in terms of backoff procedure while enhancing AP’s resource manageability
November 2023
Sanghyun Kim (WILUS), et al.
Notes: ti

## Slide 5: Channel access of the non-AP STA
AP announces channel access policy through management frames
  Policies: “Normal” / “AP priority access”
    When the policy is announced as “Normal”
      Non-AP STAs do not need to share their TXOP with AP
    When the policy is announced as “AP priority access”
      Non-AP STAs are recommended to share their TXOP with the AP
When the policy is announced as “AP priority access”, the non-AP STAs may transmit the Control frame (e.g., TXOP sharing request) at the beginning or during their TXOP
  The non-AP STAs may transmit the other frames(e.g., low latency traffic) before sharing their TXOP
November 2023
Sanghyun Kim (WILUS), et al.

## Slide 6: Control frame transmitted by the non-AP STA
Control frame (could be a new variant trigger frame) transmitted by a non-AP STA can carry the following information:
  Duration of the remaining TXOP
  STA’s queueing status
    e.g., buffer status, latency requirement, etc.
    Additionally, the parameters that the non-AP STA intends to use for responding TB PPDU could be included (e.g., RU size, MCS, # of spatial streams, TB PPDU length, etc.)
      The AP may utilize the indicated information when soliciting a TB PPDU from the non-AP STA so that the non-AP STA to transmit using the desired parameters
November 2023
Sanghyun Kim (WILUS), et al.
AP
3
Ctrl
0
TXOP
Non-AP STA
AP
3
UL PPDU
0
TXOP
Non-AP STA
BA
Ctrl

## Slide 7: Response frame transmitted by the AP
Response frame transmitted by an AP indicates whether the AP will take over the TXOP
  When the AP intends to take over the TXOP
    AP transmits CTS-to-self frame
      Duration/ID field of the CTS-to-self frame indicates later time point than the duration indicated by the Ctrl frame transmitted by the non-AP STA so that the other STAs update their NAV timer
    AP can initiate MU/M-AP operations during the shared time duration
      The AP should transmit basic trigger frame soliciting TB PPDU from the non-AP STA that has transmitted the Ctrl frame as the first frame transmitted during the shared TXOP
  When the AP doesn’t want to take over the TXOP
    AP transmits CTS frame
      The non-AP STA that has transmitted the Ctrl frame can transmit UL PPDUs during the remaining TXOP (as the TXOP holder)
      The non-AP STA can transmit UL PPDUs without additional protection because already exchanged Ctrl/Response frames act as the RTS/CTS frames
November 2023
Sanghyun Kim (WILUS), et al.
Non-AP STA
AP
3
Ctrl frame
(on P80)
0
TXOP
Response frame (P80)
TXOP shared by the non-AP STA (P80)

## Slide 8: Management of the shared TXOP
The AP schedules DL/UL MU, M-AP operations until the time limitation expires
  The time already spend by the sharing non-AP STA should also be considered
The AP can expand the BW
  If idle subchannels are observed, the AP may invoke the backoff procedure to get the rights to access the idle subchannels
The AP might return the remaining TXOP to the non-AP STA by resharing the remaining TXOP, as defined in EHT TXS procedure
November 2023
Sanghyun Kim (WILUS), et al.
AP
3
Non-AP STA
Ctrl frame
(on P80)
0
TXOP
Response frame (P80)
TXOP shared by the non-AP STA (P80)
2
1
0
IDLE
320 MHz PPDU
(e.g., MU-RTS)
MU & M-AP operations
Operating on the wider BW

## Slide 9: Benefit for the non-AP STA sharing its TXOP
When multiple non-AP STAs share their TXOP with the AP, each non-AP STA can get more chance to access the channel due to MU operations initiated by the AP
To encourage the utilization of the TXOP sharing procedure, the AP may prioritize serving non-AP STAs that actively share their TXOP
November 2023
Sanghyun Kim (WILUS), et al.

## Slide 10: Discussions
Changing the TXOP holder from non-AP STA to AP
  In order to effectively utilize the time shared by the non-AP STAs, it’s necessary for the AP to be able to initiate OFDMA-based operation
    In the baseline, the OFDMA-based operations are considered to be initiated only by the AP, which is the TXOP holder
  To allow the AP to initiate M-AP operations during the time shared by the non-AP STAs, the AP should be the TXOP holder for the shared time duration
    The Sharing/Coordinating AP is considered to be the TXOP holder [4-7]
  Moreover, an AP that is the TXOP holder can provide more chance for LL STA during the shared time duration by using preemptable frame exchange sequences
November 2023
Sanghyun Kim (WILUS), et al.

## Slide 11: Summary
Non-AP STA initiated TXOP sharing was proposed to enhance AP’s network manageability
November 2023
Sanghyun Kim (WILUS), et al.

## Slide 12: Straw Poll
Do you agree to add the following text to the TGbn SFD ?
  11bn defines procedures that a non-AP STA share its TXOP with its associated AP
November 2023
Sanghyun Kim (WILUS), et al.

## Slide 13: References
[1] 11-23/581r0 Non-AP initiated TXOP sharing (Sanghyun Kim, WILUS)
[2] 11-23/1620r0 Reverse TXOP Sharing for UHR (Sindhu Verma, Broadcom)
[3] 11-23/1387r1 TXOP sharing extenstions for XR use-cases (Dibakar Das, Intel)
[4] 11-19/1895r2 Setup for Multi-AP coordination (Sungjin Park, LGE)
[5] 11-23/261r0 TDMA for wifi-8 (Dibakar Das, Intel)
[6] 11-20/1935r66 Compendium of straw polls and potential changes to the Specification Framework Document – Part 2
[7] 11-23/41r0 Considerations on Coordinated TDMA (Yanjun, Qualcomm)
November 2023
Sanghyun Kim (WILUS), et al.

## Slide 14: APPENDIX Illustration in terms of SU/MU operation
November 2023
Sanghyun Kim (WILUS), et al.
Rx
RTS
(from STA1)
Tx
CTS
Rx
UL PPDU
from the STA1
When STA1 transmits LL traffic before sharing its TXOP
(frame exchange sequences, AP’s point of view)
When STA1 transmits Ctrl frame as the first frame
(frame exchange sequences, AP’s point of view)
Tx
Block
Ack
Rx
Ctrl frame
(STA1)
Tx
CTS-to-self
Tx
Trigger
Rx
TB PPDUs
Tx
Trigger
Rx
Ctrl frame
(STA1)
Tx
CTS-to-self
Tx
DL MU PPDU
(including TF)
Rx
TB PPDUs
(including TB PPDU from the STA1)
Rx
TB PPDUs
MU duration
SU duration
MU duration
SU duration
Tx
Block
Ack

## Slide 15: APPENDIX Illustration in terms of operating bandwidth
November 2023
Sanghyun Kim (WILUS), et al.
Rx
Ctrl frame
(from STA1)
Rx
TB PPDUs
(UL MU-MIMO, including STA1)
80 MHz
Tx
CTS-to-self
Tx
Trigger
Tx
Block
Ack
Tx
DL MU PPDU
(80 MHz)
Rx
Block
Ack
Rx
Ctrl frame
(from STA1)
Rx
TB PPDU
(from STA1)
P80
Tx
CTS-to-self
Tx
Trigger
(Allocates P80 to STA1)
Tx
Block
Ack
Tx
DL MU PPDU
(160 MHz)
2
1
0
Rx
TB PPDUs
(other STAs)
Rx
Block
Ack
S80
w/o BW expansion
(frame exchange sequences, AP’s point of view)
w/ BW expansion
(frame exchange sequences, AP’s point of view)