## Slide 1: Seamless Roaming SPs
Date: 2023-11
Authors:

## Slide 2: Introduction
In this presentation, we present some common directions for 11bn seamless roaming design, which are mentioned in various proposals ([1] – [7])
We present a few SPs seeking some technical agreements

## Slide 3: General Directions
Most proposals are trying to achieve the following:
  The non-AP MLD should be able to roam from one AP MLD to another non-colocated AP MLD with minimal data interruptions/loss
    Non-AP MLD remains associated
    No reauthen, reassoc, and no need to re-establish the BA sessions
  Allow the non-colocated AP MLDs that belong to the same ESS to be controlled by a higher layer logical entity (e.g., by a single mobility domain AP MLD)
  Allow some form of context transfer from the serving AP MLD to the target AP MLD
  Allow the non-AP MLD to retrieve buffered DL data frames from the serving AP MLD
    However, we should limit concurrent serving by non-colocated APs to only during the roaming phase

## Slide 4: SP1
Do you support to define a mechanism in 11bn that enables a non-AP MLD to roam from one AP MLD to another AP MLD while the non-AP MLD stays in state 4 during and after roaming?

## Slide 5: SP2
Do you agree that in 11bn when a non-AP MLD that is in state 4 and is not in the process of roaming, the non-AP MLD is allowed to exchange class 3 frames only with one AP MLD?

## Slide 6: SP3
Do you agree that during roaming, after the DS mapping change from the current AP MLD to the target AP MLD, the current AP MLD will be able to deliver buffered DL data frames to the non-AP MLD for a TBD period of time, during which the non-AP MLD may retrieve the buffered DL data frames.
  It is assumed that the target AP MLD is able to deliver data frames after the DS mapping change

## Slide 7: SP4
Do you support that when a non-AP MLD roams from one AP MLD to another AP MLD, the context related to the non-AP MLD is transferred from one AP MLD to the other AP MLD such that it preserves the data exchange context for the non-AP MLD?
  Details of the context that can be transferred are TBD
  How to transfer the context is TBD. For example, the transfer of context can occur over the backhaul

## Slide 8: SP5
Do you support the following for roaming:
  Define a request frame for a non-AP MLD in state 4 to initiate the roaming procedure
  The roaming procedure involves context transfer between the current AP MLD and the target AP MLD and data path change (DS mapping changed from the current AP MLD to target AP MLD)
  Define a response frame to the non-AP MLD to indicate the completion of the context transfer so the non-AP MLD may send class 3 frames to the target AP MLD
    NOTE – The details of data path change is TBD

## Slide 9: References
[1] 11-22-1910-03-0uhr-seamless-roaming-for-uhr (Duncan Ho)
[2] 11-23-0231-00-0uhr-thoughts-on-seamless-roaming-under-the-non-collocated-ap-mld-architecture (Guogang Huang)
[3] 11-23-0279-00-0uhr-considerations-on-seamless-roaming (Insun Jang)
[4] 11-23-0322-00-0uhr-improve-roaming-between-mlds (Po-kai Huang)
[5] 11-23-0324-01-0uhr-roaming-requirements (Brian Hart)
[6] 11-23-0632-01-0uhr-smooth-roaming-follow-up (Liwen Chu)
[7] 11-23-1131-00-0uhr-thoughts-on-seamless-roaming (Ryuichi Hirata)