## Slide 1: Managed Networks under highly congested scenarios
Date: 11-9-2023

## Slide 2: Goals
Identify the current problems for QoS traffic under highly congested scenarios
Discuss an approach based on the AP centric architecture or managed networks

## Slide 3: Introduction
802.11bn targets the improvement of packet delivery by reducing the transmission latency and enhancing network reliability [1]
Applications and use cases with QoS-related requirements (e.g., bounded latency and reliability) have been growing in recent times [2]
  The critical QoS services can be mainly characterized by periodic traffic patterns, and strict timing requirements for data exchange [2, 3]
  Relying on maximizing throughput is not tenable in the long term as a sole requirement for correct QoS service operation
QoS services must coexist with non-QoS services within the same BSS

## Slide 4: Problem Statement (1/2)
The wireless scenarios are getting more congested due to the increase of connected high-performance Wi-Fi devices, competing for the wireless medium.
It has been shown that as congestion increases, and under contention-based congestion management, aggregated throughput gets saturated, and the latency is highly affected [4]
  This affects services whose QoS requirements are critical for a correct operation (reliability, latency, throughput)
Throughput
Network
Load
Congestion
Mild
Congestion
Non
Control
Non-optimal Control (DCF)

## Slide 5: Problem Statement (2/2)
Under congested network scenarios, the AP competes against all the non-AP STAs
  The AP may gain efficiency and reduce latency by using MU trigger-based tools (i.e., TUA) as opposed to letting clients contend
When EDCA admission control is employed, it regulates the QoS traffic on its own BSS, but it does not consider the EDCA admitted traffic on an OBSS

## Slide 6: Managed Network
One approach to address the issues mentioned on previous slides is to centralize and control the channel access from the AP
  AP-centric scheduled operations for controlling the QoS requirements
  Provide higher priority access to the AP for QoS transactions
  Establish QoS scheduling coordination mechanisms between OBSS APs
DCF/EDCA mechanism must be preserved for coexistence with non-QoS services and legacy devices

## Slide 7: Existing Enabling Features
Existing 802.11 features may help building an AP centric managed network
  SCS/MSCS → Request resources for QoS traffic flows
  Trigger-based access → Control over UL access managed by the AP, increasing the efficiency (i.e., TUA, MU EDCA)
  Restricted TWT → Plan which STAs will be awakened within a time window and guarantee channel availability for those STAs
  BSS color → Identification of BSS networks
  BSRP → STA polling to know their transmission buffer status
  EDCA for legacy clients
Proper coordination and application of these features can already result in a more managed network

## Slide 8: Current Features Limitations
Existing features offer a starting point, but there are gaps:
  AP and STAs have the same probability of accessing the channel, which causes difficulties in scheduling the network
    There exist features for adapting STA’s EDCA parameters, but it solves the problem only partially
  The QoS management is limited to its own BSS
    How to guarantee QoS in presence of OBSS
  There are no coordination mechanisms to facilitate the cooperation between APs, covering the OBSS and ESS cases
Previous 802.11 standards have defined mechanisms in these areas
  HCCA, OBSS management (Channel selection, QLoad reports, HCCA advertisement), …
  No market traction

## Slide 9: Addressing the gaps in UHR
Several UHR proposals may further enable the concept of managed networks
  Optimized Scheduled TXOP [5]
    Pre-planned DL/UL QoS scheduling with persistence capability for periodic traffic patterns, controlling the QoS and latency
  Multi-AP C-TDMA / C-rTWT [6, 7, 8 , 9]
    Coordination of AP operations, avoiding collision, and protecting all the QoS TXOPs
  CSMA enhancements [10]
    Enhancements to regular EDCA allowing prioritized access

## Slide 10: Main Requirements
Capability of AP-scheduled DL/UL QoS transactions, while guaranteeing latency and requested QoS requirements under highly congested scenario
  Provide legacy EDCA availability during the rest of the time
Priority access for the AP during QoS accesses
  Silencing EDCA mechanism of network STAs to not disturb the QoS scheduled transfers
Capability of coordinating the QoS scheduled accesses between APs, using proposed multi-AP mechanisms (e.g., Coordinated TDMA)
  Capability of quantifying the traffic load metrics of each BSS and sharing these reports for coordinating the use of common spectral resources, while maintaining the fairness in the assignment
Capability of announcing and time synchronizing BSS operations to facilitate the coordination with other BSSs (OBSS or ESS)

## Slide 11: Conclusion
We have discussed QoS requirements under highly congested scenarios and current/future traffic applications
We believe there is a need for an operation mode based on AP-centric network access and control to address these scenarios

## Slide 12: Straw Poll
Do you support enabling a mode of operation where channel access and operation are more centrally controlled by the AP?
  Y/N/A

## Slide 13: References
[1] IEEE 802.11-23/0028r6， UHR PAR discussion
[2] Inaki Val and et al. (MaxLinear), “High Criticality Use Cases and Requirements”, 23/1522r0, September 2023.
[3] Oliver Holland and et al. “Low Latency Communication White Paper”, P802.24-23-0010r4, July 2023.
[4] Tongxin Shu and et al. (Huawei), “Requirements of Low Latency in UHR”, 22/1519r0, September 2022.
[5] Dmitry Akhmetov and et al. (Intel), “Medium efficient scheduled channel access in next generation 802.11”, 23/0936r0, July 2023.
[6] Dibakar Das and et al. (Intel), “C-TDMA procedure in UHR”, 23/0261r0, January 2023.
[7] Yanjun Sun and et al. (Qualcomm), “Follow-up on Coordinated TDMA (C-TDMA)”, 23/0739r1, July 2023.
[8] Laurent Cariou and et al. (Intel), “rTWT for Multi-AP”, 23/0297r0, April 2023.
[9] Abdel Karim Ajami and et al. (Qualcomm), “Coordination of R-TWT for Multi-AP Deployment”, 23/0226r2, July 2023.
[10] Laurent Cariou and et al. (Intel), “Low latency channel access”, 23/1065r0, July 2023.