## Slide 1: Further considerations on coordinated TWT
Date: 06-15-2023
Authors:

## Slide 2: Abstract
In this contribution, we follow on TWT based multi-AP coordination.

## Slide 3: Coordinated TWT (C-TWT)
  Multi-AP (MAP) Coordination is one of the key features considered for UHR SG and IEEE 802.11bn.
  TWT-based multi-AP coordination is considered one of the candidate technologies for UHR[1-9].
  Different modes of TWT coordination can be considered—
    Client-centric TWT coordination: catering to specific STA to reduce its perceived OBSS interference during the TWT SPs
      TWT coordination can cater to specific STA to reduce its OBSS interference
      The victim STA can request the coordinating APs to assist in reducing the OBSS interference during its TWT SPs (either individual TWT or broadcast TWT)
        The request can be made to its associated AP.
        Alternatively, the request can be made directly to the aggressor AP
    Network-wide coordination: performed to assist a group of STAs in a BSS (e.g, for faster channel access for TWT scheduled STAs)
      TWT coordination can be performed to assist a group of STAs in a BSS
      An AP can request its neighboring AP to reduce interference during TWT SPs of a B-TWT/R-TWT schedule.
      During the TWT SPs, the neighboring AP can mute its transmission (C-TDMA) or use a different channel than what the requesting AP is using.

## Slide 4: Need for MAP coordination for R-TWT
Restricted TWT is an important tool developed in 11be for low-latency traffic prioritization.
  The R-TWT supporting STAs in the BSS that are not members of an R-TWT schedule end their TXOP before an R-TWT SP corresponding to the R-TWT schedule starts (in the figure, STA1 ends TXOP before STA2’s R-TWT SP starts)
  This gives priority to AP (in trigger-based R-TWT) and R-TWT member STAs to win the contention for the R-TWT SPs.
However, the R-TWT supporting STAs in the neighboring BSS may not obey the rules to protect the R-TWT SPs of another BSS
  Transmission in the neighbor BSS may continue occupying the channel during the R-TWT SPs of the first BSS (in the figure, AP2 doesn’t end TXOP before STA2’s R-TWT SP starts)
  This OBSS interference may disrupt the latency-sensitive traffic of the R-TWT scheduled STAs.
  ** Based on the association shown in the figure in the previous slide

## Slide 5: MAP coordination for R-TWT
Coordination among neighboring APs for protecting R-TWT SPs can be beneficial for latency-sensitive applications.
  The sharing AP can request the shared AP to protect the R-TWT SPs of the sharing AP
Types for protection for OBSS R-TWT (in terms of protection-level):
  Type-1 :
    The shared AP and all its associated STAs end their TXOP before the sharing AP’s R-TWT SP
    The shared AP and all its associated STAs can’t transmit during the R-TWT SP of the sharing AP
  Type-2 :
    The shared AP and all its associated STAs end their TXOP before the sharing AP’s R-TWT SP starts
    The shared AP and all its associated STAs can start contending for the channel at the start of the sharing AP’s R-TWT SP
  Type-3:
    The shared AP ends its TXOP if it is not serving a low latency STA (e.g., serving its own R-TWT scheduled STA)
    The non-AP STAs in the shared AP’s BSS don’t end their TXOP if the TXOP has been obtained for low-latency traffic (e.g., R-TWT scheduled STA)
    Otherwise, the shared AP and all its associated STAs end TXOP before the start of the sharing AP’s R-TWT SP
    After ending the TXOP before the sharing AP’s R-TWT SP starts, the shared AP and all its associated STAs can start contending during the R-TWT SP
  Type-4:
    Only the shared AP ends its TXOP before the sharing AP’s R-TWT SP starts
    The non-AP STAs in the shared APs BSS don’t end their TXOP before the sharing AP’s R-TWT SP starts
    After ending the TXOP before the sharing AP’s R-TWT SP starts, the shared AP can start contending during the R-TWT SP
  * Note: The above rules are for R-TWT supporting STAs only.

## Slide 6: Framework for Coordinated TWT
The baseline individual TWT is established using a negotiation between the two STAs. The baseline broadcast/restricted TWT is established through an advertisement by the AP followed by a negotiation between the AP and the STA.
Multi-AP TWT coordination calls for additional steps.
The overall phases for TWT coordination can be listed as—
  MAP TWT Announcement
  MAP TWT Negotiation
  Intra-BSS TWT Announcement
  Intra-BSS TWT Negotiation
  Maintenance of a TWT schedule/agreement
  Termination of TWT coordination

## Slide 7: MAP Announcement and MAP Negotiation
MAP TWT announcement: During this phase, the TWT sharing AP can identify the other APs that are willing to participate in TWT coordination.
  Basic capability and coordination information (e.g. modes of TWT coordination (iTWT/bTWT/rTWT)) can be announced during this phase.
  If a neighboring AP is willing and prepared to participate in the TWT coordination, it can inform the TWT sharing AP by responding to the announcement received from the TWT sharing AP.
  This phase essentially forms a TWT coordination group.
MAP TWT Negotiation: During this phase, TWT parameters for MAP coordination are decided among the participating APs.
  The sharing AP can send a TWT coordination request to the other APs in the TWT coordination group. Along with the C-TWT parameters, the request can also contain types of coordination.
    For example, if the negotiation is for an R-TWT, then the sharing AP can include the level of protection it requests from the shared APs [see [3]].
  Upon receiving the request, the shared AP can either accept/reject the request or suggest an alternative set of C-TWT parameters.
  Figure: Illustration of frame exchanges for MAP TWT announcement and negotiation. Assumes wireless MAP coordination. For managed networks, frame exchanges can happen through the central controller.

## Slide 8: Intra-BSS C-TWT Procedures
When a TWT shared AP agrees to coordinate with the TWT sharing AP, based on the nature of the agreement, the shared AP can take different approaches for notifying or (announcing for) the STA(s) in its BSS*
Approach-1: The shared AP, in notifying the member(s) of its own BSS, can make a distinction between its own TWT (i.e. the TWTs generated and maintained by the shared AP for its BSS) and the coordinated TWT that the shared AP is participating in.
  The shared AP can dictate the behavior expected from its associated STAs during the SPs of the coordinated TWT.
    Example 1: if the MAP coordination is for an individual TWT and the sharing AP requests to minimize the interference towards a victim STA in the sharing AP’s BSS during the C-TWT SP, then the shared AP can indicate to the interfering STA associated with the shared AP to avoid transmission during the C-TWT SPs**.
    Example 2: if the MAP coordination is for an R-TWT, the shared AP can announce the corresponding C-TWT schedule in its BSS, but add a marker in the schedule to distinguish it from its own R-TWT schedule. The shared AP can establish different rules in regard to this C-TWT such as membership management, and differentiated TXOP ending rules [see Types of R-TWT protection in [3]].
Approach-2: The shared AP Makes no distinction between its own TWT and the coordinated TWT it is participating in.
  More applicable for B-TWT/R-TWT based coordination
  The shared AP advertises the C-TWT schedule in its BSS as if the schedule is its own TWT schedule (TWT timing param would be adapted based on the shared AP’s TSF).
  The STAs in the shared AP’s BSS would be agnostic to whether the advertised schedule is a C-TWT schedule or not, and can seek membership in the coordinated schedule.
* Sharing AP’s intra-BSS TWT operation can follow baseline procedure.
** If the shared AP itself is the interfering STA, it can create a null towards the victim STA during the C-TWT SP.
  Figure: An illustration of a shared AP advertising and establishing a coordinated R-TWT schedule in its own BSS. In the figure, STA1 is associated with AP1, and STA2 is associated with AP2; the figure assumes the TSFs of the two APs are synced or the TSF difference is known.

## Slide 9: SP1
Do you agree to define a multiple AP coordination mechanism based on target wake time (TWT)

## Slide 10: References
[1] IEEE 802.11-21/1046r0, “Multi-AP: TWT Information Sharing”, Rubayet Shafin, et.al., July 2021.
[2] IEEE 802.11-22/1530r1, “Multi-AP coordination for next-generation Wi-Fi”, Rubayet Shafin, et.al., Sept 2022.
[3] IEEE 802.11-23/932r0, “Follow-up on TWT-based Multi-AP Coordination”, Rubayet Shafin, et.al., May 2023.
[4] IEEE 802.11-23/226r1, “Coordination of R-TWT for Multi-AP Deployment”, Abdel Karim Ajami, et.al., April 2023
[5] IEEE 802.11-23/250r0, “AP coordination with R-TWT”, Liwen Chu, et.al., April 2023
[6] IEEE 802.11-23/291r0, “R-TWT Multi-AP Coordination”, Muhammad Kumail Haider, et.al., May 2023.
[7] IEEE 802.11-23/297r0, “r-TWT for Multi-AP”, Laurent Cariou, et.al., April 2023
[8] IEEE 802.11-23/355r0, “Enhanced rTWT and MAP operation”, Hanqing Lou, et.al., May 2023
[9] IEEE 802.11-23/771r0, “Coordinated R-TWT Protection in Multi-BSS”, SunHee Baek, et.al., June 2023.