## Slide 1: Inter-PPDU Low Power Listening Scheme
Date: 2023-09-11
Authors:
Name | Affiliation | Address | Phone | Email
Yunsi Ma | HiSilicon |  |  | mayunsi@hisilicon.com
Wei Ruan |  |  |  | 
Yunbo Li | Huawei |  |  | 
Ross Jian Yu |  |  |  | 

## Slide 2
According to the PAR [1], reducing power consumption of WLAN devices is necessary and critical for 802.11bn.
In [2] and [3], a low power listening (LPL) mode based on initial frame was discussed, where the RTS/Trigger frame indicates the receive operating mode/parameters, including NSS, BW and MCS. The initial frame using padding can be used to wake up the doze chains and also provide a sufficient period for changing mode/parameters. However, the initial frame exchange increases the signaling overhead [4].
In [4], a LPL scheme based on preamble extension was developed. The UHR SIG field indicates the PHY parameters and the preamble extension provides the duration of changing parameters.
Recap

## Slide 3
Low power (LP) mode usually operates using one RF chain, low MCS and small bandwidth, while high power (HP) mode utilizes multiple RF chains, large MCS and up to 320MHz bandwidth. The durations of changing different PHY parameters vary greatly.
  For a non-AP MLD with multiple receive chains, LP mode only listens on a single link with a single receive chain, while HP mode could operate on multiple links.
A STA may take only less than two hundred microseconds to change its operating links, RF chains per link, NSS and MCS.
  The amount of time that RF chains turn on or off is on the order of nanoseconds.
In contrast, changing bandwidth takes a much longer duration.
  Increasing bandwidth requires recalibration of PLL and RF, which takes from hundreds of microseconds to several milliseconds.
To provide a few hundred microseconds for changing parameters, the existing schemes need to insert intra-PPDU padding. It will lead to large latency of other STAs and inefficient use of medium.
In this contribution, we introduce an inter-PPDU LPL scheme, which is suitable for diverse changing periods. It no longer inserts an extra padding and hence has little impacts on other STAs.
Issue

## Slide 4: Inter-PPDU LPL Scheme (1/2)
The target STA initially employs a dedicated LP mode for listening. Once the wake-up indication is detected, the target STA starts switching to HP mode.
In the inter-PPDU LPL scheme, AP sends an initial PPDU (i.e., ‘Notification PPDU’) to wake up the target STA.
  The notification PPDU indicates the PHY parameters of HP mode or hi-capability receiver, which may also contain a wake-up indication or a indication of the coming data.
    The format design needs further study.
    As an example, detecting different PHY parameters could be regarded as a wake-up indication.
  The notification PPDU is mainly used for delivering the data of other STAs.
Then the subsequent PPDUs (i.e., ‘Data PPDU’) send the data of the target STA.
PPDU 1
PPDU 2
AP
STA1
STA2
(Target STA)
BA
changing PHY parameters /
wake up hi-capability RX
LP mode /
lo-capability RX
HP mode /
hi-capability RX
BA
BA
PHY header of PPDU1
SIFS
Notification PPDU for STA2
Data PPDU for STA2
PHY parameters
wake-up indication
data
data
data
maximum transition period T0

## Slide 5: Inter-PPDU LPL Scheme (2/2)
AP actively solicits a status report from the target STA (Optional)
After an interval of T0, AP sends a Poll frame for soliciting a status report of STA2.
After receiving the Poll frame, STA2 indicates that it is ready for receiving data by sending a Response frame.
  There is a completion indication of changing parameters or modes in Response frame.
If the AP determines that STA2 is in HP mode, AP will send its downlink data.
PPDU 1
PPDU 2
changing PHY parameters /
wake up hi-capability RX
LP mode /
lo-capability RX
HP mode /
hi-capability RX
…
Notification PPDU for STA2
Data PPDU for STA2
data
BA
data
BA
PHY header of PPDU1
AP
STA1
STA2
(Target STA)
…
Poll
Response
T0

## Slide 6: Alternative Inter-PPDU LPL Scheme
After receiving the notification PPDU, STA2 sends a response frame and then starts to change PHY parameters.
  The limited length of the notification PPDU can reduce the waiting time before changing modes.
During the changing period of STA2, AP can also send data of other STAs, which significantly improves the use of medium.
PPDU 1
PPDU 3
changing PHY parameters /
wake up hi-capability RX
LP mode /
lo-capability RX
HP mode /
hi-capability RX
…
Notification PPDU for STA2
Data PPDU for STA2
data
BA
data
BA
…
Ack
PPDU 2
BA
data
AP
STA1
STA2
(Target STA)
T0

## Slide 7: Summary
In this contribution, we propose an inter-PPDU LPL scheme to simultaneously reduce power consumption and signaling overhead.
  One initial PPDU (i.e., notification PPDU) is used to wake up the target STA.
  The subsequent PPDUs (i.e., data PPDU) deliver the data of the target STA.
  The interval between the notification PPDU and the first data PPDU provides a sufficient duration for changing PHY parameters/capabilities.
In an alternative inter-PPDU LPL scheme, the target STA can respond to the notification PPDU. After sending the notification PPDU, AP continues to send data of other STAs, instead of waiting for the target STA.

## Slide 8: Reference
[1] 11-23/0480r3, UHR proposed PAR
[2] 11-22/1414r1, Low power listening mode
[3] 11-22/1841r0, Follow up on the low power listening mode
[4] 11-23/1100r0, Low power and long range preamble