## Slide 1: Physical Layer Reliability Improvements – Follow Up
Date: 2023-11-07
Authors:

## Slide 2: Introduction
In [1] we discussed methods for improving the reliability in TGbn
In particular, we suggested two different PHY related approaches for handling interference (recap on those in the next two slides)
Improved reliability and more efficient use of the spectrum are important goals of UHR (Ultra-High Reliability) [2]
In this contribution we address some questions that were raised during the presentation of [1]
We present some additional results showing how these approaches deal with changing interference conditions, and discuss our view on the mode of operation

## Slide 3: Recap: Approach #1 for Mitigating Interference
Replicate data in frequency domain as shown in the figure below
The receiver can identify if a portion of its spectrum is interfered, and based on this decide which subcarriers (or which replica) to combine (and how to combine)
The choice of RU size to use and the replication order (number of replicas) can be opportunistic or based on knowledge at the transmitter side (e.g. on the interference characteristics)
Advantages:
  Simple transmit scheme
  Significantly more robust to (narrowband) interference
Disadvantages:
  Less applicable for wideband interference
26-tone
26-tone
26-tone
52-tone
26-tone
26-tone
52-tone
4x replication to STA #1
2x replication to STA #2

## Slide 4: Recap: Approach #2 for Mitigating Interference
Transmitting known pilots – interlaced with the data – will allow a (multi-antenna) receiver to track and mitigate potential interfering signals
The receiver will apply an interference mitigation (receive beamforming) scheme
  Various algorithms may be employed
Advantages:
  Can handle interference of any bandwidth
Disadvantages:
  Need ‘extra’ Rx antennas (beyond N_SS) to cancel the interference
Interference Mitigation Pilot
Data

## Slide 5: Approach #1: Comparison with a lower MCS
One question raised during the presentation of [1] was what would be the performance of a lower MCS in the presence of interference
In the figure below we show a comparison between the performance – in the presence of interference - of two schemes having (potentially) the same spectral efficiency
  MCS 2 without replication (1.5bps/Hz)
  MCS 4 with duplication (1.5bps/Hz)
We assume a 242-tone data RU and a ~2 MHz interfering signal with SIR=0dB
As can be seen, without replication even MCS 2 reaches an error floor whereas using replication yields a clear advantage

## Slide 6: Approach #1: Comparison with a lower MCS (cont.)
An alternative way to compare the results is to vary the interference power for a fixed SNR
In the figure below we show a comparison between the performance – in the presence of varying interference - of the same two schemes having (potentially) the same spectral efficiency
We assume a 242-tone data RU and a ~2 MHz interfering signal with SNR=16dB
As can be seen, there is a clear advantage to using a higher MCS with replication

## Slide 7: Approach #2: Number of Required IM Pilots
In [1] we showed simulation results – both link-level & goodput – which were based on an arbitrary number of IM pilots (~30% of the subcarriers)
We were asked during the presentation of [1] whether so many IM pilots were needed
In the figure below we show a comparison of the goodput of various values of IM pilots, when using a 106-tone RU
As seen, a minimal number of IM pilots is needed (e.g. ~14% resources used for IM pilots is not enough)
However, using around ~20% of the resources for IM pilots yields the best performance

## Slide 8: Impact of Interference Rising and Falling
What happens when the interference rises – or falls – in the middle of the PPDU? What effect does this have on the performance?
In the figure below we compare the performance of approach #2 for the following 3 cases:
  Interference is constant for the entire PPDU
  Interference starts in the middle of the PPDU (within data portion)
  Interference starts at the beginning and ends in the middle of the PPDU
As can be observed, this approach is not sensitive to where the interference begins or ends – the gaps are quite small
  Meaning it is very robust

## Slide 9: Method of Operation
We view these PHY-based improved reliability approaches as tools that can be used in various scenarios where interference is likely to be dominant: home, enterprise, industrial, etc.
Similar to MCS and NSS that can be adjusted to optimize the performance, this type of approach can be viewed as an additional Tx scheme ‘dimension’ that may be exploited only when needed – or when deemed important enough to invest resources in improving the reliability
  In other words, used only when necessary (or worth the effort)
These approaches are not optimized for any particular scenario, but rather offer a general-purpose tool in the arsenal of Tx schemes
  For example, in case of long-term interference (constant across many PPDUs), one may choose to ‘invest’ IM resources within only a subset of the PPDUs (so as to reduce overhead) and apply mitigation at the receiver throughout all received packets

## Slide 10: Conclusions
In [1] we discussed how prevalent interference is in the WLAN bands, and how mitigating this interference (or the majority thereof) would lead to significantly better results, in particular lower latency
  We presented two approaches to mitigate the interference and showed, via simulation results, how we can improve the performance in the presence of interference
In this contribution we addressed some questions that were raised during the presentation of [1] and presented some additional simulation results, both of which further justify these two approaches for improving the reliability
We also discussed how we envision the system would operate using this type of improved reliability tool

## Slide 11: References
[1] 11-23-1490r0: Physical Layer Reliability Improvements (Shimi Shilo et al)
[2] 11-23/0028r6: PAR Discussion (Laurent Cariou)
Notes: at least one mode of operation capable of improved support, compared to 802.11be, for applications with stringentworst-case latency and jitter requirementscompared to 802.11be // i.e., avoid “worst-case”