## Slide 1: TXOP Sharing based UL Relaying
Date: 2023-11-12
Authors:

## Slide 2: Introduction
“Enabling at least one mode of operation capable of increasing throughput, as measured at the MAC data service Access Point, at different Signal to Interference and Noise Ratio (SINR) levels (Rate-vs-Range), compared to EHT MAC/PHY operation” has been one of the main objectives within the scope of P802.11bn [1].
Rate-vs-range enhancement via relays has already been an important consideration for 11bn [2-4].
TXOP sharing (TXS) for relay transmission has already been considered in some contributions [5,6].
In this contribution, we consider an efficient TXOP allocation approach for TXS-based UL relaying.

## Slide 3: Recap: TXS-based UL/DL Relaying [5]
One approach for TXS-based relaying is to allocate the time duration to Relay STA for transmission between Relay STA and non-AP STA for DL relaying.
Similarly, for the UL operation, after the TXOP sharing with Relay STA, AP may send an additional trigger frame to the STA to start uplink transmission.
The limitations of allocating TXOP only to the Relay STA during UL relaying:
  Additional trigger frame increases the overhead of relaying procedure.
  TXOP sharing with a Relay STA may not be scalable if there are multiple relays.

## Slide 4: Approach for TXS-based UL Relaying
To overcome the limitations of transmitting an additional trigger frame to start uplink transmission and not supporting multiple hops in relaying, multi-user allocation in TXOP sharing procedure can be defined.
With an indication of relaying operation in the MU-RTS TXS TF and allocating different time periods to Relay STA(s) or the STA in the user info fields, both uplink and downlink relaying may be supported.

## Slide 5: TXS-based UL Relaying (1)
AP transmits a MU-RTS TXS TF allocating the first time period to the STA, then to the Relay STA, with an indication of UL relaying. The allocated STAs transmit to the next STA in the user info field or to the AP depending on the order of allocation.

## Slide 6: TXS-based UL Relaying (2)
In case the STA is outside the communication range of AP, AP transmits an MU-RTS TXS TF with allocations of time periods to STAs, also including indications of relaying and extending the range of the MU-RTS TXS TF.
Relay STA then transmits a new MRTT frame to the STA to inform it of the UL relaying. New MRTT frame contains the STA allocation.

## Slide 7: TXS-based UL Relaying (3)
In case there are multiple relays involved in relaying, proposed approach of multi-user allocation for TXOP allocation is scalable for multi-hop relaying.

## Slide 8: Adoption to DL Relaying
For DL, AP may allocate time duration to Relay STA for transmission between Relay STA and non-AP STA.
Multiple or single user allocations can be used in MRTT frame.

## Slide 9: Conclusion
Relaying is an important topic for 11bn for rate-vs-range enhancement. TXS-based relaying approaches are among the good candidates as they provide end-to-end protection.
A TXS-based UL relaying approach based on multi-user allocation has been proposed to address limitations of allocating TXOP only to the Relay STA during UL relaying.
Proposed approach is compatible with earlier proposed TXS-based DL relaying approaches and can be adopted to support both UL and DL relaying.

## Slide 10: References
[1] 23/0480r0, UHR Proposed PAR
[2] 22/2049r2, UHR PAR Discussion
[3] 22/1908r1, UHR Rate-vs-Range Enhancement with Relay
[4] 23/0042r0, Thought for Range Extension in UHR
[5] 23/1139r0, Relay transmission in UHR
[6] 23/1175r0, UHR Relay Follow-up