## Slide 1: Coexistence Protocols for UHR
Date: 2023-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Alfred Asterjadhi | Qualcomm Inc. |  |  | aasterja@qti.qualcomm.com
George Cherian |  |  |  | 
Abhishek Patil |  |  |  | 
Gaurang Naik |  |  |  | 
Duncan Ho |  |  |  | 

## Slide 2: Introduction
A STA can share its radio resources with other technologies (BT, etc.) or with other STAs that are affiliated with the same MLD
  May not be available at certain times, frequencies, etc., or
  May operate with limited operational capabilities
Improving coexistence in UHR is important; absence of which leads to
  Data losses, increased delays, reduced reliability, etc.
Resources of interest from a coexistence perspective are:
  Time/Frequency: Link becomes (partially) unavailable at certain times
  Antennae: Subset of antennas (SS) becomes unavailable
  Other Resources : Other resources can dynamically change
We will be discussing these topics in the next slides

## Slide 3: 1) Time-based Sharing
Time (un-)availability: A link can be unavailable/available at certain times
  Baseline scheduled: TWT, APSD, U-APSD Coexistence
    Available for non-AP STAs in general, if AP PS enabled then possible at AP side as well
  Baseline unscheduled: PM-based AM/PS mode transitions, flexible TWT
    Available for non-AP STAs; requires an explicit exchange to transition between two states
Issues/items to address/optimize:
  STA may not be able to complete frame exchange before an unavailability event
    E.g., unavailability starts in 5 ms but PM=1 exchange not successful (failure, etc.)
  Transitions from available to unavailable may be very frequent and not follow strict schedules
Candidate Proposals:
  Add target unavailability/availability in specific Control frames
    Initial control frame (ICF), initial control resp. (ICR), and control resp. frame (CRF)
      Should be able to include padding to allow extra processing time of such information
  Require exchanges with STAs in coex. mode to start with these frames
ICF
ICR
Target unavailability
ICF
Unavailable
Available
Target Availability
ICR
Data Exchange
Data Exchanges

## Slide 4: 1) Time/Frequency-Sharing: Cont.
Certain Control frames contain target (un)availability times
  Target Availability Time: when link is expected to be available
  Target Unavailability Time: when link is expected to be unavailable
This, along with dynamic BW negotiation, covers time/frequency aspects of co-existence
  Some changes to spec needed when these parameters are used for coexistence (enable dynamic BW negotiation with ICF/ICR exchanges, etc.)

## Slide 5: 2) Antenna Sharing
Max RX NSS update is generally performed to:
  Provide in-device coexistence (sharing with other techs (BT, LTE, etc.)
  Reduce power consumption (reduce NSS in periods of low throughput)
  Enable dynamic resource management (shift from one link to another)
    E.g., eMLSR, eMLMR, link enable/disable, etc.
Currently, a STA can dynamically adapt the Max RX NSS by sending
  An OMN frame, or an MPDU containing an OM Control field
    Changes take effect after the TXOP during which the OM notification occurred
  Relies on the pre-emptive involvement of RXer in updating the NSS
    I.e., recipient notifies the transmitter of an NSS change in a timely manner

## Slide 6: 2) Antenna Sharing: Cont.
Events that trigger/need an NSS switch may not be predictable
  RX STA may find out too late that the RX NSS needs to be reduced
  RX STA may not have enough time to notify the peer STA of an update
    E.g., due to channel busy, EDCA disabled, peer STA’s unavailability, etc.
And these events may be very frequent
  Antennae sharing across multiple links, multiple techs, etc.
Which leads to:
  Underutilization of resources (advertise conservative values) or
  Data loss (failure to receive due to higher NSS)
Ending in reduced throughput, increased delay, and increased power consumption for the STA

## Slide 7: 2) Antenna Sharing: Cont.
Proposal: Add Max RX NSS in initial control exchange of a TXOP
  This along with dyn. BW negotiation ensures a timely & efficient use of BW/NSSs
Initiate all exchanges with initial control exchange
  By default, the recipient is assumed to only use one NSS to listen to the channel
  TXer may indicate in the ICF the Max RX NSS expected from the RXer
    RXer either confirms or indicates the Max RX NSSs for that TXOP
    Similar concept to dynamic BW negotiation
  RXer switches from 1 to X NSSs after the ICR, and remains until end of TXOP
    Note: CRF can also update the RX NSSs during the TXOP
  At the end of the TXOP the RXer switches back to 1 SS
Pros: Improved power consumption, coexistence, and increased throughput
CRF
MAX RX NSS = 4
ICR
Data
ICF
MAX RX NSS = 2
1 NSS
2 NSS
1 NSS

## Slide 8: 3) Other Resources Sharing
A receiving STA may have many other parameters that may be shared
  E.g., related to memory, processing, RF blocks, etc.
And may impact its capability of storing/processing incoming MPDUs
A list of parameters (not exhaustive) that reflect the above and may change:
  Minimum MPDU start spacing, MAC frame processing (BA on/off, fragmentation on/off), max PPDU duration, number of MPDUs that can be aggregated within an A-MPDU, max number of TIDs in a multi-TID A-MPDU, total # of payload bytes in the PPDU, max (e.g., MCS, NSS, BW), LDPC, etc.
Real-time modifications of these parameters, while beneficial from RXer’ perspective, complicate TXer scheduling (APs in particular) and reactiveness
To avoid these complications, a careful evaluation of each of these parameters is needed, and if beneficial to allow their update, then the proposal would be to use existing MGMT-level mechanisms (e.g., ML reconfiguration, etc.).
  Preliminary evaluation points out some parameters of interest that can be updated post-association (Max PPDU duration, max MCS, LDPC, etc.)

## Slide 9: Conclusion
Coexistence is an important topic in need of focused discussions
We provided a brief overview of existing coexistence protocols
  Highlighted certain limitations of these existing protocols
Introduced functionalities that could avoid these limitations for UHR
And highlighted that additional coexistence protocol design needs to
  Account not only for the benefits but also for the added complexities

## Slide 10: References
TDB