## Slide 1: Further thoughts on seamless roaming
Date: 2023-11-10
Authors:

## Slide 2: Introduction
In UHR SG, seamless roaming was discussed to add Ultra High Reliability capability to a WLAN for a given scenario, especially for transitions between BSSs[1].
In the previous contribution[2], we share several considerations about architecture for seamless roaming.
In this contribution, we recap the architecture for seamless roaming and show some basic protocols for seamless roaming.

## Slide 3: Recap: Architecture for seamless roaming
In the previous contribution, we showed some considerations on architecture for seamless roaming.
  Upper MAC of roaming AP MLD will manage LMAC of each AP MLDs.
  Upper MAC(UMAC) of roaming AP MLD may be split into upper UMAC and lower UMAC.
  Upper UMAC of roaming AP MLD will be collocated or not collocated with AP MLD.
  Non-AP MLD may communicate with more than one AP MLD while roaming (transient Multiple Serving AP MLD mode) or not roaming(non-transient Multiple Serving AP MLD mode).
Then, we proposed to start discussion with a simple architecture.
  Start with Upper UMAC collocated with AP MLD.
  Start with single serving AP MLD mode and transient multiple serving AP MLD mode but should extend to non-transient multiple serving AP MLD mode.

## Slide 4: Roaming protocol for baseline architecture
We consider upper UMAC of roaming AP MLD collocated with AP MLD as a baseline architecture.
  Legacy UMAC also exists in each AP box to support legacy STAs.
  In this contribution, we call upper UMAC of roaming AP MLD as roaming UUMAC(r-UUMAC) and lower UMAC of roaming AP MLD as roaming LUMAC(r-LUMAC).
We will show protocols for seamless roaming with and without data forwarding between AP MLDs.
  Data forwarding between AP MLDs helps to keep data continuity. Without data forwarding, data might be lost in some cases.
  However, whether data forwarding is possible or not depends on, for example, the capabilities of the interface between AP MLDs.
  Therefore, we will see how roaming protocol will be depending on data forwarding.
Collocated
UMAC
LMAC
LMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
UMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
UMAC

## Slide 5: Roaming protocol with data forwarding (1/3)
Phase 1 (Preliminary phase)
  Roaming upper UMAC collocated with serving AP MLD manages association, scoreboarding, encryption.
  Roaming upper UMAC or non-AP MLD decides to initiate roaming protocol to roam link2 to target AP MLD.
  Serving AP MLD initiates context transfer to target AP MLD.
    Context may include PN, SN, BA session, and so on.
This phase is same in the protocol without data forwarding.
UMAC
LMAC
LMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
Serving AP MLD
Target AP MLD
Non-AP MLD
link1
link2
LMAC
LMAC
r-UUMAC
r-LUMAC
context

## Slide 6: Roaming protocol with data forwarding (2/3)
Phase 2 Transition
  Enable non-AP MLD to receive data from target AP MLD on link2.
    This may be done by extending ML reconfiguration(adding affiliated APs).
  Serving AP MLD forwards encrypted data to target AP MLD.
  Serving AP MLD and/or target AP MLD delivers data to the non-AP MLD.
UMAC
LMAC
LMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
Serving AP MLD
Target AP MLD
Non-AP MLD
link1
link2
UMAC
LMAC
LMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
Serving AP MLD
Target AP MLD
Non-AP MLD
Data path

## Slide 7: Roaming protocol with data forwarding (3/3)
Phase 3 Post-Transition
  After link2 roams to target AP MLD, link1 may roam to target AP MLD.
    Whether link1 will roam or not depends on serving AP MLD mode and so on.
  After all links complete roaming to target AP MLD, roaming upper UMAC may relocate from serving AP MLD to target AP MLD.
    The relocation depends, for example, on the capabilities of the backhaul or the number of associated non-AP MLDs.
UMAC
LMAC
LMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
Serving AP MLD
Target AP MLD
Non-AP MLD
link1
link2
UMAC
LMAC
LMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
Serving AP MLD
Target AP MLD
Non-AP MLD
link1
link2

## Slide 8: Roaming protocol without data forwarding (1/2)
Phase 2 Transition
  Without data forwarding, new packets from upper layer should be delivered to target AP MLD. Therefore, upper UMAC relocates to target AP MLD and data path from upper layer should already be moved to target AP MLD at this phase.
  Serving AP MLD should complete delivering buffered packets and target AP MLD delivers new packets from upper layer.
    If the link with serving AP MLD is removed before the buffered packet delivery is complete, data loss can occur.
UMAC
LMAC
LMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
Serving AP MLD
Target AP MLD
Non-AP MLD
link1
link2
UMAC
LMAC
LMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
Serving AP MLD
Target AP MLD
Non-AP MLD
new packets
buffered packets

## Slide 9: Roaming protocol without data forwarding (2/2)
Phase 3 Post-Transition
  After link2 roams to target AP MLD, link1 roams to target AP MLD.
  If not, link1 can not serve new packets from upper layer.
UMAC
LMAC
LMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
Serving AP MLD
Target AP MLD
Non-AP MLD
link1
link2
UMAC
LMAC
LMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
LMAC
LMAC
r-UUMAC
r-LUMAC
Serving AP MLD
Target AP MLD
Non-AP MLD
link1
link2

## Slide 10: Discussion point
In the coming standardization, we need to discuss about
  Protocols for context transfer, data forwarding
    It is preferred that the protocol does not depend on capability/type of interfaces.
    However, the protocol may vary depending on the capabilities of the interface, as shown in previous slides.
  Requirement/Use cases
    Number of APs to cover with upper UMAC, latency for roaming

## Slide 11: Summary
In this contribution, we revisit architecture for seamless roaming.
  Roaming upper UMAC collocated with AP MLD is good for baseline architecture because it is simple and easy to extend another architecture.
On this architecture, we show example protocols for seamless roaming with and without data forwarding and show some discussion points for TGbn.

## Slide 12: References
[1] 11-23-0480-03-0uhr-uhr-proposed-par.pdf
[2] 11-23-1131-00-0uhr-thoughts-on-seamless-roaming.pptx