## Slide 1: Discussion on UHR enhanced channel access
Date: 2023-11-4
Authors:
Name | Affiliations | Address | Phone | Email
Yanchun Li | Huawei | Huawei Industrial Base, Bantian, Longgang District, Shenzhen 518129 China |  | liyanchun@huawei.com
Dekun Liu |  |  |  | 
Yanbin Sun |  |  |  | 
Xuming Wu |  |  |  | 
Xiang Wang |  |  |  | 
Notes: November 2012

## Slide 2: Introduction
UHR PAR has defined the requirements on improved RvR and reduced latency. A number of schemes have been proposed for these, including:
Multi-AP coordination: Co-SR, Co-BF, JT, etc[1, 2 , 3].
Channel access: Non-primary channel access, preemption, etc [4][5].
This contribution discusses the non-AP STAs’ impacts on these schemes. Non-AP STA’s non-cooperative channel access can reduce the time portion of Multi-AP coordination transmission and degrades network efficiency. Besides, non-AP STA initiated non-primary channel access will increase channel collision probability.
November 2023

## Slide 3: Multi-AP coodination requirements
Reliable transmission requires AP coordination and STA’s compliance in dense networks.
Channel Access and Scheduling process:
(STA handovers TXOP holder to AP.)
AP shares TXOP with other APs in coordination group.
APs in coordination group transmit to STA according to QoS requirement.
APs refresh schedule plan according to low latency STAs’ immediate BAs.
November 2023

## Slide 4: Impairment due to non-cooperative STAs
11ax STAs can set UL MU Disable subfield in OM Control subfield to 1 to continue legacy EDCA backoff.
  It will reduce the effectiveness of APs’ coordination and degrades performance.
STAs can reject or defer AP’s BSS Transition Management (BTM) request
  It will prevent AP from balancing loads among multiple APs.
Lack of seamless band steering: Non-AP STA’s behavior in channel switch announcement is not specified
  When AP has agile frequency selection, STA could not follow. It leads to latency and packet loss.
November 2023

## Slide 5: Conclusions
This presentation discussed the requirement on UHR MAC to meet the throughput and latency goal defined in PAR.
If multi-AP coordination scheme is defined in UHR, non-AP STAs need to compline with APs instruction on scheduling, BSS transition, and channel switching.
November 2023

## Slide 6: Straw Poll
Do you agree that UHR needs to provide AP more channel access opportunities and management for multi-AP coordinated transmissions to meet reliability goal?
  Yes
  No
  Abstain
November 2023

## Slide 7: Reference
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-1176-01-0uhr-multi-ap-simulations-framework-and-joint-transmission-results.pptx IEEE 802.11ax
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-0243-00-0uhr-joint-transmission-for-uhr-additional-results.pptx
[3] https://mentor.ieee.org/802.11/dcn/22/11-22-1821-01-0uhr-system-level-simulation-of-co-bf-and-joint-tx.pptx
[4] https://mentor.ieee.org/802.11/dcn/23/11-23-0797-01-0uhr-non-primary-channel-access.pptx
[5] https://mentor.ieee.org/802.11/dcn/23/11-23-1288-00-0uhr-non-primary-channel-utilization-follow-up.pptx
November 2023