## Slide 1: Discussion on UHR enhanced channel access
Date: 2023-11-4
Authors:
Name | Affiliations | Address | Phone | Email
Yanchun Li | Huawei | Huawei Industrial Base, Bantian, Longgang District, Shenzhen 518129 China |  | liyanchun@huawei.com
Dekun Liu |  |  |  | 
Yanbin Sun |  |  |  | 
Xuming Wu |  |  |  | 
Xiang Wang |  |  |  | 
Notes: November 2012

## Slide 2: Introduction
UHR PAR has defined the requirements on improved RvR and reduced latency. A number of schemes have been proposed for these, including:
Multi-AP coordination: Co-SR, Co-BF, JT, etc[1, 2 , 3].
Channel access: Non-primary channel access, preemption, etc [4][5].
This contribution discusses the non-AP STAs’ impacts on these schemes.
November 2023

## Slide 3: Non-AP STAs’ impacts on Ultra-high-reliable sysetm operations (1)
Non-AP STA’s non-cooperative channel access can reduce the time portion of Multi-AP coordination transmission and degrades network efficiency.
STA1
AP2
Fig.1 Exposed node problem in non-AP STA (STA1)’s initiated uplink transmission
Fig.2 UHR multi-AP coordinated transmissions allow low latency and robust concurrent transmissions. (e.g. Co-SR, concurrent TWTs, Co-BF, JT/JR)
STA2
AP1
STA1
AP2
STA2
AP1
Strong RSSI prevents STA2 from transmission
SE ↗ +60% = 1.6x
Spectrum Efficiency 100%
75% Time
25% Time
Overall Spectrum Efficiency 75%*1+25%*1.6=1.15 ↗ +15%
Most of gain vanishes.

## Slide 4: Non-AP STAs’ impacts on Ultra-high-reliable sysetm operations (2)
Secondary Ch
Primary Ch
Besides, non-AP STA initiated non-primary channel access (NPCA) will increase channel collision probability.
CCA
Non-AP STA’s Virtual CCA (NAV setting) is only for primary channel due to simplicity
RTS
① OBSS 1 NAV announcement
CTS
② OBSS 2 Occupation on primary channel
③ STA1’s initiated NPCA causes collision on OBSS1
OBSS1’s behavior
OBSS2’s behavior
STA1’s behavior
Legend
Fig.3 Non-AP STA initiated NPCA’s negative impact on system reliability

## Slide 5: Multi-AP coodination requirements
Reliable transmission requires AP coordination and STA’s compliance in dense networks.
Channel Access and Scheduling process:
(STA handovers TXOP holder to AP.)
AP shares TXOP with other APs in coordination group.
APs in coordination group organize STA’s DL/UL according to QoS requirement.
  STA provides accurate channel/interference measurement, and follow AP’s schedule, e.g. Trigger based UL, BSS/link transition,
APs refresh schedule plan according to low latency STAs’ immediate BAs.
November 2023

## Slide 6: Impairment due to non-cooperative STAs
11ax STAs set UL MU Disable subfield in OM Control subfield to 1 to continue legacy EDCA backoff.
  It will reduce the effectiveness of APs’ coordination (as shown in Fig.1 and 2).
STAs reject or defer AP’s BSS Transition Management (BTM) request
  It will prevent AP from balancing loads among multiple APs.
Lack of seamless band steering: Non-AP STA’s behavior in channel switch announcement is not specified
  When AP has agile frequency selection, STA could not follow. It leads to latency and packet loss.
November 2023

## Slide 7: Conclusions
This presentation discussed the requirement on UHR MAC to meet the throughput and latency goal defined in PAR.
If multi-AP coordination scheme is defined in UHR, non-AP STAs need to compline with APs instruction on scheduling, BSS transition, and channel switching.
November 2023

## Slide 8: Straw Poll
Do you agree that UHR needs to provide AP more channel access opportunities and management for multi-AP coordinated transmissions to meet reliability goal?
  Yes
  No
  Abstain
November 2023

## Slide 9: Reference
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-1176-01-0uhr-multi-ap-simulations-framework-and-joint-transmission-results.pptx IEEE 802.11ax
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-0243-00-0uhr-joint-transmission-for-uhr-additional-results.pptx
[3] https://mentor.ieee.org/802.11/dcn/22/11-22-1821-01-0uhr-system-level-simulation-of-co-bf-and-joint-tx.pptx
[4] https://mentor.ieee.org/802.11/dcn/23/11-23-0797-01-0uhr-non-primary-channel-access.pptx
[5] https://mentor.ieee.org/802.11/dcn/23/11-23-1288-00-0uhr-non-primary-channel-utilization-follow-up.pptx
November 2023