## Slide 1: EPOCH Group Management
Date: 2023-11-13
Authors:

## Slide 2: Revision
Rev 0: initial revision

## Slide 3: Overview
The obfuscation procedure consists in performing a simultaneous change of the transmitted PE parameters (which are transmitted in clear in the frames) by the stations, to uncorrelated new values (with the previous ones) without any loss of connection.
To ensure the transmission continuity, all STAs must end the data transmissions already initiated with the old PE parameters, before starting new transmissions with the new PE parameters.
The new PE parameters and the old PE parameters must remain valid at least for a short period of time, called a transition period.

## Slide 4: Background: How to determine transition period ?
The contribution IEEE802.11-23/873r2 (Qualcomm) proposes to initiate the obfuscation of PE parameters at regular epoch period. It means that all STAs associated to the AP run the obfuscation procedure at the same time.
  Due to synchronization issue and clock drift between a STA and an AP and to finalize the already started transmissions, the new PE parameters and the old PE parameters must remain valid during the transition period. One proposal is that the transition period lasts 2 EPOCH periods.
The contribution IEEE802.11-23/1148r0 (Canon) proposes to introduce “margins” around the EPOCH(n) event and to define a short transition period between the old PE parameters and the new PE parameters. It optimizes the length of the transition period.
time
EPOCH (n-1)
EPOCH (n)
EPOCH (n+1)
PE Params(n-1) valid
PE Params(n) valid
PE Params(n+1) valid
time
EPOCH (n-1)
EPOCH (n)
EPOCH (n+1)
PE Params(n-1) valid
PE Params(n) valid
PE Params(n+1) valid
RCM ready (n)
RCM done (n)

## Slide 5: Issue: AID12 values management
During the transition period, each AP/STA must manage multiple sets of PE parameters. It requires CPU power and memory.
The usage of the new PE parameters and the old PE parameters at the same time creates issues for the management of the AID12 parameter.
The number of available AID12 values is limited to 2007 for associated STAs.
In a dense 11bi network, the number of available AID12 values could be not enough. There is a need to manage and modify the obfuscation procedure for the AID12 parameter.
Moreover, from implementation point of view, an AP can allocate range of AID12 values to STAs depending on their functionalities. So this issue can occur even if the total number of available AID12s values is not reached.
Example: a BSS comprising 1 AP and 1200 STAs – Nbr max AID12: 2007
time
EPOCH (n-1)
EPOCH (n)
EPOCH (n+1)
PE Params(n-1) valid
PE Params(n) valid
PE Params(n+1) valid
RCM ready (n)
RCM done (n)
1 group
of 1200 STAs
Obfuscation procedure not applicable

## Slide 6: Proposal
The obfuscation procedure for the AID12 parameter is adapted by creating groups of STAs and to schedule obfuscation procedure only for a set of STAs instead of changing the AID12 of all STAs at the same time.
The determination of each group of STAs can be different from one AP to another depending on an obfuscation profile of a STA, some capabilities of STAs or an AP policy related to the privacy.
EPOCH group management
  An AP can manage groups of STAs separately. It means different EPOCH periodicity, different sets of PE parameters …
  Group management can be applied at any time or only when the number of available AID12 is not enough for obfuscation procedure.
Example: a BSS comprising 1 AP and 1200 STAs – Nbr max AID12: 2007 – 2 EPOCH Groups: G1 and G2
time
EPOCH_G1 (n-1)
EPOCH_G1 (n)
EPOCH_G1 (n+1)
PE Params(n-1) valid – Group 1
PE Params(n) valid – Group 1
PE Params(n+1) valid – Group 1
2 groups
of 600 STAs
PE Params(n-1) valid – Group 2
PE Params(n) valid – Group 2
PE Params(n+1) valid – Group 2
EPOCH_G2 (n-1)
EPOCH_G2 (n)
EPOCH_G2 (n+1)

## Slide 7: Benefits
Allow to manage privacy in dense environment
Proposal adapted to the Vendor-specific implementation for the management of the AID12 values

## Slide 8: Summary
EPOCH group management allows to solve the issues related to a limited number of available values of a PE parameter.

## Slide 9
Straw Poll #1
Do you support that an AP should manage CPE parameters in multiple groups of non-AP STAs ?
Yes
No
Abstain

## Slide 10: References
[1] IEEE 802.11-21/0873r2 (Qualcomm) : Client Frame Tracking Countermeasures
[2] IEEE802.11-23/1148r0 (Canon) : RCM Follow up