## Slide 1: Improve roaming between MLDs
Date: 2023-11-09
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Laurent Cariou |  |  |  | 
Daniel F Bravo |  |  |  | 
Ido Ouzieli |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
We discuss how to improve roaming in [1]
  We highlight that it is unrealistic for the design to depend on the assumption of a central buffer to hold data of different AP MLDs for all clients associated with different AP MLDs
  We also highlight that it is unrealistic to assume the availability of parameter sync for different AP MLDs (ex. SN assignment)
  The considerations above highlight why existing MLD design can not be naively reused
We provide follow up in this presentation to improve roaming with realistic consideration

## Slide 3: Goal of Roaming
As described in [1], the ultimate goal is to have data continuity between two AP MLDs
The first step to achieve this goal is to make sure that we do not need to redo authentication and key derivation and so on, which will break data continuity
There are various steps defined in the current spec to enable data path, and a succinct way to capture this is “state 4” (authenticated and RSNA established)
Hence, in short, the goal of improved roaming is for the non-AP MLD to remain in state 4 (see 11.3) after successful roaming to the other AP MLD
Current AP MLD
Target AP MLD
Current AP MLD
Target AP MLD
Non-AP MLD
Non-AP MLD
Successful Roaming
State 4
State 4

## Slide 4: Non Goal of Roaming
As described in [1], parameter sync between AP MLDs is extremely hard
  Ex. How can two non collocated AP MLDs individually know instantaneously what is the next SN to assign?
  Design involves delay will make the performance even worse
It then makes sense to focus the “data path” that are not in the process of roaming to be still with one AP MLD at a time, so there is no unrealistic assumption of very fast parameter sync to maintain performance.
  “Class 3 frames” are the succinct way to capture the notion of “data path” in the spec
Proposal: If a non-AP MLD is not in the process of roaming initiated by the non-AP MLD and the non-AP MLD is in state 4, the non-AP MLD is allowed to exchange class 3 frames with only one AP MLD
Current AP MLD
Target AP MLD
Non-AP MLD
Some location
Delay to retrieve parameter
Delay to retrieve parameter

## Slide 5: Main Techniques to Improve Roaming
Without parameter sync, the only way to maintain data continuity is to enable AP MLDs to do context transfer
  The simplest examples are keys like PMK, PTK, and parameters like next SN/PN to assigned
Proposal: when a non-AP MLD is in the process of roaming from one AP MLD to another AP MLD, the context related to the non-AP MLD is transferred from one AP MLD to the other AP MLD such that it preserves the data exchange context for the non-AP MLD
Current AP MLD
Target AP MLD
Current AP MLD
Target AP MLD
Non-AP MLD
Non-AP MLD
Successful Roaming
State 4
State 4
Initiate roaming
Current AP MLD
Target AP MLD
Non-AP MLD
Context transfer

## Slide 6: How AP MLDs exchange contexts?
Before we answer the question, we note that exchange context has been defined in current spec.
In fast transition protocol, it is defined to allow the transfer of contexts like PMK-R1
The R0KH and the R1KH are assumed to have a secure channel between them that can be used to exchange cryptographic keys without exposure to any intermediate parties. The cryptographic strength of the secure channel between the R0KH and R1KH is assumed to be greater than or equal to the cryptographic strength of the channels for which the keys are used. This standard assumes that the key transfer includes the PMK-R1, the PMK-R1 PMKSA, the PMK-R1 context, and the associated key authorizations. The protocol for distribution of keying material from the R0KH to the R1KH is outside the scope of this standard.
FT works great today! Hence, we believe that following similar principle, as a minimum, we only need to define what are the contexts to be transferred like above and leaves the protocol for distribution outside the scope of this standard
Essentially, we define more contexts to be transferred, so the transition can then be “even faster”

## Slide 7: How the Roaming is initiated?
Where to roam is ultimately determined by user using the device, i.e., the non-AP MLD
It does not make sense to duplicate all the contexts to all AP MLDs all the time
  Waste of bandwidth
  Some contexts (ex next SN/PN to assign) need constantly update
A straightforward approach is to define context transfer request/response for non-AP MLD to initiate context transfer from current AP MLD to target AP MLD and for non-AP MLD to be indicated the completion of context transfer and start follow up operation

## Slide 8: Conclusion
We discuss how to improve roaming for 11bn with realistic implementation consideration
  Have a mechanism for the non-AP MLD to remain in state 4 when roam from current AP MLD to the target AP MLD
  Still focus on data path with one AP MLD at a time outside the roaming procedure
  Enable context transfer during roaming between AP MLDs
  Define request/response frame to initiate roaming and context transfer from current AP MLD to target AP MLD and indicate completion of context transfer

## Slide 9: SP #1
Do you support to define a mechanism in 11bn that enables a non-AP MLD to roam from one AP MLD to another AP MLD and the non-AP MLD remains in state 4 (see 11.3) after successful roaming to the other AP MLD?

## Slide 10: SP #2
Do you agree that in 11bn when a non-AP MLD is not in the process of roaming initiated by the non-AP MLD and the non-AP MLD is in state 4, the non-AP MLD is allowed to exchange class 3 frames with only one AP MLD?

## Slide 11: SP #3
Do you support to define in 11bn that when a non-AP MLD is in the process of roaming from one AP MLD to another AP MLD, the context related to the non-AP MLD is transferred from one AP MLD to the other AP MLD such that it preserves the data exchange context for the non-AP MLD?
  Details of the context that can be transferred are TBD
  How to transfer the context is TBD.

## Slide 12: SP #4
Do you support the following?
  Define a request frame for a non-AP MLD in state 4 to initiate the roaming procedure
  The roaming procedure enables context transfer between the current AP MLD and the target AP MLD
  Define a response frame to the non-AP MLD to indicate the completion of the context transfer and indicate readiness for the non-AP MLD to send class 3 frames to the target AP MLD
  NOTE - What contexts to be transferred is TBD.

## Slide 13: Reference
[1] 11-23-0322 UHR Improve Roaming between MLDs