## Slide 1: Client power save
Date: 2023-11-10
Authors:

## Slide 2: Non-AP STA and non-AP MLD power save
Always important to improve non-AP STA power save
In 802.11 we have 2 power states: Doze and Awake
But Awake state is evolving with eMLSR into 2 sub-states:
  Awake in listen mode (using SMPS or eMLSR)
  Awake in receive or transmit mode (full power)
Overall:
  We see benefits to reduce further power consumption during listen mode
  We see less gains (less priority) for receive full power mode, but open to enhancements
  we see benefits to improve flexibility in transitions between Doze and Awake with MLO.

## Slide 3: eMLSR Listen mode power consumption reduction
STAs can stay for a long time in listen mode and should consume as little power as possible
With eMLSR, STAs can already only enable reception
  of some low MCSs
  of a single NSS with a single antenna
Current gap is to be able to only enable reception on 20MHz instead of the STA’s operating BW, which would provide significant power gains
  This is theoretically possible with eMLSR, but there’s currently no time after the ICF to reconfigure the radio to a larger bandwidth and to check CCA on the TxOP BW before responding with CTS
ICF (e.g. MU-RTS)
TxOP owner
AP
TxOP responder
STA
SIFS
ICF response (e.g. CTS)
20MHz operation: listen mode
80MHz operation: power mode
Data
Transition from 20 to 80MHz
Check CCA

## Slide 4: Proposal
We need to give more time for the STA to be able to change BW so that it can check CCA during SIFS between ICF and ICF response
One could thing we can use padding, but actually the padding is included before the FCS in non-HT dup (which has to be used in that case), which forces the STA to wait until the end of the ICF PPDU before being able to switch
We propose to add a new Intermediate FCS field (called here FCS2), before the padding so that the STA can use the padding time to change BW and use SIFS to check CCA on TxOP BW.
We can exploit the trigger structure as follows:
Note that this is the same issue and solution as for dynamic subchannel operation
Frame control
Duration
RA
TA
Common info
User info
STA1
User info
STA2
FCS2 User Info
FCS2 User Info
Padding User Info
…
Padding User Info
Transition from 20 to 80MHz
20MHz operation: listen mode
80MHz operation: power mode
FCS
FCS calculated on whole data portion up to FCS2 User Info field

## Slide 5: More details on inclusion of FCS
Define a special User Info field to include the intermediate FCS
  Just one intermediate FCS for all STAs that can exploit it
  Special User Info field using an AID12 value that is unique and defined in spec
Otherwise, keep same frame structure
  Legacy STA will ignore this field and look for the FCS field at the end
  UHR STAs will be able to terminate processing of the ICF at the end of the intermediate FCS
If we do trigger frame protection:
  Protection signaling needs to be included before this intermediate FCS

## Slide 6: Allowing more flexibility in using eMLSR Power save on each link
As discussed in previous slides, we see potential for some power save enhancements with eMLSR during the listen mode operation
These benefits come from the TxOP sequence defined for eMLSR, which mandates inclusion of ICF/ICF response at the beginning of the TxOP, and includes padding for transitions between listen mode and full-power mode
This TxOP sequence defined and used for eMLSR can be used as a power save mechanism on each link
  Single link eMLSR (where the eMLSR link set is made of a single link) is actually such a power save mode that applies at the link level.
  Same as SMPS (which is per link), but with additional power saving benefits and more widespread support

## Slide 7: Per link eMLSR-like dynamic power save
We propose to allow to use such TxOP sequence (ICF with padding/ICF response) on each link, even when eMLSR is not used on this link
  Ex: dual radio non-AP MLD:
    Can do eMLSR-like power save on each link (as an SMPS replacement to be able to transition from listen mode to full power mode on each link independently from the other links)
We can define this by:
  Adapting SMPS so that it includes the TxOP sequence used for eMLSR (ICF with padding/ICF response)
  Allowing a non-AP MLD to negotiate multiple eMLSR agreements with the AP MLD and especially have multiple single link eMLSR agreements (fully reusing in this case the single link eMLSR concept as a replacement of SMPS)
  Define negotiation for a new per-link power save mechanism that uses the exact same sequence as eMLSR (ICF with padding/ICF response)
    Extract eMLSR TxOP sequence rules into a generic procedure that can evolve and be used by eMLSR across links and by this per-link power save mode at the link level.
We could use that also for a mobile AP MLD, but need to analyse this to see if the gains envisioned are sufficient

## Slide 8: Power save enhancements with MLO: Cross-link PS
First priority for us regarding power save exploiting MLO dimension is to finally enable cross link power save:
  Allowing to indicate power save mode changes and/or power state changes from one link for the other
  Really lacking in current MLO framework
    If a non-AP MLD wants to go in doze state, it has to access medium on both links to change PM mode.
  Beneficial for all types of non-AP MLDs (eMLSR, multi-radio, …)

## Slide 9: SP1
Do you agree to define a new special user info field that can be present in the eMLSR initial control frames (MU-RTS and BSRP Trigger frames) to include an additional and intermediate FCS field before the Padding field and the FCS field?

## Slide 10: SP2
Do you support to define a power save mode for a non-AP STA where the STA may transition from a lower capability mode to a higher capability mode upon reception of an initial control frame?

## Slide 11: SP3
Do you agree to define cross link power save signaling
  allowing a non-AP MLD to indicate to its associated AP MLD, in a frame sent on one enabled link, the power save mode changes and/or the power state changes for one or more of its affiliated non-AP STAs operating on other enabled links