## Slide 1: Location Dependent Performance of C-SR
Date: 2023-11-10
Authors:

## Slide 2: Introduction
Coordinated Spatial Reuse (C-SR) is one of the Multi-AP coordination schemes for TGbn[1][2]
  C-SR allows multiple stations to transmit simultaneously by suppressing inter-BSS interference through Tx power control
  C-SR can improve system throughput with lower complexity
In this contribution, we show C-SR simulation results when changing the positional relationship between APs and STAs

## Slide 3: Assumption for the C-SR Simulation
  Assume that Sharing AP can control both APs' transmission in TXOP
  Sharing AP determines whether only a single AP transmits or both APs transmit simultaneously with C-SR depending on which method achieves higher system throughput
In C-SR, Sharing AP determines the combination of Tx power for each AP that maximizes system throughput
    The system throughput is calculated by selecting MCSs that satisfy PER≦10% for the combination of Tx power
  In single AP transmission, only Sharing AP transmits to the associated STA with maximum Tx power
Sharing AP
Shared AP
Pathloss
(Sharing AP-STA1)
Pathloss
(Shared AP-STA2)
Pathloss
(Shared AP-STA1)
Pathloss
(Sharing AP-STA2)
STA1
STA2
In this contribution, C-SR allows two APs to transmit DL packets at the same time
The AP which obtains TXOP, called Sharing AP, collects pathloss information between all AP-STA

## Slide 4: Simulation Setup
Compare the following methods
  11ax OBSS_PD based SR
    Sharing AP transmits data with max Tx power
    Shared AP transmits data with Tx power that meets OBSS_PDmax = -62dBm/20MHz
      For Shared AP, MCS is determined to satisfy PER≦10%
  C-SR
    Sharing AP determines the combination of Tx power and MCS for each AP
    If a single AP transmission maximizes system throughput, only Sharing AP transmits with maximum Tx power
    MCS is determined based on SINR to satisfy PER≦10%
Definition of Throughput
  Throughput is calculated as follows
    MACTxByte: Successfully transmitted MSDU data byte size
    TxTime: PHY transmission time for data
  System throughput is the sum of throughput of each BSS

## Slide 5: Simulation Setup
Simulation Environment
  Layout
    One AP and one STA are placed in each 10[m] x 10[m] room
    The distance between APs is 12[m]
    STAs are deployed a granularity of 1[m]
  Parameter
Frequency, Bandwidth | 5[GHz], 80[MHz]
Tx Power | 0 ~ 21[dBm]
Tx/Rx Antenna | (AP, STA) = (4, 1)
Stream | 1 per STA
Beamforming | YES
MCS index | 0 ~ 11
Fading Model | Model-D
Noise Figure | 7 [dB]
Path loss model | Eq.(1)
Eq(1): Pathloss =
  𝑑 = max(2D distance[m], 1)
  = 5[GHz]
  𝑊 = number of walls traversed
10[m]
10[m]
10[m]
1[m]
AP2
AP1
1[m]
STA1
STA2
x
y
12[m]

## Slide 6: Simulation Result 1
Comparison of 11ax OBSS_PD based SR and C-SR
At the CDF = 0.9, C-SR achieves 1.4 times higher throughput than 11ax OBSS_PD based SR

## Slide 7: Simulation Result 2
Each heatmap shows the system throughput per STA2 location, with specific STA1 location
C-SR throughput is improved:
  When each STA is close to its associated AP
  When STA is far from OBSS AP
STA1 (x, y) = (4, 5)
AP1
STA1
AP2
STA1 (x, y) = (1, 5)
STA1 (x, y) = (7, 5)
STA1 (x, y) = (10,5)
When STA2 was in yellowish-green squares, single AP transmission was chosen.
Otherwise, C-SR transmission was chosen.
Slide 7

## Slide 8: Summary
This contribution showed heatmaps of the throughput property when APs and STAs are in specific locations
The simulation results showed C-SR throughput is improved when each STA is close to its associated AP or when STA is far from OBSS AP
As a future work, it will be necessary to consider the overhead for Sharing AP to collect pathloss information between all APs and STAs, and the fairness of throughout for each AP in C-SR

## Slide 9: References
[1] Kosuke Aio (Sony Corporation), “Recap on Coordinated Spatial Reuse Operation,” 22/1822r0, November 2022.
[2] Sungjin Park (LG Electronics), “Coordinated Spatial Reuse Procedure,” 20/0410r4, March 2020.
[3] Kosuke Aio (Sony Corporation), “Overhead Analysis of Coordinated Spatial Reuse,” 23/0616r0 2023.
[4] Kanke Wu (Qualcomm), “Performance of Coordinated Spatial Reuse,” 23/1037r0 2023.