## Slide 1: HT Control field expansion
Date: 2023-11-10
Authors:

## Slide 2: Background
HT Control field and A-Control subfield are useful.
  Only 5 A-Control IDs are reserved for future usage.
  Expansion with the reserved A-Control ID ONES leads to overhead and complexity.

## Slide 3: Another way for A-Control field expansion
Retry subfield is reserved in frames that are not non-A-MPDUs and under a block ack agreement.
  Most of exchanged frames in UHR are frames that are not non-A-MPDUs and under a block ack agreement.
  It is possible for other frames in UHR to check whether they are retransmissions or not, regardless Retry subfield.
Retry subfield can be leveraged for A-Control field expansion.
  If Retry subfield is equal to 0, it is HT Control field.
  If Retry subfield is equal to 1, it is A-Control Expansion field.
PV | Type | … | Retry=0 | … | +HTC=1
Duration | … | HT Control
PV | Type | … | Retry=1 | … | +HTC=1
Duration | … | A-Control Expansion

## Slide 4: Conclusion
A-Control Expansion field indicated by Retry subfield is proposed.
  Easier and no overhead.